## Slide 1: Lecture 03 Embedded Software
CE346 – Microprocessor System Design
Branden Ghena – Fall 2022
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Office hours still by request for this week
  Schedule starts next week. I’ll post it soon to Campuswire
  Seriously, send me a message if you want to chat, I’m happy to
Labs will start this Friday!!!
  You MUST come to your scheduled lab session

## Slide 3: Today’s Goals
Discuss challenges of embedded software
Describe compilation and linking of embedded code
  Actually applies to all code, but you probably never learned much about linking before
Explore the microcontroller boot process

## Slide 4: Outline
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 5: Assumptions of embedded programs
Expect limitations
  Very little memory
  Very little computational power
  Very little energy
Don’t expect a lot of support
  Likely no operating system
  Might not even have error reporting capabilities
Moral: think differently about your programs

## Slide 6: Ramifications of limited memory
Stack and Data sections are limited
  Be careful about too much recursion
  Be careful about large local variables
  Large data structures defined globally are preferred
    Fail at compile time
Heap section is likely non-existent
  Why?

## Slide 7: Ramifications of limited memory
Stack and Data sections are limited
  Be careful about too much recursion
  Be careful about large local variables
  Large data structures defined globally are preferred
    Fail at compile time
Heap section is likely non-existent
  Why?
    Malloc could run out of memory at runtime

## Slide 8: Avoiding dynamic memory
Malloc is scary in an embedded context
What if there’s no more memory available?
  Traditional computer
    Swap memory to disk
    Worst case: wait for a process to end (or kill one)
  Embedded computer
    There’s likely only a single application
    And it’s the one asking for more memory
    So it’s not giving anything back anytime soon
This is unlikely to happen at boot
  Instead it’ll happen hours or days into running as memory is slowly exhausted…

## Slide 9: Limitations on processing power
Typically not all that important
  Code still runs pretty fast
    10 MHz -> 100 ns per cycle (i.e. ~100 ns per instruction)
  Controlling hardware usually doesn’t have a lot of code complexity
    Quickly gets to the “waiting on hardware” part (apps are I/O bound)
Problems
  Machine learning
    Learning on the device is neigh impossible
    Memory limitations make it hard to fit weights anyways
  Cryptography
    Public key encryption takes seconds to minutes

## Slide 10: Common programming languages for embedded
C
  For all the reasons that you assume
  Easy to map variables to memory usage and code to instructions
Assembly
  Not entirely uncommon, but rarer than you might guess
  C code optimized by a modern compiler is likely faster
  Notable uses:
    Cryptography to create deterministic algorithms
    Operating Systems to handle process swaps
C++
  Similar to C but with better library support
  Libraries take up a lot of code space though ~100 KB

## Slide 11: Rarer programming languages for embedded
Rust
  Modern language with safety and reliability guarantees
  Relatively new to the embedded space
    And a high learning curve
Python, Javascript, etc.
  Mostly toy languages
  Fine for simple things but incapable of complex operations
    Especially low-level things like managing memory

## Slide 12: What’s missing from programming languages?
The embedded domain has several requirements that other domains do not
What is missing from programming languages that it wants?
  Sense of time
  Sense of energy

## Slide 13: Programming languages have no sense of time
Imagine a system that needs to send messages to a motor every 10 milliseconds
  Write a function that definitely completes within 10 milliseconds
Accounting for timing when programming is very challenging
  We can profile code and determine timing at runtime
  If we know many details of hardware, instructions can give timing
    Unless the code interacts with external devices

## Slide 14: Determining energy use is rather complicated
Software might
  Start executing a loop
  Turn on/off an LED
  Send messages over a wired bus to another device
Determining energy these operations take is really difficult
  Even with many details of the hardware
  Different choices of processor clocks can have a large impact
  Often profiled at runtime after writing the code
    Iterative write-test-modify cycle

## Slide 15: Break + Say hi to your neighbors
Things to share
  Name
  Major
  One of the following
    Favorite Candy
    Favorite Pokemon
    Favorite Emoji

## Slide 16: Break + Say hi to your neighbors
Things to share
  Name -Branden
  Major -Electrical and Computer Engineering, and Computer Science
  One of the following
    Favorite Candy - Twix
    Favorite Pokemon - Eevee
    Favorite Emoji - 🍢

## Slide 17: Outline
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 18: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)

## Slide 19: Cross compilers compile for different architectures
The compiler we’ll be using is a cross compiler
  Run on one architecture but compile code for another
    Example: runs on x86-64 but compiles armv7e-m
GCC is named: ARCH-VENDOR-(OS-)-ABI-gcc
  arm-none-eabi-gcc
    ARM architecture
    No vendor
    No OS
    Embedded Application Binary Interface
  Others: arm-none-linux-gnueabi, i686-unknown-linux-gnu

## Slide 20: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables

## Slide 21: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do traditional computers handle this?

## Slide 22: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do traditional computers handle this?
  Virtual memory allows all applications to use the same memory addresses
Embedded solution
  Only run a single application
  Provide an LD file
    Specifies memory layout for a certain system
    Places sections of code in different places in memory

## Slide 23: Anatomy of an LD file
nRF52833: 512 KB Flash, 128 KB SRAM
First, LD file defines memory regions
  MEMORY {
  FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x80000
  RAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x20000
  }
A neat thing about microcontrollers: pointers have meaning
  Just printing the value of a pointer can tell you if it’s in Flash or RAM

## Slide 24: Anatomy of an LD file
It then places sections of code into those memory regions
  .text : {
  KEEP(*(.Vectors))
  *(.text*)
  *(.rodata*)
  . = ALIGN(4);
  } > FLASH __etext = .;
  .data : AT (__etext) {
  __data_start__ = .;
  *(.data*)
  __data_end__ = .;
  } > RAM
  .bss : {
  . = ALIGN(4);
  __bss_start__ = .;
  *(.bss*)
  . = ALIGN(4);
  __bss_end__ = .;
  } > RAM

## Slide 25: Sections of code
Where do these sections come from?
Most are generated by the compiler
  .text, .rodata, .data, .bss
  You need to be deep in the docs to figure out how the esoteric ones work
Some are generated by the programmer
  Allows you to place certain data items in a specific way
  __attribute__((section(".foo")))
  int test[10] = {0,0,0,0,0,0,0,0,0,0};

## Slide 26: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables
Output: a binary (or hex) file

## Slide 27: Loading the hex file onto a board
This is a use case for JTAG
  You provide it a hex file which specifies addresses and values
  It writes those into Flash on the microcontroller
The LD file already specified addresses
  So passing around hex files is enough to load an application
  But a hex file for one microcontroller won’t work on another with a different memory layout

## Slide 28: Example
Demonstrated in the blink application in lab repo
  https://github.com/nu-ce346/nu-microbit-base/tree/main/software/apps/blink

## Slide 29: Outline
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 30: Embedded environments
There are a multitude of embedded software systems
  Every microcontroller vendor has their own
  Popular platforms like Arduino
We’re using the Nordic software development libraries plus some extensions made by my research group
  It’ll be a week until that matters for the most part
  We’ll start off by writing low-level drivers ourselves without libraries

## Slide 31: Software Development Kit (SDK)
Libraries provided by Nordic for using their microcontrollers
  Actually incredibly well documented! (relatively)
  Various peripherals and library tools
SDK documentation
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/index.html
  Warning: search doesn’t really work
Most useful link is probably to the list of data structures
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/annotated.html

## Slide 32: nRF52x-base
Wrapper built around the SDK by Lab11
  Branden Ghena, Brad Campbell (UVA), Neal Jackson, a few others
  Allows everything to be used with Makefiles and command line
  https://github.com/lab11/nrf52x-base
We include it as a submodule
  It has a copy of the SDK code and softdevice binaries
  It has a whole Makefile system to include to proper C and H files
  We include a Board file that specifies our specific board’s needs and capabilities
Go to repo to explain

## Slide 33: Break

## Slide 34: Outline
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 35: How does a microcontroller start running code?
Power comes on
Microcontroller needs to start executing assembly code
You expect your main() function to run
  But a few things need to happen first

## Slide 36: Step 0: set a stack pointer
Assembly code might need to write data to the stack
  Might call functions that need to stack registers
ARM: Valid address for the stack pointer is at address 0 in Flash
  Needs to point to somewhere in RAM
  Hardware loads it into the Stack Pointer when it powers on

## Slide 37: Step 1: set the program counter (PC)
a.k.a. the Instruction Pointer (IP) in x86 land
32-bit ARM: valid instruction pointer is at address 4 in Flash
  Could point to RAM, usually to Flash though
  Automatically loaded into the PC after the SP is loaded
    Again, hardware does this

## Slide 38: Step 2: “reset handler” prepares memory
Code that handles system resets
  Either reset button or power-on reset
  Address was loaded into PC in Step 1
Reset handler code:
  Loads initial values of .data section from Flash into RAM
  Loads zeros as values of .bss section in RAM
  Calls SystemInit
    Starts correct clocks for the system
    Handles various hardware configurations/errata
  Calls _start
nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/gcc_startup_nrf52833.S nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/system_nrf52.c

## Slide 39: Step 3: set up C runtime
_start is provided by newlib
  An implementation of libc – the C standard library
  Startup is a file usually named crt0
Does more setup, almost none of which is relevant for our system
  Probably is this code that actually zeros out .bss
  Sets argc and argv to 0
  Calls main() !!!
https://sourceware.org/git/gitweb.cgi?p=newlib-cygwin.git;a=blob_plain;f=libgloss/arm/crt0.S;hb=HEAD

## Slide 40: Online writeup with way more details and a diagram
Relevant guide!!
  https://embeddedartistry.com/blog/2019/04/17/exploring-startup-implementations-newlib-arm/
  Covers the nRF52!

## Slide 41: Outline
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process