## Slide 1: Lecture 09 Sensors
CE346 – Microprocessor System Design
Branden Ghena – Fall 2022
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Most groups should have now received feedback from me on their proposals
  I’ll get to the rest either today or tomorrow
  For some of you, I gave action items, be sure to handle those soon
Design presentations will be next week Tuesday & Thursday
  Details are on Campuswire
  Be sure to check the schedule for which day you are on

## Slide 3: Today’s Goals
Think about sensing and sensors
Explore a variety of sensor types, how they are made, and what their capabilities are
Discuss an example research platform with a custom sensor

## Slide 4: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 5: Definitions
A sensor is a device that measures a physical quantity
  Temperature sensor
  Light sensor
  Microphone
An actuator is a device that modifies a physical quantity
  Heater
  Motor
  Speaker

## Slide 6: Sensors transform quantity into an electric signal
Microcontrollers can interact with analog signals
  Generating an analog signal proportional to physical quantity makes the quantity able to be sensed
How do we generate an electrical signal?
  Ohm’s Law: V = I * R (Voltage = Current * Resistance)
  Vary any one of these three and an analog signal is created
    Resistive sensors are common
    As are sensors that produce a voltage/current

## Slide 7: Resistive sensors
  L: length of the conductor
  A: area of the conductor
  ρ: resistivity of the conductor material
Various materials have resistivity that is itself a function
  Based on temperature, light, strain, etc.

## Slide 8: Using a resistive sensor
Place in series with another resistor
  Between VCC and ground
Measure voltage between the two relative to ground
Forms a “voltage divider”

## Slide 9: Voltage divider
  Vin is a voltage source
  R1 and R2 are resistors
If R1 == R2
  Vout = Vin/2
Smaller R1 means larger Vout
  Vout approaches Vin
Important! Learn this

## Slide 10: Generating voltage via piezoelectric effect
Compression of the material generates a voltage
Various sources of compression:
  Air Pressure
  Acceleration
  Strain

## Slide 11: Understanding sensor voltage
Once you get a voltage, what do you do with it?
Need to understand the transfer function between voltage and the sensed quantity
  Examples for an accelerometer: senses acceleration
Hopefully, function is linear
  Occasionally, function is NOT

## Slide 12: Affine sensor model (for linear sensors)
x is the quantity being sensed
F(x) is a voltage proportional to that quantity
Parameters
  a: sensitivity, units Volts/quantity
    Change in voltage per change in quantity
  b: bias, units Volts
    Offset in voltage for zero of the quantity

## Slide 13: Bias and sensitivity example
Accel
x(g)
Vreadout (V)
F(x)
ADC (16-bit)
[0,3 V]  [0, 216-1]
-3.6
3.6
0
0
1.5
3.0
0
32768
65535
F(x) = ax+b
b = 1.5
a = 1.5/3.6 = 0.417 V/g

## Slide 14: Understanding transfer function: ADXL330 datasheet
Ratiometric
  Relative to sensor voltage
Bandwidth
  Data update speed of the sensor

## Slide 15: Active and passive sensing
Passive Sensing
Active Sensing

## Slide 16: Active and passive sensing
We usually focus on passive sensing
  Cheaper and lower energy costs!
Active sensing examples
  Flash photography
  Ultrasonic distance sensing
  Lidar and Radar

## Slide 17: Intelligent sensors
Many embedded sensors are more intelligent than simple analog
Combine it with a built-in ADC
  Can be more finely tuned and calibrated for accuracy
  Now gives digital output over some wired communication mechanism
Combine it with additional circuitry / computation
  Automatically filter data
  Detect specific signal patterns and interrupt
I pointed most groups at intelligent sensors (QWIIC)

## Slide 18: Break + Question
Accelerometer
  Measures 0-5 g
  Over a 0-5v range
What is sensitivity?
What is bias?
What acceleration is the voltage reading 3.5 volts?

## Slide 19: Break + Question
Accelerometer
  Measures 0-5 g
  Over a 0-5v range
What is sensitivity? 1 v/g
What is bias? 0 v
What acceleration is the voltage reading 3.5 volts?
  3.5 v = 1v/g * x + 0v -> 3.5 g

## Slide 20: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 21: Digital temperature sensor
Thermostat
  Original meaning of the word
Heat bends a strip of two different metals
Switches circuit on/off based on the temperature

## Slide 22: Thermo-electric temperature sensing
Thermocouple generates a voltage based on temperature
Can be used to harvest energy to run system
  Part of RTG design

## Slide 23: Resistive temperature sensing
Thermistor varies resistance based on temperature
Set up as a voltage divider to measure
Advantages: extremely cheap and easy to use
Disadvantages: non-linear transfer function
Chart: Temperature (C)

## Slide 24: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 25: Measuring light
Lux: unit of illuminance
Beware spectrum sensitivity

## Slide 26: Resistive light sensing
Photocell changes resistance with light (non-linear)
Kit version:
10 kΩ when dark
1 kΩ when light

## Slide 27: Photodiodes leak current based on light levels
When voltage is applied in reverse to an ideal diode, no current flows
But some small amount of current leaks for real-world diodes
  Proportional to light levels!
LEDs can be used as (crappy) photodiodes as well!
  Apply reverse voltage
  Read in leak current as voltage across a resistor using ADC
https://wiki.analog.com/university/courses/electronics/electronics-lab-led-sensor

## Slide 28: Light color sensing
Respond to specific light colors separately
Intelligent sensor: photodiodes combined with ADCs and a wired interface (I2C)
Allows interrupting based on comparator too

## Slide 29: Passive Infrared (PIR) sensor
Detect movement in the environment
  By detecting change in IR levels
Often come with plastic lens cover to improve field of view and range

## Slide 30: PIR sensors come in digital and analog forms
Digital includes a preconfigured comparator

## Slide 31: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 32: Inertial Measurement Unit (IMU)
IMUs (a.k.a 9 degree-of-freedom, 9DOF) are used for tracking motion of a device
  Acceleration (X, Y, Z axes)
  Rotation (X, Y, Z axes)
  Magnetism (X, Y, Z axes)
  Sometimes 6DOF with Acceleration + one of the others
Intelligent sensing: combines multiple sensors, ADCs, and computation with a wired interface
  9 analog inputs would otherwise be too many
Can be used to track motion, determine transportation method
  Smartphones, Robotics, etc.

## Slide 33: Sensing acceleration
Goal: create a voltage that changes based on force

## Slide 34: Microelectromechanical Systems (MEMS)
Same concept, but within an IC and 1 to 100 micrometers in size

## Slide 35: Using accelerometers
Accelerometers usually measure in g’s
  Where 1 g equals acceleration due to Earth gravity
Determining distance from acceleration is possible
  But messy. Error is squared when integrating
  Needs careful filtering and is only accurate over short periods
  Often fills in gaps between GPS samples (or other localization systems)
Accelerometers also work as tilt sensors
  Constantly sensing pull of gravity

## Slide 36: Gyroscopes
Measures angular velocity
  Usually lower limit than you might hope
  <10 rotations per second
Usually, we want angle instead of rotation speed
  Integrate signal to determine current angle
  Combine noise and DC bias with integration and you get a continuously accumulating error: drift

## Slide 37: Magnetometer
Measures the magnetic field
Usually used in devices as a compass
  Detect Earth’s magnetic field orientation
Problem: Earth’s magnetic field often overwhelmed by local magnetism when indoors
  Large chunks of metal in walls, for example
  Or other metal parts nearby on the circuit board!!
Satellites can use magnetometers for localization

## Slide 38: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 39: Other sensors
Environment: Pressure, Humidity, Air Velocity, Air Quality
Distance: Ultrasonic, Lidar, or Radar
Biometric: Pulse Oximeter, Heart Rate
Agricultural: Soil moisture

## Slide 40: Break + Open Question
How are new sensors discovered/created?

## Slide 41: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study

## Slide 42: PowerBlade current sensing
Example of creating a custom sensor
PowerBlade goals
  Sense current and voltage in real-time
  Be small enough to be deployable
Problem
  To measure current, you usually have to break the circuit
  But PowerBlade attaches in parallel

## Slide 43: Measuring current
Coil of wire in a changing electric/magnetic field produces a voltage
One way to make inductors is as a coil of wire wrapped horizontally around a magnetic core
Re-purpose horizontally wire-wound inductor as current sensor!

## Slide 44: Sensor placement
Is in the middle or close to a prong the best choice?
Turns out it’s closer to a prong
  Decreases with distance squared
Angled like the magnetic field is

## Slide 45: Measuring sensor values
Sensor output is very small
Amplify to make output large enough to accurately measure with ADC
Need to pick sampling rate
  AC: 60 cycles per second in US
  Need N * 60 measurements per second
  N=42 (as fast as we can measure)
    2520 measurements per second

## Slide 46: At first, our output signal was this green line

## Slide 47: Measurement into current
Search coil measures the derivative of current!!
Need to integrate to get signal and apply sensitivity and bias

## Slide 48: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Research case study