## Slide 1: Lecture 10 Analog Output
CE346 – Microprocessor System Design
Branden Ghena – Fall 2022
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Everyone should have gotten feedback by now
  If you haven’t, either check spam folder or I somehow forgot about you
Design presentations all next week!
  Happy to discuss things before then either after class or on Campuswire
Drop deadline is Friday next week
  I’m not worried about anyone in CE346
  But if you’re worried, I’m happy to talk about it.

## Slide 3: Today’s Goals
Discuss one last sensor: capacitive touch
Explore common methods for generating analog signals
Understand the role of Digital-to-Analog converters
Discuss the concepts of Pulse-Width Modulation
  And the nRF52 implementation of it

## Slide 4: Outline
Capacitive Touch Sensing
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM

## Slide 5: Capacitive Touch Sensor
Pull-up resistors connected to metal pads
  Also connected to GPIO pin
Acts as a capacitor connected to ground

## Slide 6: The touch pad recharges on its own
If you drive the GPIO pin attached to it low, touchpad clears low
If you make the GPIO pin an input (high impedance)
  The touchpad gets pulled high, which takes some amount of time
The more capacitance the longer this takes!
Low Capacitance
High Capacitance

## Slide 7: Capacitive touch sensing method
Drive GPIO pin low
  Connects the pad to ground
Set GPIO pin as input and enable low-to-high interrupt
  Gets an interrupt when the pad finally becomes high on its own
  Use a timer to determine time until interrupt
    ~70 μs with no finger, <= milliseconds with finger
    Needs to timeout after a few milliseconds and declare “touched”
Repeat periodically (a few times a second is probably good enough)
Sudden large increase in rise time ⇨ someone is touching!
  Finger acts as a large capacitor

## Slide 8: Capacitive touch works on any metal surface
Idea: Microbit door handle sensor
Connect a wire and a pull-up resistor to a metal door handle to sense when someone is touching it!
  Timing will be very different from capacitive pad, but should be repeatable and distinguishable from human touch

## Slide 9: Outline
Capacitive Touch Sensing
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM

## Slide 10: Digital-to-Analog Converters
Generates an analog voltage
DACs are conceptually the inverse of ADCs
  Number of bits of resolution choose analog step size
  Frequency determines step duration

## Slide 11: High resolution versus high frequency
What role does each play in a DAC? Which is more important?
High resolution can accurately represent a voltage
High frequency can accurately represent a changing voltage
In practice:
  Need high enough resolution, then as high of frequency as possible

## Slide 12: Infinite resolution is not sufficient
DAC frequency corresponds to representable signal changes
  Rise and fall times
Even an infinite resolution DAC cannot represent a signal if it is not fast enough

## Slide 13: Low-pass filter smooths output
Low-pass filter delays changes in voltage and smoothly transitions between them
  Low-frequency signals stay
  High-frequency are smoothed
Greatly improves quality of output but must be tuned to the desired signal frequency
  Usually not included in microcontroller

## Slide 14: Resistor string DAC
Use series of voltage dividers and switches to set output voltage
  Generates equally spaced voltages that can be selected between
Needs output buffer to provide stable current
Takes a lot of resistors
  And resistors take a lot of silicon

## Slide 15: Resistor string example
Input code is 101
  Selects switches such that 5/8*Vref is connected to output

## Slide 16: Break + DAC applications
What do you use an analog output for?

## Slide 17: Break + DAC applications
What do you use an analog output for?
  Audio output
    But it needs to be high quality (resolution and speed)
  Motors
    But only with a controller that actually drives them with enough current
  LED brightness
  Not Much
    And these last two can be done more easily with PWM

## Slide 18: DACs are not in all microcontrollers
Not rare, but not ubiquitous either
  Every microcontroller has GPIO
  Just about every microcontroller has an ADC
  Some microcontrollers have DACs (the nRF52833 does not!)
Reasons
  Hardware is complicated (but we could fit it if we wanted)
  Use cases are uncommon (and might need very high quality)
    Many devices can be controller digitally
  Pulse-Width Modulation (PWM) can emulate usably analog signals

## Slide 19: Outline
Capacitive Touch Sensing
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM

## Slide 20: Pulse-Width Modulation
Much easier to control high or low than an analog output
Idea: modify how long a signal is high within some switching frequency, a.k.a duty cycle
  On 50% of the time for half voltage
  On 10% of the time for tenth voltage
Duty cycle, not frequency!

## Slide 21: Analog to PWM example

## Slide 22: PWM to Analog Signal example
PWM period should be much faster than the desired analog signal
  PWM duty cycle represents the voltage along the way
  Multiple duty cycles per output point makes it more accurate

## Slide 23: Low-pass approach works here too
Importantly, many devices are inherent low-pass filters
Heaters, Motors
  Low-pass by physical design
  I.e., they can’t start/stop quickly
LEDs are not
  But our eyes are!

## Slide 24: Controlling PWM
Vary duty cycle by selecting transition points
  Time when set
  Time when unset
Repeat every cycle
  Period much faster than signal if possible
  Makes analog approximation more accurate
    The faster you run it, the less likely it matters that it is not actually analog
    Example: LED switching frequency
Duty cycle could vary cycle-by-cycle if it must

## Slide 25: PWM alignment
Can select alignment as well
  Equivalent to a phase delay
Centering produces cleaner analog output
  Less harmonics
Not relevant for most devices

## Slide 26: Every microcontroller can do PWM
Not every microcontroller has a PWM peripheral
But every microcontroller has timers and digital outputs
All that is needed is a GPIO and a Timer (or two)
  Timer determines when to turn GPIO on and off
  Often can be automated in hardware rather than use interrupt handler

## Slide 27: PWM is a method of encoding data
PWM is a pulse-width modulated signal
There are many other ways to “modulate” a signal to transmit data
  Amplitude, Frequency, and Phase are common
  Layers data on top of an existing “carrier signal”
Used especially for high-speed communication
  Wired (cable lines) or Wireless (basically everything)

## Slide 28: PWM applications
Servos
  Duty cycle chooses angle or rotation speed
Motor controllers
  Duty cycle chooses current and therefore speed
LED brightness
  And “breathing” effect
Audio
  Can sound okay if frequency is high enough

## Slide 29: Break + Open Question
Imagine you want to represent the following signal with PWM
  What should the PWM period be?
  What kinds of duty cycle values would you use? (3.3v is 100%)

## Slide 30: Break + Open Question
Imagine you want to represent the following signal with PWM
  What should the PWM period be?
    Signal period is ~10 μs
    PWM period should be at least 2x that
      10x faster seems like a good start
      Then if we want multiple PWM outputs per sample, that’s ~20-40x faster
  What kinds of duty cycle values would you use? (3.3v is 100%)
    2/3.3 = 61% duty cycle max
    0/3.3 = 0% duty cycle min

## Slide 31: Outline
Capacitive Touch Sensing
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM

## Slide 32: nRF52 PWM – theory of operation
A clock continuously adds to a counter value
  (just like the Timer peripheral does)
When the counter value reaches COMP[n], the GPIO value on channel n changes from high to low (or vice-versa)
When the counter value reaches COUNTERTOP, the GPIO value on channel n changes from low to high (or vice-versa)
  AND the counter value resets to zero

## Slide 33: nRF52 PWM peripheral
Uses internal timer to create PWM output on up to 4 pins
  4 peripherals, so up to 16 pins total
Loads compare values via DMA to rapidly vary “analog” signal

## Slide 34: PWM example
Counter increments up to COUNTERTOP, resets and continues
Period/Frequency
  Chosen by COUNTEROP and timer PRESCALER
Time
Counter Value
One PWM period

## Slide 35: PWM example
Counter increments up to COUNTERTOP, resets and continues
Duty Cycle
  COMP0 chooses first toggle point for OUT[0]
  Second toggle point is when the timer resets
Time
Counter Value
(right-aligned)
(left-aligned)
One PWM period

## Slide 36: Center-aligned PWM
Up-and-down mode enables center-aligned PWM
Duty Cycle
  Comp triggers toggle on rise
  Comp triggers toggle again on fall
)

## Slide 37: Trading speed and accuracy
How do you get the most accurate PWM values?
  Select the largest COUNTERTOP possible
    Most possible COMP values
    Up to 15-bit resolution (32767 max)
How do you get the fastest PWM frequency?
  Select the smallest COUNTERTOP possible
  PRESCALER also affects this
    16 MHz – 128 kHz (8 possible values)
Fastest PRESCALER + largest COUNTERTOP equals 488 Hz
  Likely need to sacrifice resolution for speed

## Slide 38: DMA with PWM
Every N periods it loads a new configuration from RAM
  N combined with PRESCALER and COUNTERTOP chooses “analog signal” period
Configuration sets COMP values for each output channel
  Also sets polarity (starting value: low or high)
Application of memory loads to channels is configurable

## Slide 39: Waveform mode
Also has the option to change COUNTERTOP every N PWM periods
Allows arbitrary waveforms to be created
  Frequency changes every period
  Duty cycle can also change each period
We don’t normally need this, as a constant frequency with changing duty cycle should be fine

## Slide 40: Other configurations
How many times the entire DMA sequence repeats
  0 to large number, infinite with a configuration in SHORTS
How long to delay between repeating sequence cycles
  Repeats last PWM configuration
Two DMA sequence configurations (0 and 1)
  Can modify one while the other is playing
  Allows continuous signal (for example, music)

## Slide 41: nRF SDK PWM driver
https://infocenter.nordicsemi.com/index.jsp?topic=%2Fsdk_nrf5_v16.0.0%2Fgroup__nrfx__pwm.html
Initialize PWM with base configuration
  Output pins, Clock frequency, COUNTERTOP, DMA grouping mode
  Handler for events from peripheral
nrfx_pwm_simple_playback(instance, sequence, count, flags)
  Instance: pointer to global variable with registers
  Sequence: struct containing sequence to be played (see next slide)
  Count: number of times (1 or more) to repeat sequence
  Flags: stop peripheral when done, loop forever, various events

## Slide 42: Sequence struct
values: pointer to array of uint16_t values (union of types)
length: length of array
repeats: number of times to repeat each individual value
  Sets period for “analog value” changing

## Slide 43: Example, playing a note
Pick PWM frequency to match note frequency
  Combination of PRESCALER, COUNTERTOP, and repeats
  440 Hz for the note A
    PRESCALER 1 MHz, COUNTERTOP 2273 -> 440 Hz
Set duty cycle of PWM to control volume
  50% duty cycle -> COMP value of 1137
Set sequence with an array of length 1, content is {1137} (polarity 0)
  Repeats 0, end_delay 0
Set playback_count to 1 and flags to NRFX_PWM_FLAG_LOOP

## Slide 44: Controlling LED Matrix brightness
Option 1: PWM peripheral
  Need to use multiple PWM peripherals to get 5 pins
  Could only allow brightness to be controlled for the entire matrix
  Then use a single PWM output to control the row
    When timer fires, change which row pin is used for PWM
Option 2: do it manually (for individual control)
  Can’t determine duty cycle when the row is turned on
    Each row already at 100 Hz, duty cycling would be slower and visible
  Instead add 5 new one-shot app timers, one for each column
    Fire at some time while the row is active (within that 2 ms)
    Use to toggle column LED back to off

## Slide 45: Outline
Capacitive Touch Sensing
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM