## Slide 1: Lecture 14 USB & CAN
CE346 – Microprocessor System Design
Branden Ghena – Fall 2022
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Hardware handout again at the end of class today
  I’ve got a bunch of hardware!
We’ll hand out Microbits next week Tuesday at the end of class
  Also the date of our last quiz!
No lab this Friday! Everybody enjoy your extra time!
  And use it to work on projects!

## Slide 3: Administrivia
Lecture schedule for the rest of the quarter
  Thursday (11/10) – Wireless Communication
  Tuesday (11/15) – Nonvolatile Memory & Energy Management
    Also the final quiz
  Thursday (11/17) – Microprocessors + Wrapup
  Tuesday (11/22) – Embedded Systems Research
    Tuesday before Thanksgiving
  Tuesday (11/28) & Thursday (12/01) – Project Office Hours

## Slide 4: Today’s Goals
Discuss more advanced wired communication protocols
  With a little less detail
  Just give a taste of what they are like
Think about higher-layer concerns like data routing, interpretation, and reliability

## Slide 5: Outline
USB
CAN

## Slide 6: USB references
USB in a NutShell
  https://www.beyondlogic.org/usbnutshell
Other stuff I found useful
  https://www.usbmadesimple.co.uk/
  http://kofa.mmto.arizona.edu/stm32all/blue_pill/usb/an57294.pdf
  https://en.wikipedia.org/wiki/USB

## Slide 7: Universal Serial Bus (USB)
Pervasive wired communication protocol
  Universal accurately applies!
  Targets predominantly external devices over a plug/cable
Good combination of simple and capable
  Base version for simple devices does not require too much in terms of pins or resources
  More complex versions can transfer a significant amount of data
    These grew organically over time though
Great support for interoperability
  Generic device profiles that allowed for plug-and-play
  Supported by OS initiatives to include driver software

## Slide 8: USB is a layered protocol
USB protocol describes how to:
  Electrically send bits
  Send frames of multiple bytes
  Communicate data between two devices
  Communicate specific application data (through device classes)
Much more complicated, compared to others
  SPI: only how to electrically send bits
  UART and I2C: how to send frames of bytes

## Slide 9: Roles and topology
Hosts and Devices
  USB On-The-Go allows host negotiation
    Added later. Support devices like smartphones
Host is in charge of communication (“Upstream”)
Devices provide various capabilities Host can interact with (“Downstream”)
Tiered star topology
  Host connects to hubs, which connect to devices
  Up to 127 devices per hub. Up to 5 layers of hubs

## Slide 10: USB signals
Four signals
  Vbus (5 volts, can power devices)
  D+
  D-
  Ground
D+/D- are a differential pair
  Signals are inverses of each other
    Usually, occasionally act separately to signal special conditions
    Increases voltage difference between states (5 - -5 = 10 volts)
  Wires are twisted to avoid interference

## Slide 11: Synchronizing data
No clock signal!! How is USB so fast?
  Partially EE magics: better receivers, matched wire impedance
  Partially easier to distinguish signal states
  Also guaranteed transitions, which allow resynchronization
Transitions are used to denote data (non-return-to-zero inverted)
  With guaranteed transition in within every 8 bits (bit stuffing)
  Allows clocks on the two devices to synchronize

## Slide 12: USB speeds
USB 1.0
  Low Speed: 1.5 Mbps
    Not clear if this is used anymore
  Full Speed: 12 Mbps
    Microcontrollers tend to support Full Speed
    We’re focusing on details from it
USB 2.0
  High Speed: 480 Mbps
USB 3.0+
  Super Speed: 5-20 Gbps
  Adds multiple parallel data connections
Pull-up resistors allow for detection of a plugged device
Also identify speed

## Slide 13: USB interactions
General transaction format
  Host sends a Token packet: identifies transfer direction and device
  Host or Device send data depending on direction
  Other side acknowledges receipt of data
Like a maxed-out version of the I2C transaction pattern
  Host always initiates communication
Reading data from Device
Writing data to Device

## Slide 14: USB token packets
Packet fields
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Token type: Setup device, Read from device, or Write to device
  Address+Endpoint to identify Device
  CRC, (Cyclical Redundancy Check) to detect bit errors
    5-bit CRC

## Slide 15: USB data packets
Packet fields
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Data: application data
  Data, up to 1023 bytes (full speed, often capped at 64 for microcontrollers)
  CRC, (Cyclical Redundancy Check) to detect bit errors
    32-bit CRC

## Slide 16: Cyclic Redundancy Check (CRC)
Determines if the data received matches the data sent
  CRC value is calculated on original data and appended to message
  CRC value is recalculated on the received data
  Value appended to message and value recalculated MUST match
Essentially some kind of hash operation
  Turns many bits into some smaller number of bits that are unique-ish
CRC algorithms are:
  Particularly good at single bit errors AND contiguous bit errors
  Relatively simple to calculate
  Very widely used in communication

## Slide 17: Interacting with USB devices
Each Device is given a separate address on the bus
Each Device also has a number of Endpoints
  Logical communication channels
  Direct data and guide communication patterns

## Slide 18: USB endpoint types
Interrupt transfers
  Guaranteed latency, small amounts of data
  Important sensor data (mice and keyboards)
  Polled frequently by Host
Bulk transfers
  Sporadic large transfers, reliable communication
  General reading/writing of data (flash drives and USB serial)
  Polled by Host whenever there is available bandwidth
Isochronous transfers
  Guaranteed data rate, unreliable communication
  Continuous data streaming (audio and webcams)
  Polled frequently by host

## Slide 19: USB control endpoint
Every USB Device has a special Control endpoint as well
Used for setting up the USB Device driver on the Host
Initializing a Device
  Host sends SETUP transaction requesting device descriptor
  Host performs IN transaction to read device descriptor
  Host performs OUT transaction to write device status

## Slide 20: USB device descriptors
Packed version of tree structure describing the device
  Interfaces it provides
  Endpoints associated with each interface

## Slide 21: Example Microbit
Interface: Communications, Abstract (modem), CDC
  Endpoint: 3, IN, Interrupt
Interface: CDC Data, CDC DATA interface
  Endpoint: 1, IN, Bulk
  Endpoint: 2, OUT, Bulk
Interface: Vendor Specific Class, Subclass, Protocol
  Endpoint: 5, IN, Bulk
  Endpoint: 4, OUT, Bulk
Interface: Mass Storage, SCSI, MSD interface
  Endpoint: 7, IN, Bulk
  Endpoint: 6, OUT, Bulk
SEGGER JTAG interface
Virtual serial device
USB external filesystem

## Slide 22: lsusb output
lsusb
  List USB devices
Combine with –s flag to select a single device
Combine with -v flag for verbose mode with more information

## Slide 23: Minimal virtual serial USB Device
Virtual Serial Device
  Endpoint 0: Control, IN/OUT
    Respond to IN requests by setting up OUT with a buffer of descriptor data of the correct size
  Endpoint 1: Interrupt, IN
    Needed for serial modem controls, just ignore it
  Endpoint 2: Bulk, OUT
    Connect to buffer from _write() (just takes raw characters)
  Endpoint 3: Bulk, IN
    Connect buffer to _read() (just provides raw characters)

## Slide 24: HID USB Device (Human Interface Device)
Used for human interaction devices, like keyboard/mouse
“Report” structure is provided over Interrupt IN endpoint
  Or on demand via Control IN endpoint
Example mouse with x,y and three buttons

## Slide 25: USB summary
Specification for fast data communication
Specification for interacting with abstract device types
  Connects correct driver to interpret and send data
Pros
  Very fast
  Very interoperable
Cons
  Hardware and software are way more complex than simple protocols like UART, SPI, and I2C
  Not very energy efficient

## Slide 26: nRF52 USBD
Implements USB Device (not Host)
  Control endpoint
  14 bulk/interrupt (7 IN, 7 OUT)
    64-byte transfers
  2 isochronous (1 IN, 1 OUT)
    1023-byte transfers
Full-speed USB
  With 5 volt signals

## Slide 27: Break + Question
What are the ramifications of many USB devices sharing a bus?
  Consider: throughput and latency
What if I really had 127 USB mice on a single USB hub?
  What if it was microphones instead?

## Slide 28: Outline
USB
CAN

## Slide 29: Controller Area Network (CAN bus)
Designed for highly reliable interactions within a vehicle
Multi-master with arbitration
  Similar to I2C
Mechanism for sending messages with “identifiers”
  Identifies the data in the message, not the device its for
  Lower value identifiers have high priority
  All messages are received by all CAN nodes
    Which can decide at higher levels which identifiers they care about

## Slide 30: CAN physical connections
Two differential, wired-AND signal lines
  Transitions are used to transmit bits (non-return-to-zero) with bit-stuffing
  Combines aspects of USB and I2C
  125 kHz – 5 Mbps speeds

## Slide 31: CAN packet format
11-bit identifier
  Check bits as they are sent to see if you win arbitration
Up to 8 bytes (64 bits) of data
CRC for checking
Acknowledgement
  Like I2C, let the line float and see if another device responds
  If not, explicitly retransmit!

## Slide 32: CAN message types
Data frame
  Transmission of data for a certain identifier
Remote frame
  Requests data transmission of a certain identifier
Error frame
  Transmitted when an error is detected with the previous message
Overload frame
  Transmitted by a node that is too busy to respond right now

## Slide 33: CAN reliability design – detecting errors
Check for errors everywhere and appropriately handle
  Bit error
    If the value found on the bus differs from the one sent
  Stuff error
    If 6 consecutive bits of the same type are found
  CRC error
    If CRC does not match
  Form error
    Format field has unexpected values
  Acknowledgement error
    No ACK received
Devices detecting an error broadcast a message signifying it!
  Multiple devices sending the same message works without arbitration loss
  Previous message is then retransmitted

## Slide 34: CAN reliability design – handling errors
Each node accepts the possibility that maybe it is the faulty one
Track errors and successes and change device state
  Passive: limited error signaling and transmissions
  Bus off: does not transmit in any way
Idea is that the CAN controller hardware can be faulty but still detect it in some cases

## Slide 35: CAN summary
Designed for reliable vehicular communication
Multi-master bus with serial communication
Pros
  Highly reliable
  Extensible to many devices
Cons
  Special-purpose design. Whole system has to agree on identifiers
  Relatively slower throughput

## Slide 36: Outline
USB
CAN