## Slide 1: Lecture 06 Timers
CE346 – Microprocessor System Design
Branden Ghena – Fall 2023
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Last chance for Lab1 checkoffs 7:00-8:30 today
  Looks like ~4 groups to go, so it shouldn’t be too bad
Don’t forget to answer the postlab questions on Gradescope
  You and your partner can work on them together, but submit separately
  Due by Tuesday this week only
Lab2 tomorrow! Virtual Timer Lab
Project proposals due next week Thursday!
  Be sure to find a group. Fill out the survey if you want to find someone!

## Slide 3: Today’s Goals
Understand the role of clocks in a microcontroller
Explore functionality of various timer peripherals on the Microbit

## Slide 4: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog

## Slide 5: What are clocks?
Clock signals, in the microcontroller context, are oscillating square wave signals used to switch transistors and latch inputs
A clock MUST be running for (almost) anything on a microcontroller to function (processor and peripherals)
  Exceptions:
    Low-power input interrupts
      GPIOTE port interrupt, Analog LPCOMP interrupt, NFC sense interrupt, USB power interrupt
    Reset signal

## Slide 6: Generating clocks
External crystal oscillator
  Creates clock signal
  Chunk of quartz
  Behaves like RLC circuit but uses less energy
Internal mechanisms
  RC oscillator
    Creates clock signal
    Less accurate and higher energy than crystal
  Phase-Locked Loop (PLL)
    Multiply input to create new higher frequency clocks

## Slide 7: Microbit crystal for nRF52833

## Slide 8: Clocks and energy
Fundamental tradeoff
  Faster clock gets things done faster but uses more energy
  Slower clock uses less energy but gets things done slower
  Which to use depends on the situation
    CPU bound: faster clock, IO bound: slower clock
Chiang et al. “Power Clocks: Dynamic Multi-Clock Management for Embedded Systems” EWSN 2021
Example of clock selection for a mixed load (part IO, part CPU)
Energy consumed becomes a horizontal line when the task is completed

## Slide 9: Controlling clocks
Some microcontrollers provide extremely fine-grained control over clocks
  Really complicated section of code to get working
  Many combinations are invalid
  Manually enable/disable clocks as needed
nRF52 instead gives almost no control but is easier to use
  One 64-MHz clock for processor
  Multiple peripheral clocks, but (most) peripherals are hardwired to one
    16 MHz for almost all peripherals (PDM and I2S are 32 MHz)
  Low-frequency 32 kHz clock for low-power peripherals
  Automatically enables/disables clocks

## Slide 10: nRF52833 clocks
Optional: for lower energy and higher accuracy

## Slide 11: Electrical characteristics
Active power of clocks
  32 kHz crystal run current: 0.23 μA
  32 kHz RC oscillator run current: 0.70 μA
  32 MHz crystal average run current: 300-700.00 μA
  32 MHz standby current: 110.00 μA
Startup time for external crystals
  32 kHz crystal: 250-500 ms (milliseconds!!!)
  32 MHz crystal: 60-200 μs
  Beware: switching can lead to delays and instability
    nRF52 uses RC oscillator while crystal is not yet ready

## Slide 12: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog

## Slide 13: Timer peripherals
Common need for embedded systems: sense of time
  Start this behavior after a certain amount of time
  Stop this behavior after a certain amount of time
  Measure how much time passed between two events
Timer peripherals
  Input is one of the system clocks
  Counts up a register at each clock tick
    Looking at register at start and end can give real-world duration
  Compare to saved value and trigger interrupt on match
    Allows interrupts to be scheduled in the future

## Slide 14: Discussion
What is the finest granularity you might need from a timer?
  Give an example of the use case
What is the longest duration you might need from a timer?
  Give an example of the use case

## Slide 15: Discussion
What is the finest granularity you might need from a timer?
  Give an example of the use case
What is the longest duration you might need from a timer?
  Give an example of the use case
Concern: high granularity for long durations require MANY bits
  We often optimize for one of the other

## Slide 16: Timer peripheral on nRF52833

## Slide 17: Input and Prescaler
𝑓TIMER =
Prescaler is a 4-bit number
  Possible timer input clocks: 16 MHz – 488 Hz
Ticks counted with (up to) 32-bit internal Counter:
  Minimum
    268 seconds until overflow
    62.5 ns per tick
  Maximum
    101 days until overflow
    2.04 ms per tick

## Slide 18: Alternate input source for counter mode
Counter mode works with non-timer inputs
  E.g. GPIO input event
Count anything!

## Slide 19: Capture/Compare registers (CC)
32-bit storage registers (each timer has multiple)
  Uses: capturing or comparing
On Capture[n] event
  Internal Counter value copied to CC[n]
  Then you can read the former Counter value from CC[n]
Capture used to measure durations of events
  Capture can be triggered by software or by Events from other peripherals
  Multiple registers to measure multi-part events

## Slide 20: Comparing with CC registers
When internal Counter value equals a CC register
  Corresponding Compare[n] event is triggered
  Can trigger interrupts
Usually written to in advance to start/stop behavior
  Toggle LED every second
  Sample sensor every five minutes
  Refresh LED matrix every 1/60 seconds

## Slide 21: The nRF52833 has multiple Timer instances

## Slide 22: Bonus concept: shorts
In a peripheral: Tasks are inputs and Events are outputs
Shorts connect an Event to a Task within a peripheral
  Tasks and Events idea is fairly nRF specific
Timer shorts
  Connect Compare[n] to Clear
  Connect Compare[n] to Stop

## Slide 23: Usage: how do we set a one second timer?
Assume timer is already running
Get current time from timer
Add 1 second worth of ticks to it
  is the number of ticks per second
Set an unused Compare register to value
Enable interrupts for that Compare event
Warning: what if you’re setting a 1 us timer instead? Or a 100 ns timer?
Timer could expire before software writes it to the peripheral.

## Slide 24: Check your understanding
Prescaler value is 4
Current internal Counter value is 0x1000
Want a 0.5 second timer
What do you set the CC[0] register to? (32-bits)
𝑓TIMER =

## Slide 25: Check your understanding
Prescaler value is 4
Current internal Counter value is 0x1000
Want a 0.5 second timer
What do you set the CC[0] register to? (32-bits)
  1 MHz Timer frequency -> 500,000 ticks in 0.5 seconds
  500000 -> 0x7A120
  Plus initial value of counter = 0x7B120
𝑓TIMER =

## Slide 26: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog

## Slide 27: Choosing resource amounts is a problem
Problem: applications may require any number of resources
  Particularly in this case: peripherals
  For example, how many timers should there be?
But hardware has to pick some number to provide
  More is wasted cost
  Too few and applications cannot succeed
Solution: virtualize the resource

## Slide 28: Virtualization pattern
Create a queue of requests and a pool of resources
  N requests to M resources
Application requests are queued when they come in
  Rather than serviced immediately
When a resource is available
  Pop request from queue (by some priority)
  Service with hardware
  Then wait until another resource is available

## Slide 29: Example: sending serial messages
Serial messages (such as printf() strings) are sent via UART
  UARTE peripheral (we’ll talk about this later)
nRF52 has two UARTE peripherals
  Can be attached to any output pins
  Changing pins is a quick operation
What if we want to talk to three serial devices?
  Console (printf output)
  GPS (NMEA)
  WiFi radio (AT commands)

## Slide 30: Virtualized UART
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
Empty

## Slide 31: Virtualized UART: serves request with hardware
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}

## Slide 32: Virtualized UART: serves until resources are full
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}

## Slide 33: Virtualized UART: additional requests are queued
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 34: Virtualized UART: moves to next item when complete
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 35: Virtualized UART: moves to next item when complete
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 36: Challenges to making virtualization work
How fast are requests coming in?
  Requests more quickly than service are an unsatisfiable system
How long does it take to reconfigure the resource?
  Long delays could mean high latency
  Might want to optimize for requests with same configuration first
Need to ensure all of the configuration changes
  Common bug: forget to modify part of one register and system works most of the time, but not in all cases
Need ability to queue requests
  Usually stored in a linked list structure
  Dynamically… But we generally want to avoid dynamic memory

## Slide 37: Dynamic resource allocation options
Create a queue with a maximum size in Virtual Driver
  Some number larger than the hardware picked, based on app knowledge
  Still either runs out or wastes memory
Just use malloc()
  Is actually possible on the nRF52 with newlib (libc implementation)
  Might run out, but then just wait for requests to complete
Create list nodes individually as global variables
  Application decides how many it needs at compile time
  Passes them into the Virtual Driver at first use
    “Here’s my request and a linked list node to store it in”

## Slide 38: Another example: managing multiple timers
You often have tasks that look like this:
Most easily thought about as three separate timers
  But maybe the system doesn’t have that many timers to spare!
  Virtualization can help

## Slide 39: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10010, A
10050, B
10110, C
20000, D
time
CC Register: 10010
10010
10050
10110
20000

## Slide 40: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10010, A
10050, B
10110, C
20000, D
time
CC Register: 10010
10010
10050
10110
20000
Call timer handler A!
Update CC register and list

## Slide 41: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10050, B
10110, C
20000, D
time
CC Register: 10050
10010
10050
10110
20000

## Slide 42: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10050, B
10110, C
20000, D
time
CC Register: 10050
10010
10050
10110
20000
Call timer handler B!
Update CC register and list

## Slide 43: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10110, C
20000, D
time
CC Register: 10110
10010
10050
10110
20000

## Slide 44: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10100, E
10110, C
20000, D
time
CC Register: 10100
10010
10050
10110
20000
New request arrives for 10100
Enqueue and sort queue
Update CC if first request has changed

## Slide 45: Enqueuing timer requests
Timer requests come in the form: {N seconds from now}
  timer_request(duration, handler);
Requests are always relative to the current time
Need to enqueue by expiration time
  Duration + Current Time
  Allows for a globally sortable list
    Need to decide how to handle overflow logic in real world

## Slide 46: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
  Check for this, and call handler manually if necessary
Timer Requests
10100, E
10110, C
20000, D
time
CC Register: 10100
10010
10050
10110
20000
Handle 10100 event, Call E

## Slide 47: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
Timer Requests
10110, C
20000, D
time
CC Register: 10110
10010
10050
10110
20000
Update list
Update CC register
Oh no! That’s in the past!!

## Slide 48: Break + Question
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
What do we do about the missed timer?
  There are multiple “correct” answers here

## Slide 49: Break + Question
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
What do we do about the missed timer?
  There are multiple “correct” answers here
Some options:
  Just call handle that timer event as soon as possible
    Possibly telling it about the delay
  Crash the system! (Deadlines cannot be missed in some systems)
    Or at least enter some fault recovery handler

## Slide 50: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
  Check for this, and call handler manually if necessary
Timer Requests
20000, D
time
CC Register: 20000
10010
10050
10110
20000
Call C manually
Update list and CC register again

## Slide 51: Some timers are periodic
Repeating timers are easy to add to this system
  Include a Boolean for “repeating” and the duration in the request
When timer expires
  If not repeating, just call handler and then drop it
  If repeating,
    First reinsert based on duration and new current time
    Then call the handler
      Don’t want the latency of the handler to slow us down

## Slide 52: Concurrency safety
Modifying the request structure in an interrupt context is dangerous
  New request might be in the middle of getting added
  Interrupt would run right in the middle of that
  Literally an OS data race example
Solution: disable interrupts during critical section
  Whenever editing request structure
  Enable interrupts after, which may result in an event
    Note: Interrupt handler might now fire but have no work to do. Should always check if something should actually be handled first

## Slide 53: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog

## Slide 54: Real-time Counter
Low-power (32 kHz) version of Timer
  Only a 24-bit internal Counter
Note: abbreviated RTC, but that already means something else (Real-Time Clock)

## Slide 55: Differences between Real-Time Counter and Timer
Runs off of LFCLK instead of HFCLK
  With smaller prescaler value (4096 vs 32768)
24-bit counter vs 32-bit counter for Timer
Can read the Counter value directly
  No need for Capture task
Otherwise extremely similar. Just a low-power version of Timer

## Slide 56: Time resolution for Real-Time Counter
𝑓TIMER =
Resolution
  Minimum: 30.517 μs ticks, overflows in 512 seconds (24-bit Counter)
  Maximum: 125 ms ticks, overflows in 582 hours
Not as precise as the Timer (which has 62.5 ns best precision)
  Possible design: use both
    Real-Time Counter for most of the waiting
    Chained into Timer for precise remaining amount of time

## Slide 57: Comparing timer types
Real-Time Counter
  Low precision and duration
  Low energy
Timer
  High precision or duration
  High energy

## Slide 58: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog

## Slide 59: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
Why?

## Slide 60: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
Why?
Resets “state” to original values, which are likely good
  Startup is often well-tested
  It’s long-running code interacting in unexpected ways that leaves systems in a broken state

## Slide 61: Watchdog timer (WDT)
Focused on failures where the system “hangs” forever
  Maybe software, maybe hardware!
Can’t know for certain the system is hung, but can know practically
  Select a timeout that is the maximum amount of time you expect the system to ever go without looping in main()
  Multiply it by 2-10
  Set a watchdog timer to that value
If watchdog timer ever expires, it resets the system (in hardware)

## Slide 62: Watchdog configuration
timeout (seconds) =
Configure watchdog
  Can choose whether to count down during Sleep mode or Debug mode
Set a Counter Reload Value (CRV, 32-bits)
Start the watchdog timer
  Loads internal Counter to CRV value
  Starts counting down at 32 kHz

## Slide 63: Running applications with a watchdog timer
Need to periodically reset the watchdog to keep it from expiring
  Known as “feeding” the watchdog or “kicking” the watchdog
Reload Request register
  Must write sequence 0x6E524635 to reload watchdog
  Incredibly unlikely to happen by accident
While running, watchdog is protected from modification
  Configure once, run forever (at least until a reboot)
  Only option is to make periodic Reload Requests
Default off on the nRF52833 (default on for the MSP430!)

## Slide 64: Outline
Clocks
Timers
Virtualizing Resources
Real-Time Counter
Watchdog