## Slide 1: Lecture 12 Wired Communication: SPI and I2C
CE346 – Microprocessor System Design
Branden Ghena – Fall 2023
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley), Sparkfun

## Slide 2: Administrivia
Purchase requests
  Place these! Soon!
  I’m going to put a deadline for initial purchasing soon.
I’ll bring items to pass out to lab tomorrow
  For stuff I’ve got on hand already

## Slide 3: Today’s Goals
Discuss additional wired communication protocols: SPI and I2C
Understand tradeoffs in design
  UART, SPI, and I2C are each useful for different scenarios
Explore real-world usage of SPI and I2C

## Slide 4: Outline
SPI
I2C
Using SPI and I2C

## Slide 5: UART Pros and Cons
Pros
  Only uses two wires
  No clock signal is necessary
  Can do error detection with parity bit
Cons
  Data frame is limited to 8 bits (20% signaling overhead)
  Doesn’t support multiple device interactions (point-to-point only)
  Relatively slow to ensure proper reception
Let’s get rid of all the cons (by sacrificing on all the pros)

## Slide 6: Synchronous UART
USART
  Synchronous/Asynchronous
  Just add a clock line
Common peripheral in many microcontrollers to allow adaptable communication
  Could build various protocols (like SPI or UART) on top of it
Still point-to-point limited in this form
DATA
CLK
Transmitter
Receiver
b0
b1
b2
b3
b4
b5
b7
b6

## Slide 7: Synchronous serial communication with a single device
Microcontroller
Data Out Clock
Device 2
Device 1
Device 3
Data In Clock

## Slide 8: Want bi-directional communication, so three wires
Microcontroller
Data Out Data In Clock
Device 2
Device 1
Device 3
Data In Data Out Clock

## Slide 9: Wire signals to all devices to form a bus
Microcontroller
Data Out Data In Clock
Data In Data Out Clock
Device 2
Device 1
Device 3
Data In Data Out Clock
Data In Data Out Clock

## Slide 10: Communicating on a bus
How do you distinguish which device you are talking to?
GPIO pin for each device
  Signal which device is being communicated with
  Only activates communication on transition of “select” line
  Needs a separate pin for each device
Address for each device
  Devices must always listen and then discard messages that aren’t for them
  Need to define packet format so it’s clear where the address is
  Need a method for addressing devices

## Slide 11: Separate chip select line for each device
Microcontroller
Data Out Data In Clock
(2) Chip Select
Chip Select
  (3) Chip Select
Device 2
Device 1
Device 3
Data In Data Out Clock
Chip Select
Data In Data Out Clock
Chip Select
Data In Data Out Clock
Chip Select

## Slide 12: Serial Peripheral Interface (SPI)
Serial, synchronous, bus communication protocol
Single controller with multiple peripherals
  Within a circuit board
High-speed communication
  Multiple Mbps
Microcontroller
Serial Data Out Serial Data In Serial Clock
Device 2
Device 1
Device 3
Serial Data In Serial Data Out Serial Clock
Serial Data In Serial Data Out Serial Clock
Serial Data In Serial Data Out Serial Clock

## Slide 13: A note on outdated notation
Master/Slave paradigm
  Master is the “Computer” and is in charge of interaction
  Slave is the “Device” and has little control over interaction parameters
  Really common notation in EE side of the world.
    Not intended to be harmful, but also literally inconsiderate.
Field is changing for the better. It’s going to take some time.
  Controller/Peripheral
  Central/Peripheral
  Device/Peripheral
  Master/Minion
  Primary/Secondary

## Slide 14: SPI naming schemes
Historical SPI Naming
  MISO – Master In Slave Out
  MOSI – Master Out Slave In
  SS – Slave Select
Revised SPI Naming
  SDI – Serial Data In -> also known as CIPO (Controller In, Peripheral Out)
  SDO – Serial Data Out -> also known as COPI (Controller Out, Peripheral In)
  CS – Chip Select
https://www.oshwa.org/a-resolution-to-redefine-spi-signal-names
https://www.sparkfun.com/spi_signal_names

## Slide 15: SPI wiring
3+N wires for N peripherals
SDI – input to the chip
SDO – output from the chip
SCK – Serial ClocK
CS –
  Active low signal
Names are always relative to this particular chip
  SDO connects to SDI
  SDI connects to SDO
Microcontroller
SDO SDI SCK
Device 2
Device 1
Device 3
SDI SDO SCK
SDI SDO SCK
SDI SDO SCK

## Slide 16: SPI timing diagram
CS goes low to start transaction and high to end
Data is sent synchronously with clock signals
Capable of full-duplex transfers
  Both directions at the same time
SCK
SDO
SDI

## Slide 17: SPI communication
Transactions usually in multiples of bytes (as many as needed)
Either bit endianness is possible
  nRF can do LSb first OR MSb first
No need for framing bits (start/stop)
  CS handles that

## Slide 18: SPI configurations
CPOL – is the clock default low or default high
CPHA – is data read on first edge or second edge
Peripherals tell you what their configuration is

## Slide 20: SPI data rate
No particular requirements
  Speed can go as fast as your clock and line capacitance can handle
Datasheet for devices will specify their speeds
  Sort of standards (less so than UART, for example)
    700 kbps
    3.4 Mbps
    10 Mbps

## Slide 21: Daisy-chaining SPI
SPI can also be formed into a ring bus
Doesn’t save on pins, but does reduce wires…
  At the cost of reliability and speed
Fairly rare in practice

## Slide 22: How do we determine when peripheral has information?
Controller starts/stops SPI transfers
  Could ask peripheral periodically
Peripherals often add interrupt outputs to signal controller that an event has occurred
  More pins, yay!

## Slide 23: Use Cases
High-speed peripherals
  Microphone, External ADC, Displays!
External memory
  Memory chips
  SD cards
    All SD cards support a SPI communication mode
  QSPI – Quad SPI (four SDO lines for more throughput)
    Often used for communication with external memory

## Slide 24: SPI Pros and Cons
Pros
  Faster throughput (and no overhead)
  No restrictions on data frame
    No addressing requirements or word size assumptions
  Full duplex transfers
Cons
  Many pins: 3+N (for N peripherals)
    CS line scales linearly (other signals are a bus)
  Controller must initiate all transfers
    Not designed for multi-controller scenarios

## Slide 25: Break + relevant xkcd
https://xkcd.com/927/

## Slide 26: Outline
SPI
I2C
Using SPI and I2C

## Slide 27: Choosing different tradeoffs from other wired communication
Things we like from SPI
  Communication over a bus
  Synchronous communication
Things we want from new protocol
  Fewer I/O pins
    Use a single data line for bi-directional communication
    Needs addressing and more specified data frame
  Multiple controllers sharing the bus
    Needs a bus contention solution

## Slide 28: Bus contention could short a shared bus
Want to enable multiple controllers
Problem
  What if they each try to transmit different data?
  At some point, there will be a short-circuit

## Slide 29: Disconnected I/O pins enable shared communication
I/O pins often have three states
  High
  Low
  Disconnected (also known as High-Impedance/High-Z)
We can use this third state to enable communication over a shared line
  Low or Disconnected
  Wired-AND
    1 if they are all disconnected
    0 if any are low
ANDing

## Slide 30: Inter-Integrated Circuit (I2C)
Two-wire, synchronous, bus communication
  Ubiquitous in the embedded world
  De-facto standard for sensors
Invented and patented by Phillips (now NXP)
  Patent expired in 2004
Also known as Two-Wire Interface (TWI)
  Occasionally as System Management Bus (SMBus or SMB) but that’s actually a related but separate thing

## Slide 31: I2C overview
SDA – Serial Data
SCL – Serial Clock
  Usually 100 kHz or 400 kHz
Communication is a shared bus between all controller(s) and peripheral(s)
Pull-up resistors for open-drain communication

## Slide 32: Open drain bus communication
SDA and SCL are open-drain
  1 – high-impedance, let line float high
  0 – active drive, pull line low
Pull-up resistor to provide high signal
  Low enough resistance that current can flow in a reasonable amount of time
  Common value: 4.7 kΩ

## Slide 33: I2C transactions
Default
  Both lines float high (pull-up resistor)
Start condition
  Drive SDA low while SCL is still high

## Slide 34: I2C transactions
First byte is chip address + R/W indication
  Address: 7-bit value that needs to be different for each participant
  R/W: 1 for read, 0 for write
Values are sent MSb first (reverse of other protocols 😱)

## Slide 35: I2C transactions
Acknowledgement from peripheral follows each byte
  Controller lets line float high
  Peripheral drives line low to signal receipt of message

## Slide 36: I2C transactions
Data frame(s) follow
  Sent as entire bytes, plus and ACK
  As many as needed before Stop condition
Stop condition
  SDA goes high while SCL is high (normally data only changes when clock is low)

## Slide 37: Bus arbitration
Arbitration decides which controller gets to proceed if multiple try to communicate simultaneously
What happens in I2C if one controller wants a low bit and the other wants a high bit?

## Slide 38: Bus arbitration
Arbitration decides which controller gets to proceed if multiple try to communicate simultaneously
What happens in I2C if one controller wants a low bit and the other wants a high bit?
  Low bit wins! (so smaller address or data)
Each controller constantly checks whether SDA matches the voltage level it expects
  Stops attempting to transmit if it ever does not
  (Only actually needs to check high signals)

## Slide 39: Repeated start conditions
Repeated start conditions allow the bus to be used again while arbitration was won
Trigger another Start condition without triggering Stop condition
  Send address again
Frequently used for write then read pattern
  Write which value you want
  Then repeated start and read

## Slide 40: Clock stretching
Clock is an open-drain line too
  Either device could keep it low
Transaction can be briefly paused by holding SCL low
ready

## Slide 41: Real-world I2C transactions

## Slide 42: Each I2C device on a bus must have a different address
Shared addresses would cause both to respond
ICs often have one or more address pin(s) used to select bit(s) of address
  0 pins: only one may be on bus
  1 pin: two may be on bus
  2 pins: four may be on bus
If no address pins (or not enough), need an I2C address translator chip
  Translates addresses for one or more peripheral chips
A0 is low: address 1001010x
A0 is high: address 1001011x

## Slide 43: Sparkfun Qwiic connect system
System for wiring multiple prototyping boards together
Four-pin connector
  VCC (3.3 volts)
  Ground
  SDA
  SCL
Daisy-chains through boards
  Actually connects to chips in parallel as a bus
https://www.sparkfun.com/qwiic

## Slide 44: System Management Bus (SMBus)
Related communication specification
  A little more strict in places, but generally interoperable
Adds ability to broadcast or unicast messages
  Generic addresses for Controller and various peripherals (Battery)
Adds an open-drain shared interrupt signal
  High-impedance or pull low, just like SDA and SCL
  Allows any device to alert a controller
    Controller has to probe bus to determine which device wants attention

## Slide 45: I2C use cases
Various sensors
  Usually low to medium speed
  Even relatively high speed stuff often has I2C for convenience
    Accelerometers and microphones
    Often with intelligent filtering built in
Communication between microcontrollers
  Either can act as the Controller when necessary
Commonly exists internally within smartphones and laptops too
  Light sensors, Temperature sensors, etc.

## Slide 46: I2C Pros and Cons
Pros
  Wiring is simple
  Only uses two pins
  Very widely supported
Cons
  Relatively slow communication rate
  Speed versus power use tradeoff (due to pull-down resistor)
  Open collector makes debugging difficult

## Slide 47: Break + Open Question
Why are SPI and I2C common internally in embedded systems, but not common externally? (like USB, Ethernet, HDMI, etc.)

## Slide 48: Break + Open Question
Why are SPI and I2C common internally in embedded systems, but not common externally? (like USB, Ethernet, HDMI, etc.)
  Too slow:
    Especially I2C (100 Kbps compared to 12 Mbps for slowest USB)
  Not robust:
    No effort put into the electrical encoding of data or error checking
    Long external cables lead to additional errors
  Overall: they’re too simple

## Slide 49: Outline
SPI
I2C
Using SPI and I2C

## Slide 50: Common sensor interaction pattern
First write one byte to the device
  This selects what data you want to interact with, called a “register address”
Second read/write one (or more) bytes
  This is the actual data
SPI and I2C devices both work this way
  Datasheet will have a list of registers you can read/write
  Each register will have some address: that’s the first byte you write

## Slide 51: Example: Microbit accelerometer
Details of each register on later pages show you the structure of the data read or written

## Slide 52: Register/data pattern in I2C
I2C is the more difficult of these
  Need some way to tell the device “this transaction is still going”, but switch from writing to reading
This is the use of the “repeated start” option
  Continues the “transaction”

## Slide 53: I2C Read Transaction
First, write the address of the register you want
Then, repeated start
Finally, read the data from the device
Peripheral Controls SDA Line
Controller Controls SDA Line

## Slide 54: I2C Write Transaction
Just write the data. No need to change modes in the middle
Some devices also allow “repeated start” in the middle of write transactions
  But it’s not necessary
Peripheral Controls SDA Line
Controller Controls SDA Line

## Slide 55: nRF I2C Implementation
nrf_twi_mngr driver: I2C (Two-Wire Interface) manager
  Expects transactions to occur and is set up to run those
Takes in an array of “transfer” operations as an argument
Each operation is either a read or a write
  Includes a device address, includes a pointer to data and length
  Includes flags like NRF_TWI_MNGR_NO_STOP which does not execute a stop bit (and instead does a repeated start for the next operation)
Your job is to set up the array of transfer operations
  Then the driver will make it happen

## Slide 56: Register/data pattern in SPI
SPI is easier to implement transactions for
  No indication of reading/writing by default
  You can just hold Chip Select low and stop clocking if you want to pause
Need some way to indicate to the peripheral whether you’re reading or writing though
  Possibly different register addresses for read versus write
  Possibly 7-bit addresses, with a bit leftover for read/write specification

## Slide 57: SPI Read Transaction
Chip select goes low to select the device
First byte is the register address and read/write selection
Next bytes are the data to write
SDO
SDI

## Slide 58: SPI Write Transaction
Chip select goes low to select the device
First byte is the register address and read/write selection
Next bytes are the data to write
SDO

## Slide 59: nRF SPI Implementation
nrfx_spim driver: nRF SPI Master (Controller)
Expects data in “XFER” (transfer) operations
  Can either be read, write, or read AND write (both simultaneously)
Flags control whether CS pin goes high afterwards or if it stays low
  Or you could just manually control the CS pin

## Slide 60: Outline
SPI
I2C
Using SPI and I2C