## Slide 1: Lecture 05 Digital Circuits
CE346 – Microprocessor System Design
Branden Ghena – Fall 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Labs
  Debrief: How did that go?
    Can use personal computers if preferred
  See schedule of Lab hours available on Canvas
Quiz
  Today at end of class

## Slide 3: Project Proposals
It is time to start forming teams and working on Proposals
  Due next week Tuesday!
  Project details are posted to Campuswire
  Specific proposal details are on the Canvas assignment

## Slide 4: Today’s Goals
Explore a final interaction pattern: DMA
Understand the basics of digital circuitry
  Enough to be able to interact with the Microbit
Finish our exploration of the GPIO peripherals on the Microbit
One step deeper in to EE-land: energy use

## Slide 5: Outline
DMA
Digital Circuits
GPIOTE
Energy

## Slide 6: Reminder: Polling I/O
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
This is the “polling” model of I/O.
“Poll” the peripheral in software repeatedly to see if it’s ready yet.

## Slide 7: Reminder: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code
Continue original code

## Slide 8: Direct Memory Access (DMA)
Even with interrupts, providing data to the peripheral is time consuming
  Need to be interrupted every byte, to copy the next byte over
DMA is an alternative method that uses hardware to do the memory transfers for the processor
  Software writes address of the data and the size to the peripheral
  Peripheral reads data directly from memory
  Processor can go do other things while read/write is occurring

## Slide 9: General-purpose DMA

## Slide 10: Special-purpose DMA
nRF52 uses “EasyDMA”, which is built into individual peripherals
  Only capable of transferring data in/out of that peripheral
  Easier to set up and use in practice
  Only available on some peripherals though (no DMA for TEMP)
Warning: addresses for DMA MUST be in RAM!

## Slide 11: Full peripheral interaction pattern
Configure the peripheral
Enable peripheral interrupts
Set up peripheral DMA transfer
Start peripheral
Continue on to other code
Interrupt occurs, signaling DMA transfer complete
Set up next DMA transfer
Continue on to other code, and repeat

## Slide 12: Outline
DMA
Digital Circuits
GPIOTE
Energy

## Slide 13: Digital signals
Exist in two states:
  High (a.k.a. Set, a.k.a. 1)
  Low (a.k.a. Clear, a.k.a. 0)
Simpler to interact with
  Constrained to two voltages
  With quick transitions between the two
  No math for voltage level
    Either high or low

## Slide 14: Digital signals map to voltage ranges
Upper range is high signal
  ~0.7*VDD
Bottom range is low signal
  ~0.3*VDD
Middle is undefined
  Only exists during transitions
http://www.sharetechnote.com/html/Electronics_CMOS.html

## Slide 15: Digital circuits
Connecting components together with digital signals
  Mostly ICs
  Also buttons/switches and LEDs
Way simpler than analog circuits
  Mostly connecting boxes with wires
  Plus a few resistors here and there
An abstraction
  Not sufficient for fully understanding electronics behavior, but close

## Slide 16: Switches
Single Pole, Double Throw switch
  Middle pin (Pole) connects to one of two outer pins (Throws)
For controlling microcontrollers
  Often connect outer pins to VCC and Ground respectively
  Input then goes High or Low depending on switch state
https://learn.sparkfun.com/tutorials/button-and-switch-basics/

## Slide 17: Buttons
Single Pole, Single Throw switch
  Pole pin either connects to Throw pin or is disconnected
  Come in normally-closed (connected) and normally-open (disconnected)

## Slide 18: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?

## Slide 19: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?
  Floating! Could be any voltage
  Solution: connect weakly to either high or low voltage

## Slide 20: Current flows through the “path of least resistance”
Simplification
  Works well for the types of circuits we use
Pull-up resistor
  When button is open (disconnected), the only path is through the resistor
  When button is closed (connected) the least resistance path is through the button to Ground

## Slide 21: Pull-up resistors and pull-down resistors
Resistor sets the “default” value of a wire
  Pull-up connects to VCC
  Pull-down connects to Ground
  Usually 10-100 kΩ
When button is open (disconnected)
  Connection through the resistor sets signal
When button is closed (connected)
  Signal is directly connected to a voltage source
  Much lower resistance means that signal dominates

## Slide 22: Buttons on the Microbit
Normally open buttons
  Disconnected by default
Active low signal
  Activating (pushing) button creates a low signal
Pull-up resistors
  Set button signal high by default

## Slide 23: LEDs
Light Emitting Diodes
  Generate light as current passes through them
  Various colors available
Diodes
  Only allow current to go through one way
  Not particularly relevant for LEDs
    Treat as a digital component
Connect anode to high voltage and cathode to ground
  Plus a resistor to limit the total amount of current
https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds

## Slide 24: Active state for LEDs
LEDs can be active high or active low depending on configuration
  Active high is how people assume they work
  Active low is often used instead
    GPIO pins can usually sink more current than they can source

## Slide 25: LEDs on the Microbit
Microphone LED
  Active high
Simple to use
Ignore this other part for now

## Slide 26: LEDs on the Microbit
Use two GPIO pins to control each LED
  Row high as VDD
  Column low as Ground
Remember, connections only exist where there are dots

## Slide 27: Controlling the LED matrix
Cannot individually control all LEDs simultaneously
  Need to light one row at a time
  Iterate rows quickly to make them appear on all the time
We’ll have a lab on these later
  Combine GPIO and timers

## Slide 28: Break + Question
Should the spot in green have?
  Pull-up Resistor
  Pull-down Resistor
  Either
  Neither

## Slide 29: Break + Question
Should the spot in green have?
  Pull-up Resistor
  Pull-down Resistor (needs to pull input low by default)
  Either
  Neither

## Slide 30: Outline
DMA
Digital Circuits
GPIOTE
Energy

## Slide 31: Handling interrupts from GPIO
Separate peripheral, GPIOTE (GPIO Task/Event)
  Manages up to 8 individual pins
    Can read inputs and trigger interrupts
    Can also connect outputs from events on other peripherals (PPI)
  Can trigger interrupts for a “Port event” as well
    Software checks which pin(s) caused the event to occur
    Very low power operation (works with system clocks off)
Unclear why this is a separate peripheral
  Presumably too complicated/expensive to have 42 of them

## Slide 32: Configuring individual input interrupts
Pick an available GPIOTE channel (0-7)
Configure it
  Port and Pin number
  Task (output), Event (input), or Disabled
  Polarity for input events
    Low-to-high
    High-to-low
    Toggle (both directions)
Enable interrupts for channel in GPIOTE (and in NVIC!)
Clear event in interrupt handler
  Doesn’t happen automatically

## Slide 33: Sensing port events
Uses the “Detect” signal. Generated from pin Sense configuration

## Slide 34: Configuring port input interrupts
Configure the Sense for each pin
  High or Low
  Allows different pins to have different “active” states
Select detect mode
  Direct connection to pins
  Latched version (saved even if pin later changes back)
Enable interrupts for port in GPIOTE (and in NVIC!)
Clear event in interrupt handler and value in Latch register
  Doesn’t happen automatically

## Slide 35: Outline
DMA
Digital Circuits
GPIOTE
Energy

## Slide 36: Ohm’s Law
  V = I x R
Volts = Current times Resistance
  P = I x V
Power = Current times Voltage
These two equations govern most of the circuit math we’ll need in this course
  Work with resistive circuits

## Slide 37: Thinking about energy
Batteries often list energy in mA*h (milliamp – hours)
  Coin cell battery: 3v at 220 mAh
  2x AA battery: 3v at 2000 mAh
  iPhone 11 battery: 3.7v at 3000 mAh
nRF52833 active current: 5.6 mA (at 3v)
  Coin cell: 40 hours -> ~2 days
  2x AA: 360 hours -> ~15 days
  iPhone 11: 535 hours -> ~22 days
So how does any of this work???

## Slide 38: Microcontroller sleep modes
Sleep mode
  Processor stops running
  Most peripherals are disabled
  Continues until an interrupt occurs and wakes the microcontroller
    Usually a timer or GPIO input
nRF52833 sleep mode current: 1.8 μA (GPIO port event only)
  Coin cell: 122222 hours -> ~5000 days -> ~14 years
Low-power systems shoot for less than 1% duty cycle
  Average current of ~100 μA or less
  Warning: other stuff on the board counts!!
    LEDs are 1-10 mA each… Power is not a concern of the Microbit

## Slide 39: Outline
DMA
Digital Circuits
GPIOTE
Energy