## Slide 1: Lecture 07 Driver Design
CE346 – Microprocessor System Design
Branden Ghena – Fall 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administriva
Project Proposals due today!
  A few are in so far and they look great and I’m super excited!!!!!

## Slide 3: Today’s Goals
Finish up Timer-like peripherals
Explore another aspect of device driver design
  Non-blocking vs Blocking interfaces
Discuss how interrupts interact with these
  Event-loop as a partial alternative

## Slide 4: Outline
Real-time Counter
Watchdog Timer
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 5: Real-time Counter
Low-power (32 kHz) version of Timer
  Only a 24-bit internal Counter
Note: abbreviated RTC, but that already means something else (Real-Time Clock)

## Slide 6: Differences between Real-Time Counter and Timer
Runs off of LFCLK instead of HFCLK
  With smaller prescaler value (4096 vs 32768)
24-bit counter vs 32-bit counter for Timer
Can read the Counter value directly
  No need for Capture task
Otherwise extremely similar. Just a low-power version of Timer

## Slide 7: Time resolution for Real-Time Counter
𝑓TIMER =
Resolution
  Minimum: 30.517 μs, overflows in 512 seconds (24-bit Counter)
  Maximum: 125 ms, overflows in 582 hours
Not as precise as the Timer (62.5 ns best precision)
  Possible design: use both
    Real-Time Counter for most of the waiting
    Chained into Timer for precise remaining amount of time

## Slide 8: Outline
Real-time Counter
Watchdog Timer
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 9: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
  Why?

## Slide 10: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
  Why?
  Resets “state” to original values, which are likely good
    Startup is often well-tested
    It’s long-running code interacting in unexpected ways that leaves systems in a broken state

## Slide 11: Watchdog timer (WDT)
Focused on failures where the system “hangs” forever
  Maybe software, maybe hardware!
Can’t know for certain the system is hung, but can know practically
  Select a timeout that is the maximum amount of time you expect the system to ever go without looping in main()
  Multiply it by 2-10
  Set a watchdog timer to that value
If watchdog timer ever expires, it resets the system (in hardware)

## Slide 12: Watchdog configuration
timeout (seconds) =
Configure watchdog
  Can choose whether to count down during Sleep mode or Debug mode
Set a Counter Reload Value (CRV, 32-bits)
Start the watchdog timer
  Loads internal Counter to CRV value
  Starts counting down at 32 kHz

## Slide 13: Running applications with a watchdog timer
Need to periodically reset the watchdog to keep it from expiring
  Known as “feeding” the watchdog or “kicking” the watchdog
Reload Request register
  Must write sequence 0x6E524635 to reload watchdog
  Incredibly unlikely to happen by accident
While running, watchdog is protected from modification
  Configure once, run forever (at least until a reboot)
  Only option is to make periodic Reload Requests
Default off on the nRF52833

## Slide 14: Break + Open Question
MSP430 microcontrollers start with the watchdog on by default
What are the pros and cons of this choice?

## Slide 15: Outline
Real-time Counter
Watchdog Timer
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 16: Callback functions
timer_start(duration, my_timer_handler, context);
Driver interfaces often provide a callback mechanism
  Caller provides a function which should be executed when complete
“Context” is often provided as well (void*)
  Ability for caller to pass an argument for the callback function
  Often a pointer to a position in a structure or a shared variable to modify

## Slide 17: Function pointers in C
Harder than in Javascript or C++. Can’t define anonymous function inline
  Instead create a pointer to an existing function in your code
void myfun (int a) {
// do something here
}
void main() {
void (*fun_ptr)(int) = &myfun;
fun_ptr(10); // dereference happens automatically
}

## Slide 18: Callbacks usually run in an interrupt mode
If the interrupt handler calls the callback, the callback will be within that same interrupt mode
Be careful which variables you modify!!
  Same concurrency problems mentioned before
Starts to get pretty annoying
  Embedded systems deal with concurrency issues just like OS

## Slide 19: Blocking function calls
Alternative option: blocking calls
  Do not return until request is complete
void myfun (void* context) {
*(boolean*)context = true; // context is the flag pointer
}
void timer_start_blocking(duration) {
boolean flag = false;
// duration, pointer, context
timer_start(duration, &myfun, &flag);
while (!flag) { }
}

## Slide 20: Temp driver example
nu-microbit-base/software/apps/temp_driver/

## Slide 21: Outline
Real-time Counter
Watchdog Timer
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 22: Interrupts are frustrating
We do not want to block on every call
We also do not want to deal with concurrency issues
Alternative: one main event loop
  Polls necessary sensors
  Iterates through state machine and determine actions
  Runs at a certain frequency

## Slide 23: Event loop
Rather than polling a single driver, poll all of them
  Each time through the loop check all relevant inputs
  Respond to events that are necessary
  Sleep until ready to start again
    while (1) {
    time start = get_time();
    boolean result = check_timer();
    if (result) { check_gps(); }
    adjust_throttle();
    sleep(1ms – (get_time() – start));
    }

## Slide 24: Top-half / Bottom-half handler design
Top half
  Implements interface that higher layers require
  Performs logic to start device requests
  Wait for I/O to be completed
    Synchronously (blocking) or asynchronously (return to event loop)
  Handle responses from the device when complete
Bottom half
  Interrupt handler
    Continues next transaction
    Or signals for top half to continue (often with shared variable)

## Slide 25: Temperature event-loop example
nu-microbit-base/software/apps/temp_event_loop/

## Slide 26: Outline
Real-time Counter
Watchdog Timer
Driver Interfaces (Blocking and Non-Blocking)
Event Loop