## Slide 1: Lecture 14 USB & CAN
CE346 – Microprocessor System Design
Branden Ghena – Fall 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administriva
Hardware handout at the end of class today
  I’ve got a bunch of hardware!
Every group can also take one microbit from CG50
  And a USB cable
  If you need two, please speak with me about it first

## Slide 3: Administrivia
Lecture schedule for the rest of the quarter
  Thursday (11/11) – Wireless Communication
  Tuesday (11/16) – Nonvolatile Memory
    Also the final quiz
  Thursday (11/18) – Sensing Systems Research Talk
    Colleen Josephson, Room TBD
  Tuesday (11/23) – No Class
    Tuesday before Thanksgiving
  Tuesday (11/30) – Wrapup Lecture

## Slide 4: Today’s Goals
Discuss more advanced wired communication protocols
  With a little less detail
  Just give a taste of what they are like
Think about higher-layer concerns like data routing, interpretation, and reliability

## Slide 5: Outline
USB
CAN

## Slide 6: USB references
USB in a NutShell
  https://www.beyondlogic.org/usbnutshell
Other stuff I found useful
  https://www.usbmadesimple.co.uk/
  http://kofa.mmto.arizona.edu/stm32all/blue_pill/usb/an57294.pdf
  https://en.wikipedia.org/wiki/USB

## Slide 7: Universal Serial Bus (USB)
Pervasive wired communication protocol
  Universal accurately applies!
  Targets predominantly external devices over a plug/cable
Good combination of simple and capable
  Base version for simple devices does not require too much in terms of pins or resources
  More complex versions can transfer a significant amount of data
    These grew organically over time though
Great support for interoperability
  Generic device profiles that allowed for plug-and-play
  Supported by OS initiatives to include driver software

## Slide 8: USB is a layered protocol
USB protocol describes how to:
  Electrically send bits
  Send frames of multiple bytes
  Communicate data between two devices
  Communicate specific application data (through device classes)
Much larger compared to others
  SPI: only how to electrically send bits
  UART and I2C: how to send frames of bytes

## Slide 9: Roles and topology
Hosts and Devices
  USB On-The-Go allows host negotiation
    Added later. Support devices like smartphones
Host is in charge of communication (“Upstream”)
Devices provide various capabilities Host can interact with (“Downstream”)
Tiered star topology
  Host connects to hubs, which connect to devices
  Up to 127 devices per hub. Up to 5 layers of hubs

## Slide 10: USB signals
Four signals
  Vbus (5 volts, can power devices)
  D+
  D-
  Ground
D+/D- are a differential pair
  Signals are inverses of each other
    Usually, occasionally act separately to signal special conditions
    Increases voltage difference between states (5 - -5 = 10 volts)
  Wires are twisted to avoid interference

## Slide 11: Synchronizing data
No clock signal!! How is USB so fast?
  Partially EE magics: better receivers, matched wire impedance
  Partially easier to distinguish signal states
  Also guaranteed transitions, which allow resynchronization
Transitions are used to denote data (non-return-to-zero inverted)
  With guaranteed transition in within every 8 bits (bit stuffing)
  Allows clocks on the two devices to synchronize

## Slide 12: USB speeds
USB 1.0
  Low Speed: 1.5 Mbps
    Not clear if this is used anymore
  Full Speed: 12 Mbps
    Microcontrollers tend to support Full Speed
    We’re focusing on details from it
USB 2.0
  High Speed: 480 Mbps
USB 3.0+
  Super Speed: 5-20 Gbps
  Adds multiple parallel data connections
Pull-up resistors allow for detection of a plugged device
Also identify speed

## Slide 13: USB data frames
General packet format
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Token, setup Device or read/write data from/to Device
    Data, application data
    Handshake, acknowledgement (or explicit NAK)
  Address+Endpoint, for Token packets to identify Device
  Data, up to 1023 bytes (full speed, often capped at 64 for microcontrollers)
  CRC, (Cyclical Redundancy Check) to detect bit errors
  End-of-packet

## Slide 14: USB transactions
All transmissions are initiated by the Host, which can periodically request reading from a Device if desired
Reading data from Device
Writing data to Device

## Slide 15: Interacting with USB devices
Each Device is given a separate address on the bus
Each Device also has a number of Endpoints
  Logical communication channels
  Direct data and guide communication patterns

## Slide 16: USB endpoint types
Interrupt transfers
  Guaranteed latency, small amounts of data
  Important sensor data (mice and keyboards)
  Polled frequently by Host
Bulk transfers
  Sporadic large transfers, reliable communication
  General reading/writing of data (flash drives and USB serial)
  Polled by Host whenever there is available bandwidth
Isochronous transfers
  Guaranteed data rate, unreliable communication
  Continuous data streaming (audio and webcams)
  Polled frequently by host

## Slide 17: USB control endpoint
Every USB Device has a special Control endpoint as well
Used for setting up the USB Device driver on the Host
Initializing a Device
  Host sends SETUP transaction requesting device descriptor
  Host performs IN transaction to read device descriptor
  Host performs OUT transaction to write device status

## Slide 18: USB device descriptors
Packed version of tree structure describing the device
  Interfaces it provides
  Endpoints associated with each interface

## Slide 19: Example Microbit
Interface: Communications, Abstract (modem), CDC
  Endpoint: 3, IN, Interrupt
Interface: CDC Data, CDC DATA interface
  Endpoint: 1, IN, Bulk
  Endpoint: 2, OUT, Bulk
Interface: Vendor Specific Class, Subclass, Protocol
  Endpoint: 5, IN, Bulk
  Endpoint: 4, OUT, Bulk
Interface: Mass Storage, SCSI, MSD interface
  Endpoint: 7, IN, Bulk
  Endpoint: 6, OUT, Bulk
SEGGER JTAG interface
Virtual serial device
USB external filesystem

## Slide 20: Minimal virtual serial USB Device
Virtual Serial Device
  Endpoint 0: Control, IN/OUT
    Respond to IN requests by setting up OUT with a buffer of descriptor data of the correct size
  Endpoint 1: Interrupt, IN
    Needed for serial modem controls, just ignore it
  Endpoint 2: Bulk, OUT
    Connect to buffer from _write() (just takes raw characters)
  Endpoint 3: Bulk, IN
    Connect buffer to _read() (just provides raw characters)

## Slide 21: HID USB Device (Human Interface Device)
Used for human interaction devices, like keyboard/mouse
“Report” structure is provided over Interrupt IN endpoint
  Or on demand via Control IN endpoint
Example mouse with x,y and three buttons

## Slide 22: USB summary
Specification for fast data communication
Specification for interacting with abstract device types
  Connects correct driver to interpret and send data
Pros
  Very fast
  Very interoperable
Cons
  Hardware and software are way more complex than simple protocols like UART, SPI, and I2C
  Not very energy efficient

## Slide 23: nRF52 USBD
Implements USB Device (not Host)
  Control endpoint
  14 bulk/interrupt (7 IN, 7 OUT)
    64-byte transfers
  2 isochronous (1 IN, 1 OUT)
    1023-byte transfers
Full-speed USB
  With 5 volt signals

## Slide 24: Outline
USB
CAN

## Slide 25: Controller Area Network (CAN bus)
Designed for highly reliable interactions within a vehicle
Multi-master with arbitration
  Similar to I2C
Mechanism for sending messages with “identifiers”
  Identifies the data in the message, not the device its for
  Lower value identifiers have high priority
  All messages are received by all CAN nodes
    Which can decide at higher levels which identifiers they care about

## Slide 26: CAN physical connections
Two differential, wired-AND signal lines
  Transitions are used to transmit bits (non-return-to-zero) with bit-stuffing
  Combines aspects of USB and I2C
  125 kHz – 5 Mbps speeds

## Slide 27: CAN packet format
11-bit identifier
  Check bits as they are sent to see if you win arbitration
Up to 8 bytes (64 bits) of data
CRC for checking
Acknowledgement
  Like I2C, let the line float and see if another device responds
  If not, explicitly retransmit!

## Slide 28: CAN message types
Data frame
  Transmission of data for a certain identifier
Remote frame
  Requests data transmission of a certain identifier
Error frame
  Transmitted when an error is detected with the previous message
Overload frame
  Transmitted by a node that is too busy to respond right now

## Slide 29: CAN reliability design – detecting errors
Check for errors everywhere and appropriately handle
  Bit error
    If the value found on the bus differs from the one sent
  Stuff error
    If 6 consecutive bits of the same type are found
  CRC error
    If CRC does not match
  Form error
    Format field has unexpected values
  Acknowledgement error
    No ACK received
Devices detecting an error broadcast a message signifying it!
  Multiple devices sending the same message works without arbitration loss
  Previous message is then retransmitted

## Slide 30: CAN reliability design – handling errors
Each node accepts the possibility that maybe it is the faulty one
Track errors and successes and change device state
  Passive: limited error signaling and transmissions
  Bus off: does not transmit in any way
Idea is that the CAN controller hardware can be faulty but still detect it in some cases

## Slide 31: CAN summary
Designed for reliable vehicular communication
Multi-master bus with serial communication
Pros
  Highly reliable
  Extensible to many devices
Cons
  Special-purpose design. Whole system has to agree on identifiers
  Relatively slower throughput

## Slide 32: Outline
USB
CAN