## Slide 1: Lecture 18 Wrapup
CE346 – Microprocessor System Design
Branden Ghena – Fall 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
This is the last lecture!! 😭
  No class on Thursday
  I can schedule meetings with groups if needed
Project Demos - Next week Tuesday
  Tuesday 12/7
  Mudd 3514
  2:00-5:00 pm

## Slide 3: Today’s Goals
Discuss remaining parts of the Microbit and nRF52833
  Realize that we’ve covered almost everything on the system!!
Explore sensing systems research

## Slide 4: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 5: Microbit
Used almost all of this!
Remaining:
  Batteries
  Wireless
  KL27Z I2C

## Slide 6: Internal Microbit connections

## Slide 7: KL27 I2C Interface
Device information
  Version of board and JTAG firmware
  Power state of board
    USB, Battery, both
    Voltage values for battery and VIN
  USB connection state
  Disable the power LED!!
Flash Storage
  128 kB of the KL27’s Flash is readable/writable over I2C

## Slide 8: Outline
What haven’t we talked about?
  Microbit
  nRF52833
    Task/Event Chaining with PPI
Sensing Systems Research

## Slide 9: Software stops when the processor does, but peripherals continue
Solution to low power: keep the processor off
Problem: when the processor is off, no code is running
Solutions
  Peripherals can wake it up again
    Can probably go for milliseconds to minutes without any actions
    Timer interrupt can wake processor to do things
  Have hardware handle some parts in the background without the processor’s involvement
    DMA
    PPI

## Slide 10: Controlling peripherals while processor sleeps
DMA (Direct Memory Access)
  Set up a pointer to memory and a length
  Peripheral can load/store memory without processor’s involvement
  Usually use completion interrupt to wake processor
PPI (Programmable Peripheral Interconnect)
  Any Event can be tied to any Task within the nRF52
  Allows for complicated actions to be chained together

## Slide 11: nRF52 Tasks and Events
Tasks are used to perform some operation
  Often written to by software
Events change value when some change in status occurs
  Often used to trigger interrupts
PPI peripheral can connect any TASK to any EVENT
Example: Timer peripheral

## Slide 12: nRF52 PPI peripheral
Connects Events to Tasks via hardware
Each channel gets one Event pointer and up to two Task pointers
  Must point to Event/Task registers

## Slide 13: Example PPI use case
Automatic high-speed ADC sampling
Software configures and sleeps
  ADC (buffer and enable)
  Timer (prescaler, compare value, short from compare to clear, and start)
PPI: When Timer fires (EVENTS_COMPARE[0]),
  Sample ADC (TASKS_SAMPLE)
PPI: When ADC buffer full (EVENTS_END),
  Stop Timer (TASKS_STOP)
  Fork: wake processor (via software interrupt from EGU)

## Slide 14: Outline
What haven’t we talked about?
  Microbit
  nRF52833
    Peripheral overview
Sensing Systems Research

## Slide 15: nRF52833 Peripherals
Tour of the nRF52833 peripherals
With some details on the ones we haven’t talked about
  Wireless
  Crypto
  Audio

## Slide 16: nRF52833 Peripherals
Cortex-M4F processor
32-bit ARM core
Floating point
Includes Interrupt control and SysTick (an extra timer)

## Slide 17: nRF52833 Peripherals
Memory buses

## Slide 18: nRF52833 Peripherals
JTAG and Debugging
Allows code updates
Allows GDB to step through code

## Slide 19: nRF52833 Peripherals
Volatile memory
SRAM, 128 kB

## Slide 20: nRF52833 Peripherals
Nonvolatile memory
Flash, 512 kB
Non-Volatile Memory Controller

## Slide 21: nRF52833 Peripherals
Power and Clock management

## Slide 22: nRF52833 Peripherals
GPIO pins

## Slide 23: nRF52833 Peripherals
Various timers
Watchdog Timer
Real-Time Counter
Timer peripheral

## Slide 24: nRF52833 Peripherals
Programmable Peripheral Interconnect
Random Number Generator
Temperature sensor

## Slide 25: nRF52833 Peripherals
Wireless radio
  Bluetooth Low Energy
  802.15.4 (Zigbee or Thread)
Cryptography
  ECB (AES mode)
  CCM (AES mode)
  AAR (Accelerated Address Resolver)
    For BLE random addresses

## Slide 26: nRF52833 Peripherals
Wired communication protocols
USB Device
SPI
  Controller/Peripheral
TWI (I2C)
  Controller/Peripheral
UART

## Slide 27: nRF52833 Peripherals
Inter-IC Sound (I2S)
  Wired communication bus explicitly for audio data
  Unrelated to I2C
Like a synchronous UART
  Clock, data in, data out
Additional signals
  MCK – synchronization
  LRCK – left/right channel select

## Slide 28: nRF52833 Peripherals
NFC
  Near-Field Communication
Close-range wireless communication protocol
“Tap-to-pay” systems

## Slide 29: nRF52833 Peripherals
GPIOTE
  GPIO interrupts

## Slide 30: nRF52833 Peripherals
Analog inputs
Comparator
Low-Power Comparator
Successive Approximation Analog-to-Digital Converter

## Slide 31: nRF52833 Peripherals
Quadrature Decoder peripheral
Detects rotation speeds and direction
  Usually for motors

## Slide 32: Quadrature Encoding

## Slide 33: nRF52833 Peripherals
Pulse Width Modulation
Pulse Density Modulation
  Similar idea to PWM
  Input-only peripheral
  Targets microphones

## Slide 34: nRF52833 is complete
That’s just about everything!
First 550 out of 600 pages of nRF52833 datasheet
  Remaining 50 are hardware details
    Pinout for different packages
    Recommended circuit layout
    Soldering details

## Slide 35: This knowledge is transferrable!
Example: SAM4L datasheet
  Atmel Cortex M4F
  Various peripherals
    USART, SPI, TWI, I2S, DAC, ADC, Timer, …

## Slide 36: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 37: Conferences for sensing systems research
SenSys
  Conference on Embedded Networked Sensor Systems
IPSN
  Conference on Information Processing in Sensor Networks
MobiCom
  Conference on Mobile Computing and Networking
UbiComp
  Conference on Pervasive and Ubiquitous Computing
Various other systems or HCI venues
  Occasionally Electrical or Civil Engineering venues too

## Slide 38: Sensing systems research
Combination of engineering and exploration
Generally divides into two different focuses
  Often projects will mix some of each domain
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 39: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 40: Permamote (Jackson, Adkins, Dutta)
Goal: create a 10-year wireless sensor
Solutions
  Modern sensors and microcontroller
  Energy harvesting combined with rechargeable battery
  Non-rechargeable battery as backup power
https://lab11.eecs.berkeley.edu/content/pubs/jackson19capacity.pdf

## Slide 41: Bfree (Kortbeek, Bakar, Cruz, Yildririm, Pawelczak, Hester)
Goal: hobbyist intermittent systems
Solutions
  Automatic checkpointing in python runtime
  Hardware module for easy prototyping
  User studies to demonstrate improvements
https://dl.acm.org/doi/abs/10.1145/3432191

## Slide 42: Tock (Levy, Campbell, Ghena, Giffin, Pannuto, Dutta, Levis)
Goal: safe and reliable embedded OS
  Demonstrate this is possible on small embedded platforms
Solutions
  Dedicated OS kernel with separate applications
  Protect applications with hardware features
    Memory Protection Unit
  Protect kernel with language features
    Rust programming language
https://lab11.eecs.berkeley.edu/content/pubs/levy17multiprogramming.pdf

## Slide 43: Tock software organization
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
System Calls
6LoWPAN
SI7021
SD Card
Console
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf
Syscall Interface

## Slide 44: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 45: Opo (Huang, Kuo, Pannuto, Dutta)
Goal: sense distance of human interactions
  Real-time, high accuracy, deployable
Solutions
  Ultrasonic allows for low-power detection of nearby devices
  Also provides directionality
  Measure difference in arrival time of RF and Ultrasonic to determine distance
https://lab11.eecs.berkeley.edu/content/pubs/huang14opo.pdf

## Slide 46: Powerwatch (Klugman, Adkins, et al.)
Goal: measure electric grid reliability in developing regions
“Access alone is insufficient. Reliability matters too.”
Solutions:
  Wall-powered sensor with battery-backup to detect outages and report over cellular
  Infrastructure to collect measurements and cross-correlate
  Create a team to manage the deployment
https://lab11.eecs.berkeley.edu/content/pubs/klugman19scale.pdf

## Slide 47: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research