## Slide 1: Lecture 03 Embedded Software
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Updates
Hardware for anyone who filled out the form by class Wednesday
  Should be here today? Maybe Monday.
All orders have been placed
  Except for a few new students

## Slide 3: Today’s Goals
Discuss challenges of embedded software
Describe compilation and linking of embedded code
Explore the microcontroller boot process

## Slide 4: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 5: Micro:bit v2
Circuit board
  Entire thing
  a.k.a “Dev Board”
  a.k.a PCB (Printed Circuit Board)
Microcontroller
  The computer on it
  Microbit has two
    One as a programmer
    One for applications
Microcontrollers

## Slide 6: KL27Z – Programmer on the Micro:bit v2
32-bit ARM Cortex-M0+ microcontroller
  48 MHz core, 16 KB RAM, 256 KB Flash
Acts as a programming interface to nRF52833
  Connects to USB and to JTAG (SWD)

## Slide 7: nRF52833 – Microcontroller on the Micro:bit v2
32-bit ARM Cortex-M4F microcontroller
  64 MHz core, 128 KB RAM, 512 KB Flash
  Floating point support
  2.4 GHz Radio: Bluetooth Low energy / 802.15.4
  Various peripherals
    ADC, PWM
    I2C, UART, SPI, USB
    RNG, 32-bit Timers, Watchdog, Temperature
    Up to 42 I/O pins

## Slide 8: To the datasheet!
nRF52833 Product Specification
  Online: https://infocenter.nordicsemi.com/index.jsp?topic=%2Fps_nrf52833%2Fkeyfeatures_html5.html
  PDF: https://infocenter.nordicsemi.com/pdf/nRF52833_PS_v1.3.pdf

## Slide 9: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 10: Assumptions of embedded programs
Expect limitations
  Very little memory
  Very little computational power
  Very little energy
Don’t expect a lot of support
  Likely no operating system
  Might not even have error reporting capabilities
Moral: think differently about your programs

## Slide 11: Ramifications of limited memory
Stack and Data sections are limited
  Be careful about too much recursion
  Be careful about large local variables
  Large data structures defined globally are preferred
    Fail at compile time
Heap section is likely non-existent
  Why?

## Slide 12: Ramifications of limited memory
Stack and Data sections are limited
  Be careful about too much recursion
  Be careful about large local variables
  Large data structures defined globally are preferred
    Fail at compile time
Heap section is likely non-existent
  Why?
    Malloc could run out of memory at runtime

## Slide 13: Avoiding dynamic memory
Malloc is scary in an embedded context
What if there’s no more memory available?
  Traditional computer
    Swap memory to disk
    Worst case: wait for a process to end (or kill one)
  Embedded computer
    There’s likely only a single application
    And it’s the one asking for more memory
    So it’s not giving anything back anytime soon
This is unlikely to happen at boot
  Instead it’ll happen hours or days into running as memory is slowly exhausted…

## Slide 14: Limitations on processing power
Typically not all that important
  Code still runs pretty fast
    10 MHz -> 100 ns per cycle
  Controlling hardware usually doesn’t have a lot of code complexity
    Quickly gets to the “waiting on hardware” part
Problems
  Machine learning
    Learning on the device is neigh impossible
    Memory limitations make it hard to fit weights anyways
  Cryptography
    Public key encryption takes seconds to minutes

## Slide 15: Common programming languages for embedded
C
  For all the reasons that you assume
  Easy to map variables to memory usage and code to instructions
Assembly
  Not entirely uncommon, but rarer than you might guess
  C code optimized by a modern compiler is likely faster
  Notable uses:
    Cryptography to create deterministic algorithms
    Operating Systems to handle process swaps

## Slide 16: Rarer programming languages for embedded
C++
  Similar to C but with better library support
  Libraries take up a lot of code space though ~100 KB
Rust
  Modern language with safety and reliability guarantees
  Relatively new to the embedded space
    And a high learning curve
Python, Javascript, etc.
  Mostly toy languages
  Fine for simple things but incapable of complex operations

## Slide 17: What’s missing from programming languages?
The embedded domain has several requirements that other domains do not
What is missing from programming languages that it wants?
  Sense of time
  Sense of energy

## Slide 18: Programming languages have no sense of time
Imagine a system that needs to send messages to a motor every 10 milliseconds
  Write a function that definitely completes within 10 milliseconds
Accounting for timing when programming is very challenging
  We can profile code and determine timing at runtime
  If we know many details of hardware, instructions can give timing
    Unless the code interacts with external devices

## Slide 19: Determining energy use is rather complicated
Software might
  Start executing a loop
  Turn on/off an LED
  Send messages over a wired bus to another device
Determining energy these operations take is really difficult
  Even with many details of the hardware
  Different choices of clocks can have a large impact
  Often profiled at runtime after writing the code
    Iterative write-test-modify cycle

## Slide 20: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 21: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)

## Slide 22: Cross compilers compile for different architectures
The compiler we’ll be using is a cross compiler
  Run on one architecture but compile code for another
    Example: runs on x86-64 but compiles armv7e-m
GCC is named: ARCH-VENDOR-(OS-)-ABI-gcc
  arm-none-eabi-gcc
    ARM architecture
    No vendor
    No OS
    Embedded Application Binary Interface
  Others: arm-none-linux-gnueabi, i686-unknown-linux-gnu

## Slide 23: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables

## Slide 24: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do traditional computers handle this?

## Slide 25: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do traditional computers handle this?
  Virtual memory allows all applications to use the same memory addresses
Embedded solution
  Only run a single application
  Provide an LD file
    Specifies memory layout for a certain system
    Places sections of code in different places in memory

## Slide 26: Anatomy of an LD file
nRF52833: 512 KB Flash, 128 KB SRAM
First, LD file defines memory regions
  MEMORY {
  FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x80000
  RAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x20000
  }
A neat thing about microcontrollers: pointers have meaning
  Just printing the value of a pointer can tell you if it’s in Flash or RAM

## Slide 27: Anatomy of an LD file
It then places sections of code into those memory regions
  .text : {
  KEEP(*(.Vectors))
  *(.text*)
  *(.rodata*)
  . = ALIGN(4);
  } > FLASH __etext = .;
  .data : AT (__etext) {
  __data_start__ = .;
  *(.data*)
  __data_end__ = .;
  } > RAM
  .bss : {
  . = ALIGN(4);
  __bss_start__ = .;
  *(.bss*)
  . = ALIGN(4);
  __bss_end__ = .;
  } > RAM

## Slide 28: Sections of code
Where do these sections come from?
Most are generated by the compiler
  .text, .rodata, .data, .bss
  You need to be deep in the docs to figure out how the esoteric ones work
Some are generated by the programmer
  Allows you to place certain data items in a specific way
  __attribute__((section(".foo")))
  int test[10] = {0,0,0,0,0,0,0,0,0,0};

## Slide 29: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables
Output: a binary (or hex) file

## Slide 30: Example
Demonstrated in the blink application in lab repo
  https://github.com/nu-ce346/nu-microbit-base/tree/main/software/apps/blink

## Slide 31: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 32: Embedded environments
There are a multitude of embedded software systems
  Every microcontroller vendor has their own
  Popular platforms like Arduino
We’re using the Nordic software plus some extensions made by my research group
  It’ll be a few weeks until that matters for the most part
  We’ll start off by writing low-level drivers ourselves

## Slide 33: Software Development Kit (SDK)
Libraries provided by Nordic for using their microcontrollers
  Actually incredibly well documented! (relatively)
  Various peripherals and library tools
SDK documentation
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/index.html
  Warning: search doesn’t really work
Most useful link is probably to the list of data structures
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/annotated.html

## Slide 34: nRF52x-base
Wrapper built around the SDK by Lab11
  Branden Ghena, Brad Campbell (UVA), Neal Jackson, a few others
  Allows everything to be used with Makefiles and command line
  https://github.com/lab11/nrf52x-base
We include it as a submodule
  It has a copy of the SDK code and softdevice binaries
  It has a whole Makefile system to include to proper C and H files
  We include a Board file that specifies our specific board’s needs and capabilities
Go to repo to explain

## Slide 35: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process

## Slide 36: How does a microcontroller start running code?
Power comes on
Microcontroller needs to start executing assembly code
You expect your main() function to run
  But a few things need to happen first

## Slide 37: Step 0: set a stack pointer
Assembly code might need to write data to the stack
  Might call functions that need to stack registers
ARM: Valid address for the stack pointer is at address 0 in Flash
  Needs to point to somewhere in RAM
  Hardware loads it into the Stack Pointer when it powers on

## Slide 38: Step 1: set the program counter (PC)
a.k.a. the Instruction Pointer (IP) in x86 land
ARM: valid instruction pointer is at address 4 in Flash
  Could point to RAM, usually to Flash though
  Automatically loaded into the PC after the SP is loaded
    Again, hardware does this

## Slide 39: Step 2: “reset handler” prepares memory
Code that handles system resets
  Either reset button or power-on reset
  Address was loaded into PC in Step 1
Reset handler code:
  Loads initial values of .data section from Flash into RAM
  Loads zeros as values of .bss section in RAM
  Calls SystemInit
    Handles various hardware configurations/errata
  Calls _start
nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/gcc_startup_nrf52833.S nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/system_nrf52.c

## Slide 40: Step 3: set up C runtime
_start is provided by newlib
  An implementation of libc – the C standard library
  Startup is a file usually named crt0
Does more setup, almost none of which is relevant for our system
  Probably is this code that actually zeros out .bss
  Sets argc and argv to 0
  Calls main() !!!
https://sourceware.org/git/gitweb.cgi?p=newlib-cygwin.git;a=blob_plain;f=libgloss/arm/crt0.S;hb=HEAD

## Slide 41: Online writeup with way more details and a diagram
Relevant guide!!
  https://embeddedartistry.com/blog/2019/04/17/exploring-startup-implementations-newlib-arm/
  Covers the nRF52!

## Slide 42: Outline
Microbit microcontroller
Embedded Software
Embedded Toolchain
Lab Software Environment
Boot Process