## Slide 1: Lecture 07 Driver Design
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Today’s Goals
Explore two aspects of device driver design
  Virtualization
  Non-blocking vs Blocking interfaces
Discuss how interrupts interact with these
  Event-loop as a partial alternative

## Slide 3: Outline
Virtualized Drivers
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 4: Choosing resource amounts is a problem
Problem: applications may require any number of resources
  Particularly in this case: peripherals
  For example, how many timers should there be?
But hardware has to pick some number to provide
  More is wasted cost
  Too few and applications cannot succeed
Solution: virtualize the resource

## Slide 5: Virtualization pattern
Create a queue of requests and a pool of resources
  N requests to M resources
Application requests are queued when they come in
  Rather than serviced immediately
While a resource is available
  Pop request from queue (by some priority)
  Service with hardware
  Wait until another resource is available

## Slide 6: Example: sending serial messages
Serial messages (such as printf() strings) are sent via UART
  UARTE peripheral (we’ll talk about this later)
nRF52 has two UARTE peripherals
  Can be attached to any output pins
  Changing pins is a quick operation
What if we want to talk to three serial devices?
  Console (printf output)
  GPS (NMEA)
  WiFi radio (AT commands)

## Slide 7: Virtualized UART
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
Empty

## Slide 8: Virtualized UART: serves request with hardware
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}

## Slide 9: Virtualized UART: serves until resources are full
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}

## Slide 10: Virtualized UART: additional requests are queued
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 11: Virtualized UART: moves to next item when complete
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 12: Virtualized UART: moves to next item when complete
Serial Console
GPS
WiFi Radio
Microcontroller
Virtual UART
UARTE0
UARTE1
Request Queue
Application
{Serial Console, TX, 0x20001F00, 20}
{GPS, RX, 0x20001000, 150}
{WiFi Radio, TX, 0x20000020, 1500}
{Serial Console, TX, 0x20000500, 20}
{Serial Console, TX, 0x20001E00, 10}

## Slide 13: Challenges to making virtualization work
How fast are requests coming in?
  Requests more quickly than service are an unsatisfiable system
How long does it take to reconfigure the resource?
  Long delays could mean high latency
  Might want to optimize for requests with same configuration first
Need to ensure all of the configuration changes
  Common bug: forget to modify part of one register and system works most of the time, but not in all cases
Need ability to queue requests
  Usually stored in a linked list structure
  Dynamically… But we generally want to avoid dynamic memory

## Slide 14: Dynamic resource allocation options
Create a queue with a maximum size in Virtual Driver
  Some number larger than the hardware picked, based on app knowledge
  Still either runs out or wastes memory
Just use malloc()
  Is actually possible on the nRF52 with newlib (libc implementation)
  Might run out, but then just wait for requests to complete
Create list nodes individually as global variables
  Application decides how many it needs at compile time
  Passes them into the Virtual Driver at first use
    “Here’s my request and a linked list node to store it in”

## Slide 15: Another example: managing multiple timers
You often have tasks that look like this:
Most easily thought about as three separate timers
  But maybe the system doesn’t have that many timers to spare!
  Virtualization can help

## Slide 16: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10010
10050
10110
20000
time
CC Register: 10010
10010
10050
10110
20000

## Slide 17: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10010, A
10050, B
10110, C
20000, D
time
CC Register: 10010
10010
10050
10110
20000
Call timer handler A!
Update CC register and list

## Slide 18: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10050, B
10110, C
20000, D
time
CC Register: 10050
10010
10050
10110
20000

## Slide 19: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10050, B
10110, C
20000, D
time
CC Register: 10050
10010
10050
10110
20000
Call timer handler B!
Update CC register and list

## Slide 20: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10110, C
20000, D
time
CC Register: 10110
10010
10050
10110
20000

## Slide 21: Virtual timers
Solution: keep a list of timer expiration times
  Soonest expiration goes in the Capture/Compare register
  Others stay in linked list, sorted by expiration
Timer Requests
10100, E
10110, C
20000, D
time
CC Register: 10100
10010
10050
10110
20000
New request arrives for 10100
Enqueue and sort queue
Update CC if first request has changed

## Slide 22: Enqueuing timer requests
Timer requests come in the form: {N seconds from now}
  timer_request(duration, handler);
Requests are always relative to the current time
Need to enqueue by expiration time
  Duration + Current Time
  Allows for a globally sortable list
    Need to decide how to handle overflow logic in real world

## Slide 23: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
  Check for this, and call handler manually if necessary
Timer Requests
10100, E
10110, C
20000, D
time
CC Register: 10100
10010
10050
10110
20000
Handle 10100 event, Call E

## Slide 24: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
  Check for this, and call handler manually if necessary
Timer Requests
10110, C
20000, D
time
CC Register: 10110
10010
10050
10110
20000
Update list
Update CC register
Oh no! That’s in the past!!

## Slide 25: Make sure not to miss timers
Sorting list and modifying the CC register takes time
  Might have skipped right past the soonest event
  Check for this, and call handler manually if necessary
Timer Requests
20000, D
time
CC Register: 20000
10010
10050
10110
20000
Call C manually
Update list and CC register again

## Slide 26: Some timers are periodic
Repeating timers are easy to add to this system
  Include a Boolean for “repeating” and the duration in the request
When timer expires
  If not repeating, just call handler and then drop it
  If repeating,
    First reinsert based on duration and new current time
    Then call the handler
      Don’t want the latency of the handler to slow us down

## Slide 27: Concurrency safety
Modifying the request structure in an interrupt context is dangerous
  New request might be in the middle of getting added
  Interrupt would run right in the middle of that
  Literally an OS data race example
Solution: disable interrupts during critical section
  Whenever editing request structure
  Enable interrupts after, which may result in an event
    Note: Interrupt handler might now fire but have no work to do. Should always check if something should actually be handled first

## Slide 28: Outline
Virtualized Drivers
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 29: Callback functions
timer_start(duration, my_timer_handler, context);
Driver interfaces often provide a callback mechanism
  Caller provides a function which should be executed when complete
“Context” is often provided as well (void*)
  Ability for caller to pass an argument for the callback function
  Often a pointer to a position in a structure or a shared variable to modify

## Slide 30: Function pointers in C
Harder than in Javascript or C++. Can’t define anonymous function inline
  Instead create a pointer to an existing function in your code
void myfun (int a) {
// do something here
}
void main() {
void (*fun_ptr)(int) = &myfun;
fun_ptr(10); // dereference happens automatically
}

## Slide 31: Callbacks usually run in an interrupt context
If the interrupt handler calls the callback, the callback will be within that same interrupt context
Be careful which variables you modify!!
  Same concurrency problems mentioned before
Starts to get pretty annoying
  Embedded systems deal with concurrency issues just like OS

## Slide 32: Blocking function calls
Alternative option: blocking calls
  Do not return until request is complete
void myfun (void* context) {
*(boolean*)context = true; // context is the flag pointer
}
void timer_start_blocking(duration) {
boolean flag = false;
// duration, pointer, context
timer_start(duration, &myfun, &flag);
while (!flag) { }
}

## Slide 33: Temp driver example
nu-microbit-base/software/apps/temp_driver/

## Slide 34: Outline
Virtualized Drivers
Driver Interfaces (Blocking and Non-Blocking)
Event Loop

## Slide 35: Interrupts are frustrating
We do not want to block on every call
We also do not want to deal with concurrency issues
Alternative: one main event loop
  Polls necessary sensors
  Iterates through state machine and determine actions
  Runs at a certain frequency

## Slide 36: Event loop
Rather than polling a single driver, poll all of them
  Each time through the loop check all relevant inputs
  Respond to events that are necessary
  Sleep until ready to start again
    while (1) {
    time start = get_time();
    boolean result = check_timer();
    if (result) { check_gps(); }
    adjust_throttle();
    sleep(1ms – (get_time() – start));
    }

## Slide 37: Top-half / Bottom-half handler design
Top half
  Implements interface that higher layers require
  Performs logic to start device requests
  Wait for I/O to be completed
    Synchronously (blocking) or asynchronously (return to event loop)
  Handle responses from the device when complete
Bottom half
  Interrupt handler
    Continues next transaction
    Or signals for top half to continue (often with shared variable)

## Slide 38: Outline
Virtualized Drivers
Driver Interfaces (Blocking and Non-Blocking)
Event Loop