## Slide 1: Lecture 16 Nonvolatile Memory
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Friday
  Will do last checkoffs for people who need them on Lab 6
  Also available to discuss projects
    Will put a sign-up form online
Moving forward
  Only two lectures left!!
  Time to put some serious effort into projects (two weeks remaining)
  Week after next is project demos
    Details to come

## Slide 3: Today’s Goals
Discuss uses of memory, especially nonvolatile memory, in embedded systems
Introduce protocols for interacting with non-volatile memory
  Internal Flash
  External SD Card

## Slide 4: Outline
Embedded Memories
nRF52 NVMC
SD Cards

## Slide 5: Memory in computing
Various different memories serve different purposes in computing
Needs
  Fast, infinite-lifetime memory to keep things like stack memory
  Nonvolatile memory that can be read from
Desires
  Fast, infinite-lifetime nonvolatile memory

## Slide 6: Register technology: SRAM
Static RAM (SRAM)
  Each cell stores a bit in a bi-stable circuit, typically a six-transistor circuit
  Static – no need for periodic refreshing; keeps data while powered
  Relatively insensitive to disturbances such as electrical noise
    Energetic particles (alpha particles, cosmic rays) can flip stored bits
Fastest memory on computer
  Also most expensive and takes up most space per bit
  Typically used for registers and cache memories

## Slide 7: SRAM can be used a permanent memory in a pinch
Gameboy and Gameboy Color used batteries to save state
Gameboy Advanced games used batteries for an internal clock
PSA: your old Gameboy games have likely lost their save files

## Slide 8: Main memory technology: DRAM
Dynamic RAM (DRAM)
  Each cell stores a bit as a charge in a capacitor
  Capacitors lose charge; each cell must be refreshed every 10-100 ms
  More sensitive to disturbances (EMI, radiation, …) than SRAM
Slower than SRAM, but cheaper and denser
  ~100x slower than registers

## Slide 9: Accessing DRAM
Read entire row of data at a time
  Large in practice, kilobytes
Select actual bytes that are wanted
  Possibly modifying those bits
Write row back to memory
  Must always happen!
  Reading is destructive
Typically used for main memory in traditional computing systems
  Constant refresh makes it untenable for low-power embedded systems

## Slide 10: Disk drive storage

## Slide 11: Need breeds creativity
Original iPod used a small disk drive

## Slide 12: Floating-gate transistors
Concept behind transistor-based non-volatile memory
  EPROM, EEPROM, and Flash
  High voltage on control gate creates charge on floating gate
  Charge on floating gate activates/deactivates transistor
High voltage degrades structure, leading it to eventually fail after enough writes

## Slide 13: EPROM
Erasable programmable read-only memory
Erasable
  If you shine UV light directly on the IC
  Needed a window to expose the IC
Programmable
  With high voltage (25-50 volts)
Typically acted as read-only memory in circuits

## Slide 14: EEPROM
Electrically-erasable programable read-only memory
Same concept as EPROM, but includes internal circuitry to allow rewriting under normal conditions
  Slow and high-power to write
  Has a longer lifetime compared to flash, ~100k writes
Can be built into other ICs
  Example: AT90USB162 microcontroller (512 bytes)

## Slide 15: Flash
Similarly based on floating-gate transistors
  But with a different design that allows for faster erase of entire blocks
  More limited lifetime, ~1k-100k writes (10k common for embedded)
Cannot erase individual bytes, must erase in units of blocks
  Read can happen in units of bytes though
Heavily used in commercial devices
  Flash drives
  SSDs
  Smartphone storage
  Microcontroller non-volatile storage!

## Slide 16: More exotic memories
FRAM and MRAM are both rising protentional Flash replacements
  Non-volatile
  Writable at the byte level
  Very high to infinite write/erase cycles
  Lower energy costs for writing and reading
The two use unrelated magnetic techniques for data storage
Starting to appear in microcontrollers
  TI MSP430s have used 16 kB FRAM
  Apollo4 (ARM Cortex-M4F) has 2 MB of MRAM

## Slide 17: Outline
Embedded Memories
nRF52 NVMC
SD Cards

## Slide 18: Flash memory on the nRF52833
512 kB total Flash memory
  128 pages each 4 kB in size
Non-Volatile Memory Controller (NVMC) controls access
  Enables writing to flash
  Enables erasing flash
  Manages status of flash

## Slide 19: Writing to Flash
Configurable, disabled by default
  Enable with configuration register
Rules for writing to Flash
  Must write word-aligned 32-bit values
  Can only write 0 values, not ones
  Can only write 2 times before erasing (even if there are still 1 bits)
Takes 42.5 μs to write a 32-bit word
  64 MHz clock ⇨ 2720 cycles per 32-bit write

## Slide 20: Erasing Flash
Lifetime: 10000 erase cycles per page
Options
  Erase a single page (4 kB): 87.5 ms
  Erase all of flash (512 kB): 173 ms
CPU is halted if executing code from Flash during the erase
  That’s 5.6 million cycles…
  Code can execute from SRAM instead
  Can also be split into a series of partial erases
    Which must add up to a complete erase time before writing

## Slide 21: Factory Information Configuration Registers
Read-only memory
Chip-specific information and configuration
  Code size
  Unique device ID
  Production IDs
  Temperature conversion functions

## Slide 22: User Information Configuration Registers
Additional Flash memory for non-volatile user configurations
  Writable and erasable through NVMC processes described earlier
32 words of customer information (128 bytes total)
Special configurations
  Reset pin
  NFC pin enable/disable
  Debug configuration

## Slide 23: Outline
Embedded Memories
nRF52 NVMC
SD Cards

## Slide 24: SD card references
ChaN
  Embedded systems engineer in Japan (and is amazing)
  http://elm-chan.org/docs/mmc/mmc_e.html
  http://elm-chan.org/fsw/ff/00index_e.html
Various others
  http://users.ece.utexas.edu/~gerstl/ee445m_s15/lectures/Lec08.pdf
  http://alumni.cs.ucr.edu/~amitra/sdcard/Additional/sdcard_appnote_foust.pdf
  https://luckyresistor.me/cat-protector/software/sdcard-2/
  http://users.ece.utexas.edu/~valvano/EE345M/SD_Physical_Layer_Spec.pdf
  https://github.com/tock/tock/blob/master/capsules/src/sdcard.rs

## Slide 25: SD cards
“Secure Digital” Card
  Includes various formfactors
  Flash memory
  Capacities from 8 MB to 128 TB
    512 byte blocks
Supports 1-bit SPI interface
  As well as 4-bit SD bus protocol
Easy to support in embedded systems
  Cheap but high power

## Slide 26: Electrical connections for an SD card
SD Card connections
  SPI CIPO, COPI, CS, SCLK
  Plus a switch to enable/disable the SD card and a detect signal

## Slide 27: Controlling the SD card
Index: 6-bit value of command being sent
Argument: 32-bit value that may be arguments to commands
CRC: checks for bit errors
Response (after delay)

## Slide 28: SD card SPI commands

## Slide 29: Reading from the SD card
Single block read
Multiple block read (CMD12 – Stop Transmission)

## Slide 30: SD card delays can be significant
Performing a single byte read
  Almost 300 μs before the SD card starts sending data
  ~200 μs additional time to send the 512 bytes (20 Mbps data, 8 Mbps total)

## Slide 31: Writing to the SD card
Single block write
Multiple block write

## Slide 32: Layering a filesystem on top of an SD card
FatFs library implements the filesystem agnostic of application and storage medium
Enables the use of file system calls:
  Open, Close, Read, Seek
Connects to generic interface for low-level implementation
  disk_status, disk_init, disk_read, disk_write

## Slide 33: Outline
Embedded Memories
nRF52 NVMC
SD Cards