## Slide 1: Lecture 06 Arithmetic Instructions
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2024
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Pack Lab due Thursday by midnight
  Expect office hours to start getting very busy
  Morning office hours today were totally empty though…
Bomb Lab releases today or tomorrow
  Practice interpreting assembly code
  Due after the midterm exam
    But we strongly recommend you start it early as assembly practice
  Partnership survey will go out on Piazza soon

## Slide 3: Administrivia
Midterm exam in 1.5 weeks
  Class time next week Thursday (February 1st)
  Covers everything from the start of class through Control Flow
    Does NOT cover function calls in assembly (“Procedures” lecture next week)
  Bring a pencil and one 8.5”x11” inch paper with notes
    Notes can be on both sides, handwritten or typed
  No calculators
  Practice exams (and solutions) are on the Canvas home page
  Also good practice: Homework 2 (due Tuesday), phases 1-3 of Bomb Lab
ANU students: I’ll reach out this week with details

## Slide 4: Instruction Set Architecture sits at software/hardware interface
C Language
x86-64
Intel Pentium 4
Intel Core i7
AMD Ryzen
GCC
ARMv8 (AArch64/A64)
ARM Cortex-A53
Apple M1
Clang
Program B
Program A
Compiler
Source code
Architecture
Different applications
or algorithms
Perform optimizations,
generate instructions
Different implementations
Hardware
Instruction set

## Slide 5: x86-64 Integer Registers
%rax
%eax
%ax
%ah
%al
%rbx
%ebx
%bx
%bh
%bl
%rcx
%ecx
%cx
%ch
%cl
%rdx
%edx
%dx
%dh
%dl
%rsi
%esi
%si
%rdi
%edi
%di
%rbp
%ebp
%bp
%rsp
%esp
%sp
%r8
%r8d
%r8w
32-bit registers
16-bit registers
8-bit
…
%r15
%r15d
%r15w
…
…
%sil
%dil
%bpl
%spl
%r8b
%r15b
64-bit registers
8-bit

## Slide 6: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic operation on register or memory data
  c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
In x86-64 these basic types can often be combined
    Remember: Memory is indexed just like an array of bytes!

## Slide 7: Operand Combinations
 | Source | Dest | Src, Dest | C Analog
movq | Imm | Reg | movq $0x4, %rax | 
 |  | Mem | movq $-147, (%rax) | 
 | Reg | Reg | movq %rax, %rdx | 
 |  | Mem | movq %rax, (%rdx) | 
 | Mem | Reg | movq (%rax), %rdx | 
var_a = 0x4;
*p_a = -147;
var_d = var_a;
*p_d = var_a;
var_d = *p_a;
Cannot do memory-memory transfer with a single instruction
Notes: Mem -> Reg
Reg -> Mem
movq (%rax), %rdx
movq %rdx, (%rbx)

## Slide 8: Today’s Goals
Continue exploring x86-64 assembly
  Arithmetic
Discuss real-world x86-64
  Special cases
  Generating assembly
Understand condition codes
  Method for testing Boolean conditions

## Slide 9: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly

## Slide 10: Some arithmetic operations
Two-operand instructions
Instruction | Effect | Description
addq S, D | D ← D + S | Add
subq S, D | D ← D – S | Subtract
imulq S, D | D ← D * S | Multiply
xorq S, D | D ← D ^ S | Exclusive or
orq S, D | D ← D ¦ S | Or
andq S, D | D ← D & S | And
Instruction | Effect | Description
sarq k, D | D ← D >> k | Shift arithmetic right
shrq k, D | D ← D >> k | Shift logical right
salq k, D | D ← D << k | Shift left
shlq k, D | D ← D << k | Shift left (same as salq)
Shifts
Operand types
Immediate
Register
Memory
(Only one can be memory)
Be careful with operand order!!!
(Matters for some operations)
Notes: Watch out for argument order!
No distinction between signed and unsigned int (why?)

## Slide 11: A note on instruction names
Instruction names can look somewhat arcane
  shlq? movzbl?
But, good news: names (usually) follow conventions
  Common prefixes (add), suffixes (b, w, l, q), etc.
  So you can understand pieces separately
  Then combine their meanings

## Slide 12: Some Arithmetic Operations
Unary (one-operand) Instructions:
See textbook Section 3.5.5 for more instructions: mulq, cqto, idivq, divq
Instruction | Effect | Description
incq D | D ← D + 1 | Increment
decq D | D ← D – 1 | Decrement
negq D | D ← -D | Negate
notq D | D ← ~D | Complement
Notes: Why have a different inc operator?
  Smaller bit representation!
  Maybe faster implementation

## Slide 13: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
op src, dst

## Slide 14: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
  movq %rbx, %rax (a = b;)
  addq %rcx, %rax (a += c;)
op src, dst

## Slide 15: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
  movq $0, %rax
  addq %rbx, %rax
  addq %rcx, %rax
Is this okay?
op src, dst

## Slide 16: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
  movq $0, %rax
  addq %rbx, %rax
  addq %rcx, %rax
Is this okay?
Yes: just a little slower
op src, dst

## Slide 17: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
  addq %rbx, %rcx
  movq %rcx, %rax
Is this okay?
op src, dst

## Slide 18: Converting C to Assembly
Suppose a → %rax, b → %rbx, c → %rcx Convert the following C statement to x86-64:
a = b + c;
  addq %rbx, %rcx
  movq %rcx, %rax
Is this okay?
No: it overwrites C which could still be used later in code!
op src, dst

## Slide 19: Question + Break
Suppose a → %rax, b → %rbx, c→ %rcx Convert the following C statement to x86-64:
        c = (a-b)+5;
Reminder addq, src, dst → dst = dst + src
[A]
movq %rax, %rcx
subq %rbx, %rcx
addq $5, %rcx
[B] movq %rax, %rcx
subq %rbx, %rcx
movq $5, %rcx
[C]
subq %rcx, %rax, %rbx
addq %rcx, %rcx, $5
[D]
subq %rbx, %rax
addq $5, %rax
movq %rax, %rcx

## Slide 20: Question + Break
Suppose a → %rax, b → %rbx, c→ %rcx Convert the following C statement to x86-64:
        c = (a-b)+5;
[A]
movq %rax, %rcx
subq %rbx, %rcx
addq $5, %rcx
[B] movq %rax, %rcx
subq %rbx, %rcx
movq $5, %rcx
[C]
subq %rcx, %rax, %rbx
addq %rcx, %rcx, $5
[D]
subq %rbx, %rax
addq $5, %rax
movq %rax, %rcx
Reminder: addq, src, dst → dst = dst + src
c = 5
Not x86
Overwrites a

## Slide 21: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly

## Slide 22: x86-64 Integer Registers
%rax
%eax
%ax
%ah
%al
%rbx
%ebx
%bx
%bh
%bl
%rcx
%ecx
%cx
%ch
%cl
%rdx
%edx
%dx
%dh
%dl
%rsi
%esi
%si
%rdi
%edi
%di
%rbp
%ebp
%bp
%rsp
%esp
%sp
%r8
%r8d
%r8w
32-bit registers
16-bit registers
8-bit
…
%r15
%r15d
%r15w
…
…
%sil
%dil
%bpl
%spl
%r8b
%r15b
64-bit registers
8-bit

## Slide 23: Moving data of different sizes
“Vanilla” move can only move between source and dest of the same size
  Larger → smaller: use the smaller version of registers
  Smaller → larger: extension! We have two options: zero-extend or sign-extend
Instruction | Effect | Description
movX S,D X ∈ {q, l, w, b} | D ← S | Copy quad-word (8B), long-word (4B), word (2B) or byte (1B)
movsXX S,D XX ∈ {bw, bl, wl, bq, wq, lq} | D ← SignExtend(S) | Copy sign-extended byte to word, byte to long-word, etc.
movzXX S,D XX ∈ {bw, bl, wl, bq, wq, lq} | D ← ZeroExtend(S) | Copy zero-extended byte to word, byte to long-word, etc.
cltq (convert long to quad) | %rax ← SignExtend(%eax) | Sign-extend %eax to %rax
Notes: So far, we’ve seen moving data from a source of one size, to a destination of the same size.
It’s also useful to go to a larger destination, but there’s some choices to make wrt how to fill the rest.
If you want to copy to a smaller destination, you should instead use a smaller view on the source.

## Slide 24: Example: moving byte data
Note the differences between movb, movsbl and movzbl
Assume %dl = 0xCD, %eax = 0x98765432 movb %dl,%al movsbl %dl,%eax movzbl %dl,%eax
%eax = 0x987654CD
%eax = 0xFFFFFFCD
%eax = 0x000000CD
op src, dst

## Slide 25: 32-bit Instruction Peculiarities
Instructions that move or generate 32-bit values also set the upper 32 bits of the respective 64-bit register to zero, while 16 or 8 bit instructions don't.
movabsq $0xffffffffffffffff, %rax # rax = 0xffffffffffffffff
movb $0, %al # rax = 0xffffffffffffff00
movw $0, %ax # rax = 0xffffffffffff0000
movl $0, %eax # rax = 0x0000000000000000
This includes 32-bit arithmetic! (e.g., addl)
op src, dst

## Slide 26: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly

## Slide 27: Complete Memory Addressing Modes
General:
  D(Rb,Ri,S)
    Rb: Base register (any register)
    Ri: Index register (any register except %rsp)
    S: Scale factor (1, 2, 4, 8) (sizes of common C types)
    D: Constant displacement value (a.k.a. immediate)
Mem[ Reg[Rb] + Reg[Ri]*S + D ]
Notes: Syntax for memory operands can be more complex
Designed to do things that are common with pointers
D: displacement, add a constant
Rb: base pointer
Ri: index into array
S: scale the index (pointer arithmetic needs to scale by the size of the pointer target)
  compiler keeps track of what the pointer points to and scales accordingly
  int x[] x[i]
  ith element of an array of ints: Ri=i, S=4 (bytes)
See figure 3.3 in 3e textbook

## Slide 28: Saving computed addresses
Generally, any instruction with () in it, accesses memory
  Address is computed first
  Loads from memory if in a source operand
  Stores into memory if in a destination operand
But what if what you really want is the address?
  lea – load effective address
  Exception to () rule. Does NOT access memory
  Also used for arbitrary arithmetic
    This is the compiler’s favorite instruction

## Slide 29: Address computation instruction
leaq src, dst
  "lea" stands for load effective address
  src MUST be an address expression (any of the formats we’ve seen)
  dst is a register
  Sets dst to the address computed by the src expression (does not go to memory! – it just does math)
  Example: leaq (%rdx,%rcx,4), %rax
Uses:
  Computing addresses without a memory reference
    e.g. translation of p = &x[i];
  Computing arithmetic expressions of the form x+k*i+d
    Though k can only be 1, 2, 4, or 8
Notes: Those address calculations always go to memory except in one special case

## Slide 30: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x2
0x100
%rdi
%rsi
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi

## Slide 31: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x108
0x2
0x100
%rdi
%rsi
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi

## Slide 32: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x108
0x10
0x2
0x100
%rdi
%rsi
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi

## Slide 33: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x108
0x10
0x2
0x100
%rdi
0x100
%rsi
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi

## Slide 34: Example: lea vs. mov
0x120
0x118
0x110
0x108
0x100
Word
Address
Memory
123
0x10
0x1
0x400
0xF
0x8
Registers
%rax
%rbx
%rcx
%rdx
0x108
0x10
0x2
0x100
%rdi
0x100
%rsi
0x1
leaq (%rdx,%rcx,4), %rax
movq (%rdx,%rcx,4), %rbx
leaq (%rdx), %rdi
movq (%rdx), %rsi

## Slide 35: Why does the compiler love lea?
Sometimes it’s good for computing addresses
Usually the compiler uses it to do math in fewer instructions
  addq only adds a source and a destination, and overwrites destination
  leaq adds up to two registers and an immediate, AND stores to a different register!

## Slide 36: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 37: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
leaq (%rsi,%rdi),%rcx # rcx = x+y (t1)
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 38: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
leaq (%rsi,%rdi),%rcx # rcx = x+y (t1)
leaq (%rsi,%rsi,2),%rsi # rsi = y + 2*y = 3*y
salq $4,%rsi # rsi = (3*y)*16 = 48*y (t4)
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 39: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
leaq (%rsi,%rdi),%rcx # rcx = x+y (t1)
leaq (%rsi,%rsi,2),%rsi # rsi = y + 2*y = 3*y
salq $4,%rsi # rsi = (3*y)*16 = 48*y (t4)
addq %rdx,%rcx # rcx = z+t1 (t2)
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 40: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
leaq (%rsi,%rdi),%rcx # rcx = x+y (t1)
leaq (%rsi,%rsi,2),%rsi # rsi = y + 2*y = 3*y
salq $4,%rsi # rsi = (3*y)*16 = 48*y (t4)
addq %rdx,%rcx # rcx = z+t1 (t2)
leaq 4(%rsi,%rdi),%rdi # rdi = t4+x+4 (t5)
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 41: Compiling Arithmetic Operations
int arith (long x, long y, long z) {
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
....
}
# rdi = x
# rsi = y
# rdx = z
leaq (%rsi,%rdi),%rcx # rcx = x+y (t1)
leaq (%rsi,%rsi,2),%rsi # rsi = y + 2*y = 3*y
salq $4,%rsi # rsi = (3*y)*16 = 48*y (t4)
addq %rdx,%rcx # rcx = z+t1 (t2)
leaq 4(%rsi,%rdi),%rdi # rdi = t4+x+4 (t5)
imulq %rcx,%rdi # rdi = t2*t5 (rval)
Compiler can reorder operations
Can have one statement take multiple instructions
Can have one instruction handle multiple statements
Don’t expect a 1-1 mapping

## Slide 42: Practice Question #1
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
movq (%rax, %rbx), %rcx |  | 
First, determine whether an address is loaded, and if so, which address?

## Slide 43: Practice Question #1
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
movq (%rax, %rbx), %rcx | 0x2020 | 
Second, determine the final value in %rcx

## Slide 44: Practice Question #1
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
movq (%rax, %rbx), %rcx | 0x2020 | 0xE3

## Slide 45: Practice Question #2
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
leaq (%rax, %rbx), %rcx |  | 
First, determine whether an address is loaded, and if so, which address?

## Slide 46: Practice Question #2
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
leaq (%rax, %rbx), %rcx | None | 
Second, determine the final value in %rcx

## Slide 47: Practice Question #2
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x2000 | B5 | B7 | DC | ED | 7D | 59 | 08 | 93
0x2008 | 1D | 23 | 58 | 46 | 9C | 22 | 2F | 5D
0x2010 | C6 | 83 | 75 | 00 | 41 | 19 | 87 | 1C
0x2018 | 24 | 0C | 26 | AA | C7 | BD | 03 | 1E
0x2020 | E3 | 00 | 00 | 00 | 00 | 00 | 00 | 00
0x2028 | 8B | DB | 66 | D7 | 21 | 23 | 6B | 99
Register | Value
%rax | 0x2000
%rbx | 0x20
%rcx | 0x8
Operation | Address Loaded | %rcx Value
leaq (%rax, %rbx), %rcx | None | 0x2020

## Slide 48: Break + Say hi to your neighbors
Things to share
  Name
  Major
  One of the following
    Favorite Candy
    Favorite Pokemon
    Favorite Emoji

## Slide 49: Break + Say hi to your neighbors
Things to share
  Name -Branden
  Major -Electrical and Computer Engineering, and Computer Science
  One of the following
    Favorite Candy - Twix
    Favorite Pokemon - Eevee
    Favorite Emoji - 🍢

## Slide 50: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly

## Slide 51: What can instructions do?
Move data: ✓
Arithmetic: ✓
Transfer control: ✘
  Instead of executing next instruction, go somewhere else
Let’s back out. Why do we want that?
  Sometimes we want to go from the red code to the green code
  But the blue code is what’s next!
  Need to transfer control! Execute an instruction that is not the next one
  And conditionally, too! (i.e., based on a condition)
if (x > y)
result = x-y;
else
result = y-x;
while (x > y)
result = x-y;
return result;

## Slide 52: Condition codes
Control is mediated via Condition codes
  single-bit registers that record answers to questions about values
  E.g., Is value x greater than value y? Are they equal? Is their sum even?
  Let’s keep “question” abstract for now. We’ll see the details in a bit.
  Terminology:
    a bit is set if it is 1
    a bit is cleared (or reset) if it is 0

## Slide 53: Conditionals at the machine level
At machine level, conditional operations are a 2-step process:
  Perform an operation that sets or clears condition codes (ask questions)
  Then observe which condition codes are set, do the operation (or not)
Can express Boolean operations, conditionals, loops, etc.
  We will see the first today, and more control next lecture
So now we need three things:
  Instructions that compare values and set condition codes
  Instructions that observe condition codes and do something (or not)
  A set of actual condition codes (what questions do we track answers to?)

## Slide 54: Two-Step Conditional Process: Boolean Operations
Carnegie Mellon
Lots of new pieces
Lets give an example first, then learn more about each
  Translate C code on right into assembly
  We’ll do this in the next steps
bool gt (int x, int y)
{
return x > y;
}
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when x > y (i.e., %rdi > %rsi)
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 55: Two-Step Conditional Process: Boolean Operations
Carnegie Mellon
Step 1, cmpq: compare quad words
  compare the values in %rsi and %rdi, keep track of all you can learn, and set the relevant condition codes
  Are the two equal? Set the condition codes that records they were equal
  Was the right one greater? Or less? Etc.
  We don’t know yet which answer we are going to need! So just save them all.
bool gt (int x, int y)
{
return x > y;
}
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when x > y (i.e., %rdi > %rsi)
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
y
x

## Slide 56: Two-Step Conditional Process: Boolean Operations
cmpq %rsi, %rdi # Compare x to y
  setg %al # Set when x > y (i.e., %rdi > %rsi)
ret
Carnegie Mellon
Step 2, setX: set destination register to 1 if condition is met
  setg = set if the 2nd operand is greater than the 1st (careful about the order!)
    There’s also setl for less than, etc.
  Reads the condition codes that encodes the answer to that question
  Set the 1-byte register %al to 1 if true
al = (x > y)
y
x
bool gt (int x, int y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 57: Step 1: Setting condition codes
Analogy: Asking ALL the possible questions at once
  And recording the answers
  We don’t know yet which question is the one we care about!
Done in one of two ways
  Implicitly: all* arithmetic instructions set (and reset) condition codes in addition to producing a result
    *except lea; it’s not “officially” an arithmetic instruction
  Explicitly: by instructions whose sole purpose is to set condition codes
    E.g., cmpq
    They don’t actually produce results (in registers or memory)
  Condition codes are left unchanged by other operations (such as mov)

## Slide 58: What are the Condition Codes?
Condition codes on x86
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
  PF Parity Flag
  Not an arbitrary set! By combining them, can keep track of answers to many useful questions! (We’ll see exactly which in a bit.)

## Slide 59: Implicitly Setting Condition Codes
Set (or reset) based on the result of arithmetic operations
  Example: addq Src,Dest # C-analog: t = a+b
  ZF set if t == 0
  SF set if t < 0 (as signed encoding)
  CF set if carry out from most significant bit (unsigned overflow)
      also CF takes the value of the last bit shifted (left or right)
  OF set if twos-complement (signed) overflow (pos/neg overflow) (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
  also, set if a 1-bit shift operation changes the sign of the result
  PF set if t has an even number of 1 bits
CF (Carry) SF (Sign) ZF (Zero) OF (Overflow) PF (Parity)

## Slide 60: Explicitly Setting Condition Codes: Compare
Carnegie Mellon
cmp{b,w,l,q} Src2, Src1
cmpq b,a computes t = a-b, then throws away the result
  And sets condition codes along the way, like subq would!
  Follows the rules we saw on the previous slide for arithmetic instructions
  Beware the order of the cmp operands!
Use cases
  ZF set if a == b
  SF set if (a-b) < 0 (as signed), i.e., b > a in a signed comparison!
  CF and OF used mostly in combinations with others (see in a few slides)

## Slide 61: Explicitly Setting Condition Codes: Test
Carnegie Mellon
test{b,w,l,q} Src2,Src1
testq b,a computes t = a&b, then throws away the result!
  And sets condition codes like andq would (order doesn’t matter here)
  So again, same rules as arithmetic instructions
Use cases
  ZF set when a&b == 0, i.e., a and b have no bits in common
  SF set when a&b < 0
Useful when doing bit masking
  E.g., x & 0x1, to know whether x is even or odd
  If the result of the & is 0, it’s even, if 1, it’s odd

## Slide 62: Step 2: Reading Condition Codes
Carnegie Mellon
Cannot read condition codes directly; instead observe via instructions
  And generally observe combinations of condition codes, not individual ones
Example: the setX family of instructions
  Write single-byte destination register based on combinations of condition codes
    set{e, ne, s, …} D where D is a 1-byte register
    Example: sete %al
      Means: %al=1 if flag ZF is set, %al=0 otherwise

## Slide 63: Using condition codes for comparison
setle – Less than or equal (signed)
  Combination of condition codes: (SF^OF)|ZF
  SF - Sign Flag (true if negative)
  OF – Overflow Flag (true if signed overflow occurred)
  ZF – Zero Flag (true if result is zero)
All of the combos expect to be run after a cmp src,dst
  dst <= src (runs dst-src)
    If:
      The result is zero – src and dst were equal
    OR if one but not both:
      The result is negative (and didn’t overflow) – src was larger than dst
      The result overflowed (and is positive) – dst is negative, src is positive

## Slide 64: Condition codes combinations
Carnegie Mellon
SetX | Description | Condition
sete | Equal / Zero | ZF
setne | Not Equal / Not Zero | ~ZF
sets | Negative | SF
setns | Nonnegative | ~SF
setg | Greater (Signed) | ~(SF^OF)&~ZF
setge | Greater or Equal (Signed) | ~(SF^OF)
setl | Less (Signed) | (SF^OF)
setle | Less or Equal (Signed) | (SF^OF)¦ZF
seta | Above (unsigned) | ~CF&~ZF
setb | Below (unsigned) | CF
  Note: suffixes do not
  indicate operand sizes,
  but rather conditions
  These same suffixes
  will come back when we see other instructions
  that read condition codes.
  Expect to be run after a cmp

## Slide 65: Step 2: Reading Condition Codes
setX (and others) read the current state of condition codes
  Whatever it is, and whichever instruction changed it last
So when you see (for example) setne, work backwards!
  Look at previous instructions, to find the last one to change conditions
  Then you’ll know the two values that were compared
  Ignore instructions that don’t touch condition codes (like moves)
Usually you’ll see a cmpX (or testX, or arithmetic) right before
  But not always, so know what to do in general

## Slide 66: What do you need to know?
90%+ of the time
  cmp instruction followed by setX instruction (or a jump, next lecture)
  Don’t have to think about condition codes at all!
  Think of as dst X src
    dst <= src or dst != src etc.
10% or less of the time
  Arbitrary arithmetic instruction sets the condition codes
    Or testq sets the condition codes
  Followed by a setX or branch (next lecture)
  And you actually have to think about which condition codes are set to figure out what the assembly is doing, which can be challenging

## Slide 67: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly

## Slide 68: How to Get Your Hands on Assembly
From C source code, using a compiler
  gcc –O1 -S sum.c
    Produces file sum.s
  Warning: May get very different results on different machines due to different versions of gcc and different compiler settings
C Code: sum.c
long plus(long x, long y);
void sum(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 assembly: sum.s
sum:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret

## Slide 69: How to Get Your Hands on Assembly
From machine code, using a disassembler
  objdump -d sum.o
  Within the gdb Debugger
  linux> gdb prog
  (gdb) disassemble sum
    gdb tutorial coming soon!
  Warning: Disassemblers are approximate; some information is lost during translation from assembly to machine code
    Label names are lost, what is just data (vs code) is lost, etc.
  Useful if you don’t have the source
0000000000400595 <sum>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 70: Godbolt
Ignore section labeled: “_dl_relocate_static_pie”
Play around with this to try stuff on your own
https://godbolt.org/

## Slide 71
Godbolt example!

## Slide 72: Outline
Arithmetic Instructions
Special Cases
  Non 64-bit Data
  Load Effective Address
Condition Codes
Viewing x86-64 Assembly