## Slide 1: Lecture 12 Memory Hierarchy
CS213 – Intro to Computer Systems
Branden Ghena – Spring 2021
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Reminder: office hours
  Course staff is amazing!!
  Can help with topics as well as assignments
Get started on Homework 3
And on Attack Lab

## Slide 3: Changing the focus of CS213
So far in class we’ve focused on how computers do things
  Represent data
  Run instructions
Now we’re focusing on how to improve those things
  Secure (last lecture plus some stuff in two weeks)
  Efficient (today and next week
As we’ll show today, the most important thing to speed up is memory
  It is possible and hardware does so already
  Software can be designed to take advantage of this

## Slide 4: Today’s Goals
Explore the memory systems available in modern computers
  Understand capabilities and limitations of each
Discuss the memory hierarchy
  How it improves performance through caching
Describe software patterns that caching is designed to support

## Slide 5: Outline
Technologies and Trends
Memory Hierarchy
Locality of Reference

## Slide 6: Storage in a Computer System
Data can be stored in different places
  Registers, caches, memory, disk, etc.
  Caches are temporary storage in processor used to speed up memory access
Hugely different characteristics
  Storage size
    x86-64: 16 registers. 128 B total (not including FP registers, etc.)
    Memory is measured in GB, disks in TB
  Latency (i.e., time to access data)
    Registers are really fast, memory less so, disk is incredibly slow
  Cost per byte
    Registers are really expensive, disks are really cheap, memory somewhere in the middle
Each serves a different purpose in a system
  Can design systems to get the best of all worlds (in most cases)

## Slide 7: Computing timescales
Assuming 4 GHz processor, Instruction (with registers): 0.25 ns
Jeff Dean (Google AI): “Numbers Everyone Should Know”

## Slide 8: Jim Gray’s storage latency analogy
How “far” is data for the CPU, converted to human scale
Storage
Distance
Time
Registers
On-chip cache
On-board cache
Main memory
Disk
Tape
In my apartment
Across the street
A few blocks away
In Milwaukee
On Mars
On Kepler-76b
1 minute
2-4 minutes
10 minutes
1.5 hours
2 years
2000 years (at speed of light)
Jim Gray
Turing Award 1998

## Slide 9: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus

## Slide 10: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Registers and Caches

## Slide 11: Register storage
x86-64
  16 registers (general-purpose) with 8 bytes each
  32 registers (special-purpose) with up to 64 bytes each
  Plus some other odds and ends (%rip, flags, segments, etc.)
128 bytes for general purpose registers
Order 1-2 kB for everything
Accesses are very fast. Within a single cycle

## Slide 12: Register technology: SRAM
Static RAM (SRAM)
  Each cell stores a bit in a bi-stable circuit, typically a six-transistor circuit
  Static – no need for periodic refreshing; keeps data while powered
  Relatively insensitive to disturbances such as electrical noise
    Energetic particles (alpha particles, cosmic rays) can flip stored bits
Fastest memory on computer
  Also most expensive and takes up most space per bit
  Typically used for registers and cache memories

## Slide 13: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
RAM

## Slide 14: Main memory
The “RAM” in your computer
  Random Access Memory
  Can access any byte you want in “random” order
Typically measured in GB
  1-128 GB
  Some special purpose systems may have MUCH less
This is the “array of bytes” we’ve been using in assembly

## Slide 15: Main memory technology: DRAM
Dynamic RAM (DRAM)
  Each cell stores a bit as a charge in a capacitor
  Capacitors lose charge; each cell must be refreshed every 10-100 ms
  More sensitive to disturbances (EMI, radiation, …) than SRAM
Slower than SRAM, but cheaper and denser
  ~100x slower than registers
Typically used for main memory

## Slide 16: Accessing DRAM
Read entire row of data at a time
  Large in practice, kilobytes
Select actual bytes that are wanted
  Possibly modifying those bits
Write row back to memory
  Must always happen!
  Reading is destructive

## Slide 17: Connecting main memory and the processor
Data flows between main memory and processor over buses
  A collection of parallel wires that carry address, data, and control signals
  Typically shared by multiple devices
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
memory bus
Includes memory controller
movl A, %eax (load)
Processor writes address A to the bus
Memory writes data to the bus
Processor reads data from the bus
movl %eax, A (store)
Processor writes address A to the bus
Processor writes data to the bus
Memory reads data from the bus
system bus

## Slide 18: Sidebar: memory security is important
Data in RAM disappears without power
  But the rate depends on temperature, minutes to decay if frozen
  Cold Boot Attack: freeze RAM to remove from computer and steal contents

## Slide 19: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Disk: Hard drive or SSD

## Slide 20: Disk storage
Workhorse storage devices
  Terabytes in size in modern computers
  Milliseconds to read
    100,000x longer than reading from DRAM
    10,000,000x longer than reading from SRAM
IBM 350 Disk Storage Unit
First disk drive, 1956
WD Red 6TB NAS, 2015
101.6mm
146.99mm
Storage?
5MB!
Basic mechanisms the same!

## Slide 21: Disk types

## Slide 22: Hard disk drive operation
The disk surface
spins at a fixed
rotational rate
(5400-15000 RPM)
spindle
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 23: Accessing data on disk
Three-step process
  Read head needs to move to the right cylinder: seek time
  Platter turns until start of sector under the read head: rotational latency
  Sector passes under read head and data is read: transfer time
Time cost dominated by seek time and rotational latency
  Consequence: reading first bit of a sector is expensive
  But reading the rest of the sector is basically free!
When using disks, best to favor large sequential reads/writes
  Terrible for random access! (reading a little bit here, a little bit there)
  But overall still really slow compared to main memory or registers

## Slide 24: Solid State Drives (SSDs)
Flash memory
  Just like Flash Drives
Pages: 2KB to 512KB, Blocks: 32 to 128 pages
Data read/written in units of pages
Page can be written only after its block has been erased
  Need to copy rest of the data to not lose it. Expensive!
A block wears out after repeated writes (10k – 100k writes) and can no longer be used
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
Notes: SSD based on flash memory (non-volatile memory based on EEPROM – electrically erasable programmable ROM)
Plugs into a standard disk slot – typically USB or SATA
Made of a few chips and a flash translation layer, a hw/firmware piece similar to a disk controller

## Slide 25: SSDs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    Order petabyte (1015 bytes) of random writes before they wear out
  More expensive per byte (but getting cheaper)
    2021: HDD $0.02 per GB, SSD $0.09 per GB
Applications
  Portable electronics (phones, tablets, etc.)
  Began to appear in desktops and servers circa 2007
  Now common on laptops as well
Biggest speed improvement to your computer:
Get an SSD

## Slide 26: Reading memory from disk
Data from disk is always read into Main Memory
Direct Memory Access (DMA)
  Processor starts a read and then returns to programs
  Disk performs the read, transfers data, then notifies processor when done
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface

## Slide 27: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus

## Slide 28: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works

## Slide 29: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works
  Secretly make it larger than it claims to be
    e.g. 200 GB when it claims to be 100 GB
  Behind the scenes move around memory as necessary so the device can still hold 100 GB even if half of the flash is
    Maintain a mapping of which data is located where

## Slide 30: Outline
Technologies and Trends
Memory Hierarchy
Locality of Reference

## Slide 31: The CPU-Memory gap
Increasing gap between DRAM, disk, and CPU speeds.
SRAM roughly keeping up
DRAM, disk and CPU
performance gap widening
Split reflects the introduction of multicores
Disk
DRAM
CPU
SSD
SRAM
Notes: In early 21st century computer manufacturers discover they couldn’t keep increasing CPU clock freq. because chips would consume too much power; answer was multicore – there you see the cycle times getting slower but effective cycle times keeping about the same improvement rate

## Slide 32: The CPU-Memory Gap
CPUs outspeed memory
  But they can’t compute on data they don’t have!
  If the CPU has to wait for data to reach it, it just sits idle!
    All these GHz don’t look so useful anymore, do they?
Challenge: get data to the CPU despite “slow” memory
  So the CPU can work at full speed, without waiting for data
Two-pronged strategy
  Memory hierarchy: keep data we need closer to the CPU
  Locality of reference: predict which data we’re likely to need

## Slide 33: Memory hierarchy
Some fundamental and enduring properties of systems
  The faster the storage, the more expensive ($) it is
  The faster the storage, the smaller (capacity) it is
  The gap between processor and main memory speed is widening
Key idea: keep the data you need the most in fast memory!
  Data you only need from time to time can be in slow memory, no big deal
  Most used data goes in registers
  Least used data goes to disk
Analogy: kitchen ingredients I use
  Salt, all the time: it sits out on the counter
  Oregano, frequently: front of the cabinet
  Onion powder, occasionally: back of the cabinet
  Brown sugar, sometimes: somewhere in the pantry
  Saffron, never: I can go buy some if I do need it

## Slide 34: Memory hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
Main memory holds disk
blocks retrieved from local
disks.
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from main memory.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 35: Caching, general principle
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device
  Data lives in both places (typically)
  When the consumer (e.g., CPU) reads the data, it gets it from the smaller, faster storage
  If the data we want is not in the cache, we pay the full cost of bringing it over from the larger, slower storage into the smaller, faster storage
    The hope: we don’t need to do it too often
Fundamental idea in systems. Shows up all over!
  Memory hierarchies
  Content delivery networks (CDNs) on the Internet (Akamai, Cloudflare, etc.)

## Slide 36: Caching in a memory hierarchy
Fundamental idea of a memory hierarchy
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1
    L2 cache memory as a cache for main memory
    Main memory as a cache for disk, etc.
  Each level stores some of the most frequently accessed data
  The closer the cache is to the processor, the “hotter” the cached data

## Slide 37: Memory hierarchies make memory fast and large
Why do memory hierarchies work?
  Programs tend to access the data at level k more often than they access the data at level k+1
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit
Net effect:
  A large pool of memory that costs as little as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top
  Best of both worlds!

## Slide 38: Caching in a memory hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
Blocks cannot be stored in an arbitrary location!
They can only live at one of a fixed set of locations.
In this example: they must be in the same “column” for both levels.

## Slide 39: General caching concepts
Request
14
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
14
4*
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14

## Slide 40: General caching concepts
12
Request
12
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14
Cache miss
  b is not at level k, so the level k cache must fetch it from level k+1, e.g., block 12
  If the level-k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Here, we pick 4; same column as 12
    4 is “dirty”, need to write back to k+1
    More on this next lecture
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
12
4*
Request
12
4*
4*
12
12
“ * ” means the block is dirty (i.e., it has been modified)

## Slide 41: Cache Misses Taxonomy
Cold (compulsory) miss
  Cold misses occur when a block is accessed for the first time
  No one ever accessed it, so there wasn’t any reason to bring it into cache
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
  There’s no way the working set can all fit in the cache, so there will be misses
Conflict miss
  In most caches, blocks cannot be stored in any available slot
  If two blocks need to go in the same slot, need to evict the old one to store the new!
  If after that, we need to access the old block, conflict miss!
    We had a conflict, evicted a block, and now we miss trying to access that block
  Note: can happen even when there is “room” elsewhere in the cache!

## Slide 42: Break + Video
How do you remember which cache miss is which?
  Mr. Bean can help you tell the difference! (video)

## Slide 43: Outline
Technologies and Trends
Memory Hierarchy
Locality of Reference

## Slide 44: Locality
Goal: predict which data the CPU will want to access
  So we can bring it to (and keep it in!) fast memory
  Problem: memory is huge! (billions of bytes) how do you decide which to save?
Principle of Locality
  Programs tend to reuse/use data items recently used or nearby those recently used
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time

## Slide 45: Types of locality practice
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time
Quiz: what kind of locality?
  Data
    Reference array elements in succession:
    Reference sum each iteration:
  Instructions
    Execute instructions in sequence:
    Cycle through loop repeatedly:
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Spatial locality
Temporal locality
Temporal locality

## Slide 46: Locality example
Can get a sense for whether a function has good locality just by looking at its memory access patterns
Does this function have good locality?
Yes!
  Array is accessed in same row-major order in which it is stored in memory
  a through a+3 , a+4 through a+7, a+8 through a+11, etc.
int sumarrayrows(int a[M][N]){
int sum = 0;
for (int i = 0; i < M; i++) {
for (int j = 0; j < N; j++) {
sum += a[i][j];
}
}
return sum;
}
Temporal or spatial locality?
Spatial: accesses to array
Temporal: accesses to sum
Notes: sum: both
a: mostly spatial
loop body instructions: both

## Slide 47: Locality example
Does this function have good locality?
No!
  Scans array column-wise instead of row-wise
  a through a+3, then a+4*N through a+4*N+3, etc.
  Holy jumping around memory Batman!
More on that in a couple of lectures
int sumarraycols(int a[M][N]){
int sum = 0;
for (int j = 0; j < N; j++) {
for (int i = 0; i < M; i++) {
sum += a[i][j];
}
}
return sum;
}
Notes: sum: both
instructions: both
a: nope!

## Slide 48: Locality to the Rescue!
How can we exploit locality to bridge the CPU-memory gap?
  Use it to determine which data to put in a cache!
Spatial locality
  When level k needs a byte from level k+1, don’t just bring one byte
  Bring neighboring bytes as well!
  Good chances we’ll need them too in the near future
Temporal locality
  When you bring something into the cache, try to keep it there
  Good chances we’ll need it again in the near future
Result: most accesses should be cache hits!
  Memory system: size of largest memory, with speed close to that of fastest memory
We’ll see how that works in detail next time

## Slide 49: Outline
Technologies and Trends
Memory Hierarchy
Locality of Reference