## Slide 1: Lecture 08 Procedures
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2022
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Homework 2 due today
  Good practice for the exam
  With slip days, not sure when I can post solutions
Midterm Exam 1 Tuesday, during class
  I have already contacted you if you’re at a different time
  Covers material including Tuesday (Control Flow in Assembly)
    Not today’s material
  80 minutes to complete (starts at 9:35am sharp)
    Bring a pencil!
    Bring one 8.5x11 inch sheet of paper with notes on front and back

## Slide 3: Today’s Goals
Describe C memory layout
Explore functions in assembly
  How do we call them and return from them?
  How do we create local variables?
Understand how we manage register use between functions

## Slide 4: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 5: C memory layout
Stack Section
  Local variables
  Function arguments
Heap Section
  Memory granted through malloc()
Static Section (a.k.a. Data Section)
  Global variables
  Static function variables
Text Section (a.k.a Code Section)
  Program code
Stack
Heap
Static
Text
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF

## Slide 6: C memory layout
char glob_str[80] = {0};
void func(short b, int* d) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 7: C memory layout
char glob_str[80] = {0};
void func(short b, int* d) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 8: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 9: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 10: C memory layout
char glob_str[80] = {0};
void func(short b, int* d) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 11: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 12: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 13: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 14: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 15: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text

## Slide 16: C memory layout
char glob_str[80] = {0};
void func(short b, int* f) {
static int c = 3;
char* d = “Test”;
int* e = malloc(sizeof(int));
printf(“Hello CS213\n”);
}
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF
Stack
Heap
Static
Text
Assembly code goes in the Text section

## Slide 17: Interacting with data sections in assembly
Stack
  Stack pointer is saved in %rsp and can be moved as needed
  We’ll discuss this today
Heap
  C library (malloc) handles this above the machine level
  i.e. from the machine point of view, there is no heap
Static
  Arbitrary pointers to memory can be created and used
    With memory addressing instructions
  Assembly directive can place values into Static section
Text
  Assembly code is placed here automatically
  Labels are just addresses within the Text section

## Slide 18: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 19: Mechanisms in Procedures
Passing control
  To beginning of procedure code
  Back to return point
Passing data
  Procedure arguments
  Return value
Local memory management
  Allocate during procedure execution
  Deallocate upon return
No one instruction does all that
  Need instructions for each
The stack is the key to all 3 of these!
P(…) {
•
•
y = foo(x);
z = y+1;
•
}
int foo(int i)
{
int t = 3*i;
int v[10];
•
•
return v[t];
}

## Slide 20: Procedure control flow
Use stack to support procedure call and return!
Procedure call
  callq label Push return address on stack; jump to label
Procedure return retq Pop address from stack; jump there (stack should be as it was when the call began)
  Return value is in %rax
Return address value
  Address of instruction immediately following callq
  Example from disassembly
  400544: call 400550 <mult2>
  400549: mov %rax,(%rbx)
Return address: 0x400549
If you don’t know where
you’re going, you may
not get there.
— Yogi Berra
Just call and ret are fine, the q is assumed (there is no other option)

## Slide 21: Code Examples
long mult2 (long a, long b){
long s = a * b;
return s;
}
void multstore(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
... (we’ll fill the start in soon)
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Store at address dest
... (we’ll fill the end in soon too)
40054d: retq # Return

## Slide 22: Control Flow Example about to execute callq
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip
Next instruction
to execute

## Slide 23: Control Flow Example callq step 1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip
0x400544
Next instruction
to execute

## Slide 24: Control Flow Example callq step 2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rip
%rsp
0x120
0x128
0x130
0x118
Next instruction
to execute

## Slide 25: Control Flow Example about to execute retq
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip
Next instruction
to execute
QUIZ: What is the address of the instruction we execute after retq?

## Slide 26: Control Flow Example retq step 1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip
Next instruction
to execute

## Slide 27: Control Flow Example retq step 2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip
Next instruction
to execute

## Slide 28: Function data flow
First 6 arguments are in registers
  %rdi is first argument
Next n arguments are on the stack
  This means more arguments is slower
Return value is in %rax
Registers
Stack
(Only allocate stack space when needed)
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •
top

## Slide 29: Data Flow Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore (long x, long y, long *dest){
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
# a in %rdi, b in %rsi
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
# s in %rax
400557: retq # Return
0000000000400540 <multstore>:
# x in %rdi, y in %rsi, dest in %rdx
• • •
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
# t in %rax
400549: mov %rax,(%rbx) # *dest = t
• • •

## Slide 30: Break + Open Question
How did we decide how many registers to use for arguments and return values?
Do all functions have to use this same convention?
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax

## Slide 31: Break + Open Question
How did we decide how many registers to use for arguments and return values?
  Testing lots of real-world programs
  Many style guides suggest you use four or less arguments
  x86 (32-bit) only had four arguments
    x86-64 added two more
  C only has one return result, so one register is fine
Do all functions have to use this same convention?
  All functions within a program must, or they won’t work
  Different programs, or different OSes, could choose different
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax

## Slide 32: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 33: Call-Local State
Need some place to store state for each call
  Return address
  Arguments
  Local variables
  Temporary space (if needed)
Note: these are separate for each call, not each function
  Function could be called recursively, but each needs its own local variables
State only needs to exist until the function returns

## Slide 34: Using the Stack for Call-Local State
Place local state on the stack
Stack discipline
  That state is only needed for limited time
    Starts when function is called; ends when it returns
  Callee returns before caller does
    Callee: for a specific call, the function being called
    Caller: for a specific call, the function calling the other
Stack allocated in Frames
  Frame = State for a single procedure invocation
  Allocated by “setup” code at the start of function
  Deallocated by “teardown” code before returning
Stack Pointer: %rsp
Stack “Top”
Previous Frame
Current Frame

## Slide 35: Call Chain Example
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI(2);
• • •
amI(0);
• • •
}
amI(int x)
{
•
if(x)
amI(x-1);
•
•
}
yo
who
amI(2)
amI(1)
amI(0)
Example
Call Chain
amI(0)
Procedure amI() is recursive

## Slide 36: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
Call Chain
yo(…)
{
•
•
who();
•
•
}

## Slide 37: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI(2);
• • •
amI(0);
• • •
}

## Slide 38: Example
yo
who
amI
amI
amI
amI
yoo
Stack
yo
who
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
if(x)
amI(x-1);
•
•
}
%rsp

## Slide 39: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
amI
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
if(x)
amI(x-1);
•
•
}

## Slide 40: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
amI
amI
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
if(x)
amI(x-1);
•
•
}

## Slide 41: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
amI
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
•
amI();
•
•
}
amI(…)
{
•
if (x)
amI(x-1);
•
•
}

## Slide 42: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
if(x)
amI(x-1);
•
•
}

## Slide 43: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI(2);
• • •
amI(0);
• • •
}

## Slide 44: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
amI
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI();
• • •
amI();
• • •
}
amI(…)
{
•
if(x)
amI(x-1);
•
•
}

## Slide 45: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
who
yo(…)
{
•
•
who();
•
•
}
who(…)
{
• • •
amI(2);
• • •
amI(0);
• • •
}

## Slide 46: Example
yo
who
amI
amI
amI
amI
yoo
%rsp
Stack
yo
yo(…)
{
•
•
who();
•
•
}

## Slide 47: x86-64/Linux Stack Frame
Current Stack Frame (“Top” to Bottom)
  “Argument build”: Arguments for function we’re about to call
  Local variables If we can’t keep them in registers (too many, or if must be in memory)
  Saved register context (we’ll get to that soon)
Caller Stack Frame
  Return address
    Pushed by call instruction
  Arguments for this call
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Arguments 7+
Caller
Frame
Stack pointer
%rsp
Current
(Callee)
Frame

## Slide 48: Example: incr
long incr(long* p, long val) {
long x = *p;
long y = x + val;
*p = y;
return x;
}
incr:
movq (%rdi), %rax # x = *p
addq %rax, %rsi # y = x+val
movq %rsi, (%rdi) # *p = y
ret
Register | Use(s)
%rdi | Argument p
%rsi | Argument val, also y
%rax | x, Return value
x
...
Memory
...
%rdi
x+val
...
...
%rdi

## Slide 49: Example: Calling incr #1 (local variables)
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
%rsp
Resulting Stack Structure
. . .
Rtn address

## Slide 50: Example: Calling incr #1 (local variables)
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Stack pointer must be multiple of 16
We take v1’s address, so must be in memory

## Slide 51: Example: Calling incr #2 (argument build)
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 52: Example: Calling incr #3 (control transfer)
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
15213
Unused
%rsp+8
Stack Structure
. . .
Rtn address
%rsp+16
RetAddr
%rsp
Register | Use(s)
%rdi | &v1
%rsi | 3000

## Slide 53: Example: executing incr
long incr(long *p, long val) {
long x = *p;
long y = x + val;
*p = y;
return x;
}
incr:
movq (%rdi), %rax
addq %rax, %rsi
movq %rsi, (%rdi)
ret
Register | Use(s)
%rdi | Argument p
%rsi | Argument val (3000)
%rax | ...
15213
...
Memory
...
%rdi
18213
...
...
%rdi
Register | Use(s)
%rdi | Argument p
%rsi | 18213
%rax | 15213 (return value)

## Slide 54: Example: right after executing incr
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rdi | &v1
%rsi | 18213
%rax | 15213
QUIZ: where do we find
the return value of incr?

## Slide 55: Example: Calling incr #4 (cleanup)
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
18213
Unused
%rsp
Previous stack Structure
. . .
Rtn address
%rsp+8
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address

## Slide 56: Example: Calling incr #5
call_incr:
subq $16, %rsp
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq 8(%rsp), %rax
addq $16, %rsp
ret
long call_incr() {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return v1+v2;
}
Register | Use(s)
%rax | Return value
%rsp
Updated Stack Structure
. . .
Rtn address
%rsp
Final Stack Structure
. . .

## Slide 57: Break + Open Questions
What are the initial values of variables created on the stack?
Is there a limit to how many local variables a function can have?
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Arguments 7+
Caller
Frame
Stack pointer
%rsp
Current
(Callee)
Frame

## Slide 58: Break + Open Questions
What are the initial values of variables created on the stack?
  Undefined behavior in C (compiler chooses)
  Machine just creates a variable in the stack
    Initial value is whatever was there before
Is there a limit to how many local variables a function can have?
  Based on memory limit of the process
  Stack keeps growing until it runs out of space
    OS can do lots of tricks to give it more memory
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Arguments 7+
Caller
Frame
Stack pointer
%rsp
Current
(Callee)
Frame

## Slide 59: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 60: Register Saving
Can a function use %rdx for temporary storage?
  Contents of register %rdx overwritten by who!
  This could be trouble → something should be done!
    Need some coordination
yo:
• • •
movq $15213, %rdx
call who
addq %rdx, %rax
• • •
ret
who:
• • •
subq $18213, %rdx
• • •
ret
Caller
Callee

## Slide 61: Reusing registers
Problem: registers are shared between functions
  Callee could overwrite caller’s registers by accident
How does each function know which registers are safe to use?
Solution:
  Save original register value to stack
  Use register as needed
  Restore original register value from stack
  New question: when should the saving happen? In advance or on demand?

## Slide 62: Saving registers in advance
New question: who should save the registers, Caller or Callee?
Attempt 1: Save everything in advance
  Caller knows which registers it is using
  Save all registers it is going to need after the call
  Downside: Caller doesn’t know what Callee needs
    Wasted stores to memory if Callee doesn’t need those registers

## Slide 63: Saving registers on demand
New question: who should save the registers, Caller or Callee?
Attempt 2: Save everything on demand
  Callee knows which registers it is using
  Save all registers it is going to use at the start of the function
  Downside: Callee doesn’t know what Caller was using
    Wasted stores to memory if Caller wasn’t using those registers

## Slide 64: Compromise: some registers in advance, some on demand
Neither the Caller nor the Callee has perfect knowledge of register availability
Designate based on register which are saved when
  Some are saved in advance: Caller saved
  Some are saved on demand: Callee saved
Remember: Caller and Callee are just designations for one call event
  Functions can and do act as both at different times

## Slide 65: x86-64 Linux Register Usage #1 (caller-saved, in advance)
%rax
  Return value
  Caller-saved
  Will be modified by function we’re about to call
%rdi, ..., %r9
  Arguments
  Caller-saved
  Can be modified by function we’re about to call
  If more than 6 arguments, then pass the rest on the stack
%r10, %r11
  Caller-saved
  Can be modified by function we’re about to call
%rax
%rdx
%rcx
Return value
(caller-saved)
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
(caller-saved)
Caller-saved
temporaries

## Slide 66: x86-64 Linux Register Usage #2 (callee-saved, on demand)
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rsp
  Special form of callee-saved
  Restored to original value upon exit from procedure
    Stack frame is removed
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14
%r15

## Slide 67: x86-64 Integer Registers: Usage Conventions
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rsp
%rbp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
Callee saved
Callee saved
Callee saved
Callee saved
Callee saved
Caller saved
Callee saved
Stack pointer
Caller Saved
Return value
Argument #4
Argument #1
Argument #3
Argument #2
Argument #6
Argument #5
Callee saved
Caller Saved
In advance
On demand

## Slide 68: Push and Pop instructions
Example:
  %rax = 0x123, %rdx = 0x0, %rsp = 0x108
  pushq %rax
  popq %rdx
Remember, stack is just memory
  Can also use memory moves and modify %rsp manually!
Stack “top”
Stack “bottom”
0x108
Stack “top”
0x100
%rdx = 0x123;
%rsp = 0x100
%rsp = 0x108
Increasing memory address
0x123
Instruction | Effect | Description
pushq S | R [%rsp] ← R [%rsp] – 8; M [ R[%rsp] ] ← S | Store S onto the stack
popq D | D ← M [ R[%rsp] ] R [%rsp] ← R [%rsp] + 8; | Retrieve D from the stack

## Slide 69: Register Saving Example #1
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
Someone called us
We’re the callee
Save %rbx
Still need x after the call!
%rbx is callee-save (on demand)

## Slide 70: Register Saving Example #2
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movq $3000, %rsi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Pre-return Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx
Our caller can
expect its own
value in %rbx
Restore it!
%rbx is callee-save (on demand)

## Slide 71: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 72: Recursive Function
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Note: rep instruction inserted as no-op. You can ignore it.
Notes: we see that the procedure ends with the instruction combination rep; ret, rather than simply ret. Looking at the Intel and AMD documentation for the rep instruction, we see that it is normally used to implement a repeating string operation [3, 6]. It seems completely inappropriate here. The answer to this puzzle can be seen in AMD’s guidelines to compiler writers [1]. They recommend this particular combination to avoid making the ret instruction be the target of a conditional jump instruction. This is the case here, because it is preceded by a a jg instruction, and in the event the jump condition does not hold, the program “falls through” to the return. According to AMD, the processor does a better job predicting the outcome of the branch if it does not have a ret instruction as a target. This rep instruction will have no effect, since it is not followed by a string manipulation instruction. Its only purpose is to serve as a branch target. End Aside.
rep; nop is indeed the same as the pause instruction (opcode F390). It might be used for assemblers which don't support the pause instruction yet. On previous processors, this was simply did nothing, just like nop but in two bytes. On new processors which support hyperthreading, it is used as a hint to the processor that you are executing a spinloop to increase performance. From Intel's instruction reference: Improves the performance of spin-wait loops. When executing a “spin-wait loop,” a Pentium 4 or Intel Xeon processor suffers a severe performance penalty when exiting the loop because it detects a possible memory order violation. The PAUSE instruction provides a hint to the processor that the code sequence is a spin-wait loop. The processor uses this hint to avoid the memory order violation in most situations, which greatly improves processor performance. For this reason, it is recommended that a PAUSE instruction be placed in all spin-wait loops.

## Slide 73: Recursive Function Base Case
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rax | Return value | Return value

## Slide 74: Recursive Function Register Save
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x | Argument
%rsp
. . .
Rtn address
Saved %rbx

## Slide 75: Recursive Function Call Setup
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rdi | x >> 1 | Rec. argument
%rbx | x & 1 | Callee-saved

## Slide 76: Recursive Function Call
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Recursive call return value | 

## Slide 77: Recursive Function Result
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rbx | x & 1 | Callee-saved
%rax | Return value | 

## Slide 78: Recursive Function Completion
/* Recursive popcount */
long pcount_r(unsigned long x) {
if (x == 0)
return 0;
else
return (x & 1)
+ pcount_r(x >> 1);
}
pcount_r:
movq $0, %rax
testq %rdi, %rdi
je .L6
pushq %rbx
movq %rdi, %rbx
andq $1, %rbx
shrq %rdi # (by 1)
callq pcount_r
addq %rbx, %rax
popq %rbx
.L6:
rep; ret
Register | Use(s) | Type
%rax | Return value | Return value
%rsp
. . .

## Slide 79: Example three recursions in
. . .
Rtn address
Saved %rbx
Rtn address
Saved %rbx
%rsp
Rtn address
Saved %rbx
main()
pcount_r()
pcount_r()
pcount_r()
Executing, but has not yet called pcount_r() again

## Slide 80: x86-64 Procedure Summary
Important Points
  A stack is the right data structure for procedure call / return
    If P calls Q, then Q returns before P
  The stack makes recursion work
Calling convention
  Caller-saved registers saved in advance before call
  Put arguments in registers (1-6)
  Put further arguments on top of stack (7+)
  Put return address on top of stack
  Callee can safely store values in local stack frame and in callee-saved registers (after saving them)
  Result return in %rax and restore callee-saved registers before returning
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Arguments 7+
Caller
Frame
Stack pointer
%rsp
Current
(Callee)
Frame

## Slide 81: Outline
C Code Layout
x86-64 Calling Convention
Managing Local Data
Register Saving
  Recursion Example

## Slide 82: Outline
Bonus: Stack Frame Example

## Slide 83: x86-64 Stack Frame Example
Keeps values of &a[i] and &a[i+1] in callee-save registers
Must set up stack frame to save these registers
long sum = 0;
/* Swap a[i] & a[i+1] */
void swap_ele_su(long a[], int i)
{
swap(&a[i], &a[i+1]);
sum += (a[i]*a[i+1]);
}
swap_ele_su:
movq %rbx, -16(%rsp)
movq %rbp, -8(%rsp)
subq $16, %rsp
movslq %esi,%rax
leaq 8(%rdi,%rax,8), %rbx
leaq (%rdi,%rax,8), %rbp
movq %rbx, %rsi
movq %rbp, %rdi
call swap
movq (%rbx), %rax
imulq (%rbp), %rax
addq %rax, sum(%rip)
movq (%rsp), %rbx
movq 8(%rsp), %rbp
addq $16, %rsp
ret

## Slide 84: Understanding x86-64 Stack Frame
swap_ele_su:
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
movslq %esi,%rax # Extend i
leaq 8(%rdi,%rax,8), %rbx # &a[i+1] (callee save)
leaq (%rdi,%rax,8), %rbp # &a[i] (callee save)
movq %rbx, %rsi # 2nd argument
movq %rbp, %rdi # 1st argument
call swap
movq (%rbx), %rax # Get a[i+1]
imulq (%rbp), %rax # Multiply by a[i]
addq %rax, sum(%rip) # Add to sum
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame
ret

## Slide 85: Understanding x86-64 Stack Frame
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
rtn addr
%rsp
  
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame

## Slide 86: Understanding x86-64 Stack Frame
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
rtn addr
%rsp
−8
%rbx
−16
  
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame

## Slide 87: Understanding x86-64 Stack Frame
rtn addr
%rbp
%rsp
−8
%rbx
−16
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
  
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame

## Slide 88: Understanding x86-64 Stack Frame
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
  
rtn addr
%rbp
%rsp
+8
%rbx
rtn addr
%rbp
%rsp
−8
%rbx
−16
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame

## Slide 89: Understanding x86-64 Stack Frame
movq %rbx, -16(%rsp) # Save %rbx
movq %rbp, -8(%rsp) # Save %rbp
subq $16, %rsp # Allocate stack frame
movq (%rsp), %rbx # Restore %rbx
movq 8(%rsp), %rbp # Restore %rbp
addq $16, %rsp # Deallocate frame
  
rtn addr
%rbp
%rsp
+8
%rbx
rtn addr
%rbp
%rsp
−8
%rbx
−16
rtn addr
%rsp