## Slide 1: Lecture 10 Structured Data
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2022
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Remember: drop deadline is Friday
  Please come by office hours if you’re concerned and want to talk
  Or email me and I can schedule a meeting whenever
  If I’m worried at all, I reached out to you
    So if you didn’t get an email, you’re doing fine

## Slide 3: Administrivia
Bomb Lab due on Thursday (2/10)
  Keep up the hard work on it!
  Remember, it’s tricky, but not trying to trick you
    You can trust function names to roughly do what they say
New assignments will be released on Thursday/Friday

## Slide 4: Today’s Goals
Wrap up x86-64 assembly!
  Discuss how structures are accessed
Memory layout details
  Explore details about how structure memory is aligned
  Introduce unions in C
Bonus: deep-dive into how processors work

## Slide 5: Outline
Structure Layout
Struct Padding and Alignment
Unions

## Slide 6: Structure representation in C
Structure represented as block of memory
  Big enough to hold all of the fields
Fields ordered according to declaration order
  Even if another ordering could yield a more compact representation
  (We’ll see how that could happen in a bit)
Compiler determines overall size + positions of fields
  Looking at memory, no way to tell it’s a struct (like arrays); just bytes
  It’s all in how the code treats that region of memory!
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 7: Structure access
Accessing Structure Member
  Pointer r indicates first byte of structure
  Access member with offsets
  Offset of each structure member determined at compile time
    Another use for Displacement in memory addressing!
r+16
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};
size_t get_i(struct rec *r)
{
return r->i;
}
# r in %rdi
movq 16(%rdi), %rax
ret
r is a pointer to a struct.
Dereference the ponter, then get the i field of the struct.

## Slide 8: Array within a struct
# r in %rdi
# idx in %rsi
movq (%rdi,%rsi,4), %rax
ret
int get_a (struct rec *r,
size_t idx)
{
return r->a[idx];
}
Same as before; just need to also index in the array
  Pointer r indicates first byte of structure
    Offset of each structure member determined at compile time
    Offset into array determined based on index and type
  Compute as *(structAddr + offset + K*index);
    Uses full addressing mode!
r+4*idx
a
r
i
next
0
16
24
32
struct rec {
int a[4];
size_t i;
struct rec *next;
};

## Slide 9: Structure Access Practice 1
struct rec {
int j;
int i;
int a[2];
struct rec *n;
};
movl ______, _______
ret
void
set_i(struct rec *r,
int val)
{
r->i = val;
}
%esi
4(%rdi)
Arguments:
  %rdi
  %rsi
  %rdx
  %rcx
  %r8
  %r9

## Slide 10: Structure Access Practice 2
struct rec {
int j;
int i;
int a[2];
struct rec *n;
};
movl ______, _______
ret
void
set_i(struct rec *r,
int val)
{
r->a[1] = val;
}
%esi
12(%rdi)
Arguments:
  %rdi
  %rsi
  %rdx
  %rcx
  %r8
  %r9

## Slide 11: Structure Access Practice 3
struct rec {
int j;
int i;
int a[2];
struct rec *n;
};
movl ______, _________________
ret
void
set_i(struct rec *r,
int val,
int index)
{
r->a[index] = val;
}
%esi
8(%rdi, %rdx, 4)
Arguments:
  %rdi
  %rsi
  %rdx
  %rcx
  %r8
  %r9

## Slide 12: Following Linked List
.L11: # loop:
movslq 24(%rdi), %rax # i = M[r+24]
movl %esi, 8(%rdi,%rax,4) # M[r+8+4*i] = val
movq (%rdi), %rdi # r = M[r]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
struct rec *next;
int a[4];
int i;
}; // DIFFERENT ORDER!
r
i
next
0
8
24
28
a
By convention, null next
pointer indicates end of list

## Slide 13: Following Linked List
.L11: # loop:
movslq 24(%rdi), %rax # i = M[r+24]
movl %esi, 8(%rdi,%rax,4) # M[r+8+4*i] = val
movq (%rdi), %rdi # r = M[r]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
struct rec *next;
int a[4];
int i;
}; // DIFFERENT ORDER!
r
i
next
0
8
24
28
a
By convention, null next
pointer indicates end of list
Load i

## Slide 14: Following Linked List
.L11: # loop:
movslq 24(%rdi), %rax # i = M[r+24]
movl %esi, 8(%rdi,%rax,4) # M[r+8+4*i] = val
movq (%rdi), %rdi # r = M[r]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
struct rec *next;
int a[4];
int i;
}; // DIFFERENT ORDER!
r
i
next
0
8
24
28
a
By convention, null next
pointer indicates end of list
Write val into r->a[i]

## Slide 15: Following Linked List
.L11: # loop:
movslq 24(%rdi), %rax # i = M[r+24]
movl %esi, 8(%rdi,%rax,4) # M[r+8+4*i] = val
movq (%rdi), %rdi # r = M[r]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
struct rec *next;
int a[4];
int i;
}; // DIFFERENT ORDER!
r
i
next
0
8
24
28
a
By convention, null next
pointer indicates end of list
Move to next node in list

## Slide 16: Following Linked List
.L11: # loop:
movslq 24(%rdi), %rax # i = M[r+24]
movl %esi, 8(%rdi,%rax,4) # M[r+8+4*i] = val
movq (%rdi), %rdi # r = M[r]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
struct rec *next;
int a[4];
int i;
}; // DIFFERENT ORDER!
r
i
next
0
8
24
28
a
By convention, null next
pointer indicates end of list
NULL check

## Slide 17: Outline
Structure Layout
Struct Padding and Alignment
Unions

## Slide 18: Problem: reordering can lead to different layouts
.L11: # loop:
movslq 16(%rdi), %rax # i = M[r+16]
movl %esi, (%rdi,%rax,4) # M[r+4*i] = val
movq ??(%rdi), %rdi # r = M[r+??]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
int a[4];
int i;
struct rec *next;
};
SOMETHING’S WRONG….
r
i
next
0
16
20
28
a
Notes: What’s wrong is that the code generated by the compiler (our ground truth) does not match what we think the data looks like.
Our picture is wrong.

## Slide 19: Padding is added to struct to preserve alignment
.L11: # loop:
movslq 16(%rdi), %rax # i = M[r+16]
movl %esi, (%rdi,%rax,4) # M[r+4*i] = val
movq 24(%rdi), %rdi # r = M[r+24]
testq %rdi, %rdi # Test r
jne .L11 # if !=0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->next;
}
}
Register | Value
%rdi | r
%rsi | val
struct rec {
int a[4];
int i;
struct rec *next;
};
r
i
next
0
16
24
32
a
pad
20

## Slide 20: Alignment
Aligned data
  Primitive data type requires K bytes
  Address must typically be a multiple of K (e.g., 1,2,4 or 8)
    an address that is a multiple of K is called “K-byte aligned”
Required on some machines; recommended on x86-64
  But not doing it will really slow down your program
In our example, pointer needed 8-byte alignment
  offset 24 ok, 20 was not

## Slide 21: The why and how of alignment
Motivation for aligning data
  Inefficient to load or store datum that spans quad word boundaries
  Hardware is really good at loading, e.g., 8 bytes at address 16, or 24, or 32
    If you want 8 bytes at address 12, may need two memory reads. Oops…
Secondary motivations
  Having one datum spanning 2 cache lines = two cache accesses per access
    See upcoming lecture on caching
  Virtual memory very tricky when a datum spans 2 pages
    See upcoming lecture on virtual memory
The compiler manages alignment
  Inserts gaps in structure to ensure correct alignment of fields
  Also occurs on the stack!

## Slide 22: Specific Cases of Alignment (x86-64, Linux)
1 byte: char
  1-byte aligned (no restrictions on address)
2 bytes: short
  2-byte aligned (lowest 1 bit of address must be 0)
4 bytes: int, float
  4-byte aligned (lowest 2 bits of address must be 00)
8 bytes: long, long long, double, char* (any pointer)
  8-byte aligned (lowest 3 bits of address must be 000)
16 bytes: long double
  16-byte aligned (lowest 3 bits of address must be 0000)
  Max possible alignment requirement on x86-64

## Slide 23: Satisfying Alignment within Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    Where K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example:
  K = 8, due to double element
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 24: Meeting Overall Alignment Requirement
Entire struct must be a multiple of its largest element
For largest alignment requirement K
Overall structure must be multiple of K
  Trailing padding
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
Multiple of K=8

## Slide 25: Arrays of Structures
Arrays are the reason for the overall length requirement
  Each struct must start at a multiple of its largest member. This means the member is aligned
The compiler adds trailing padding even without array declaration
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 
struct S2 {
double v;
int i[2];
char c;
} a[10];

## Slide 26: Accessing Array Elements
sizeof(S3)=12, including padding
Compute array offset 12*idx
Element j is at offset 8 within structure
Assembly contains displacement a+8
  Compile-time constant resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %rdi = idx
leaq (%rdi,%rdi,2),%rax # 3*idx
movzwl a+8(,%rax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[idx] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12*idx |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | i | 2 bytes |  | v |  |  | j | 2 bytes |  |  | 
 |  |  |  | a+12*idx |  |  |  |  |  | a+12*idx+8 |  |  |  |  | 

## Slide 27: Saving Space
Put large data types first
Effect: saved 4 bytes
C compilers cannot do this automatically!
  They have to preserve field ordering
  Programmers must do it manually
  Other languages aren’t bound to preserve ordering. Rust may reorder for you
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes

## Slide 28: Break + Quiz
What is the total size of this struct?
  typedef struct { short a; int b; char* c[3]; char d; }

## Slide 29: Break + Quiz
What is the total size of this struct?
  typedef struct { short a; int b; char* c[3]; char d; }
2 bytes for a
(2 bytes for padding)
4 bytes for b (no padding needed, 8-aligned) 24 bytes for c
(no padding needed, 1-aligned) 1 byte for d (7 bytes padding after struct)
= 40 bytes total
Could have been 32 bytes if reordered

## Slide 30: Outline
Structure Layout
Struct Padding and Alignment
Unions

## Slide 31: Unions
Structs = combine multiple pieces of data into one
  Think: “all of the above”
Unions = choose between multiple different kinds of data
  Think: “any of the above”
Typically used in conjunction with a struct: variants
  That tells us which branch of the union is used
  E.g., which_kind of 0 to mean sandwich meal, 1 for pizza, etc.
typedef struct {
int n_pieces_bread;
char *toppings[2];
float mayo_ounces;
} Sandwich_t;
typedef union {
Sandwich_t s;
Pizza_t p;
Burrito_t b;
} MealKind_t;
typedef struct {
char which_kind;
char n_sides;
char cost;
MealKind_t mk;
} Meal_t;

## Slide 32: Union allocation
Principles
  Overlay union elements
  Allocate according to largest element (strictest)
  Can only use one field at a time
union U1 {
char c;
int i[2];
double v;
} up;
struct S1 {
char c;
int i[2];
double v;
} sp;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  | v |  |  |  |  |  | 
sp+0 |  |  |  | sp+4 |  |  |  | sp+8 |  |  |  |  |  |  | sp+16 |  |  |  |  |  | sp+24 | 
 | c | 7 bytes |  |  |  |  | 
 | i[0] |  |  | i[1] |  |  | 
 | v |  |  |  |  |  | 
up+0 |  |  | up+4 |  |  | up+8 | 
Structs: All of the above,
together, one after the other.
Unions: One of the above,
you pick the one you want.
Union: same bits, different contexts
  8 bytes are allocated for the union
  Can be interpreted as any member
  Changing one member will change some bits of the others
Notes: Struct: all of the above, together
Union: one of the above, pick one

## Slide 33: Union allocation
Principles
  Overlay union elements
  Allocate according to largest element (strictest)
  Can only use one field at a time
union U1 {
char c;
int i[2];
double v;
} up;
struct S1 {
char c;
int i[2];
double v;
} sp;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  | v |  |  |  |  |  | 
sp+0 |  |  |  | sp+4 |  |  |  | sp+8 |  |  |  |  |  |  | sp+16 |  |  |  |  |  | sp+24 | 
 | c | 7 bytes |  |  |  |  | 
 | i[0] |  |  | i[1] |  |  | 
 | v |  |  |  |  |  | 
up+0 |  |  | up+4 |  |  | up+8 | 
Quiz: If we had 3 ints in that array, how much space would the union take?
Answer: 16 bytes (8-byte aligned)
Structs: All of the above,
together, one after the other.
Unions: One of the above,
you pick the one you want.
Notes: Struct: all of the above, together
Union: one of the above, pick one

## Slide 34: Using union to access bit patterns
typedef union {
float f;
unsigned u;
} bit_float_t;
unsigned float2bit(float f) {
bit_float_t temp;
temp.f = f;
return temp.u;
}
# procedure with float arg
# arg1 passed in %xmm0
# movss = move single-precision
movss %xmm0, -4(%rsp)
movl -4(%rsp), %eax
ret
 | f |  |  |  | 
 | u |  |  |  | 
0 |  |  |  | 4 | 
Store union using one type & access it with another one
Get direct access to bit representation of float
float2bit generates bit pattern from float
  NOT the same as (unsigned) f !
  Doesn’t convert value to unsigned
  Keeps the same bits but interprets them differently
Assembly doesn’t have type info
  Just moves the bytes

## Slide 35: Access to Bit Pattern Non-Solution
unsigned float2bit(float f) {
unsigned *p;
p = (unsigned *) &f;
return *p;
}
Undefined behavior in C.
Don’t do that.

## Slide 36: Byte ordering revisited
Idea
  Words/long words/quad words stored in memory as 2/4/8 consecutive bytes
  At which byte address in memory is the most (least) significant byte stored?
  Can cause problems when exchanging binary data between machines
Little Endian
  Least significant byte has lowest address
  Intel x86(-64), ARM Android and IOS
Big Endian
  Most significant byte has lowest address
  Sun/Sparc, Networks
Have to worry about it when working with unions!

## Slide 37: Byte Ordering Example
for (int j = 0; j < 8; j++) {
dw.c[j] = 0xf0 + j;
}
printf("Chars 0-7 == [0x%x, 0x%x, 0x%x, 0x%x, 0x%x, 0x%x, 0x%x, 0x%x]\n",
dw.c[0], dw.c[1], dw.c[2], dw.c[3],
dw.c[4], dw.c[5], dw.c[6], dw.c[7]);
printf("Shorts 0-3 == [0x%x, 0x%x, 0x%x, 0x%x]\n",
dw.s[0], dw.s[1], dw.s[2], dw.s[3]);
printf("Ints 0-1 == [0x%x, 0x%x]\n",
dw.i[0], dw.i[1]);
printf("Long 0 == [0x%lx]\n",
dw.l[0]);
union {
unsigned char c[8];
unsigned short s[4];
unsigned int i[2];
unsigned long l[1];
} dw;

## Slide 38: Byte ordering on Little Endian
Output:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
LSB
MSB
union {
unsigned char c[8];
unsigned short s[4];
unsigned int i[2];
unsigned long l[1];
} dw;
Contents
Print
Characters 0-7 == [0xf0, 0xf1, 0xf2, 0xf3, 0xf4, 0xf5, 0xf6, 0xf7]
Shorts 0-3 == [0xf1f0, 0xf3f2, 0xf5f4, 0xf7f6]
Ints 0-1 == [0xf3f2f1f0, 0xf7f6f5f4]
Long 0 == [0xf7f6f5f4f3f2f1f0]
Views

## Slide 39: Byte ordering on Big Endian
Characters 0-7 == [0xf0, 0xf1, 0xf2, 0xf3, 0xf4, 0xf5, 0xf6, 0xf7]
Shorts 0-3 == [0xf0f1, 0xf2f3, 0xf4f5, 0xf6f7]
Ints 0-1 == [0xf0f1f2f3, 0xf4f5f6f7]
Long 0 == [0xf0f1f2f3f4f5f6f7]
Output:
f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7
c[0] | c[1] | c[2] | c[3] | c[4] | c[5] | c[6] | c[7]
s[0] |  | s[1] |  | s[2] |  | s[3] | 
i[0] |  |  |  | i[1] |  |  | 
l[0] |  |  |  |  |  |  | 
MSB
LSB
union {
unsigned char c[8];
unsigned short s[4];
unsigned int i[2];
unsigned long l[1];
} dw;
Contents
Print
Views

## Slide 40: Break + Thinking
We’ve covered everything we need to from assembly
Do we know enough to “compile” C++ in x86-64?
  Yes!
  Classes are structs
    Likely with extra members to keep track of things
    And function pointers as members
  References are just pointers that the compiler handles for you

## Slide 41: Lecture BONUS Assembly to Transistors
CS213 – Intro to Computer Systems
Branden Ghena
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 42: Assembly into machine code
Machine code are the numerical versions of each instruction
Number breaks down into parts
  Operation
  Source
  Destination
Immediates are stored in the instruction encoding

## Slide 43: Machine code ideas
Example:
  ADD $0x4351FF23, %rax
  ADD with destination %rax translates into 0x05
  Immediate is appended on to that
  Machine code: 0x0523FF5143
Number of bytes for each instruction is variable
  1-15 bytes depending on instruction and operands
Translation in complicated
  We’re not going to do it by hand, although Attack Lab will touch it a bit

## Slide 44: Representing instructions as numbers
Why represent instructions as numbers?
Everything in memory is “just a number”
  And instructions go in memory
Hardware can “decode” number to figure out what to do
  Break number apart into bits (just like floating point)
  Some bits pick operation
  Some bits pick register or specify immediate

## Slide 45: Computer Processor (in five easy steps)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 46: These steps are relatively easy (we’ll skip them)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 47: This is extremely complicated for x86-64 (skip it too)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 48: We can talk about what execution means though!
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 49: Arithmetic Logic Unit (ALU)
Piece of hardware
Takes in two operands
  Source and Destination values
Takes in an Opcode
  Which operation to run
Performs operation and outputs result

## Slide 50: What can an ALU do?
All the basic arithmetic operations
  Add
  Subtract
  Bitwise And
  Bitwise Or
  Bitwise Xor
  Arithmetic Shift Right
  Logical Shift Right
  Logical Shift Left
Complex operations are separate hardware
  Multiply, Divide, Anything floating point

## Slide 51: Let’s zoom in

## Slide 52: Inside an ALU
Input values go into separate hardware blocks for each operation
Every operation occurs in parallel, simultaneously
  We are in hardware so this is essentially free
ALU Inputs

## Slide 53: Inside an ALU – selecting the correct output
Selector
ALU Output
ALU Inputs
Opcode
Selects ALU output based on Opcode

## Slide 54: Let’s zoom in

## Slide 55: How is an ALU made?
All of those arithmetic operations can be broken down into a series of 1-bit Boolean operations
  Add is XOR for result + AND for carry
  Subtract is Flip bits (NOT), Add one (XOR + AND), then Add (XOR + AND)
  And/Or/Xor are just their respective operations
  Shifts are just move the bits around (simple in hardware, just move wires)

## Slide 56: 32-bit OR operation
Perform OR operation on each individual bit
  Pictured is a series of 1-bit OR gates

## Slide 57: 32-bit ADD operation
Below is the 1-bit version with carry-in/out
  Two 1-bit AND, two 1-bit XOR, one 1-bit OR
  Repeat 32 times, connecting carries together

## Slide 58: Let’s zoom in

## Slide 59: Logic gates can be created with transistors
CMOS implementation of logic gates
  Complementary Metal-Oxide Semiconductor
Transistors are just on/off switches

## Slide 60: Let’s zoom in

## Slide 61: Transistors are made out of silicon and other materials
Turning gate on/off causes source and drain to connect or disconnect
  Acts as a switch
We can make very small transistors

## Slide 62: That’s the bottom

## Slide 63: Zooming out again
Transistors make logic gates
1-bit AND gate
F

## Slide 64: Zooming out again
Logic gates make operations
1-bit AND gate
1-bit ADD operation

## Slide 65: Zooming out again
1-bit operations make 32-bit operations
1-bit ADD operation

## Slide 66: Zooming out again
Operations make an ALU
Selector
ALU Output
ALU Inputs
Opcode

## Slide 67: ALU allows us to execute operations
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 68: All the way back to software
C compiles into assembly
Assembly translates into machine code
Machine code specifies what should be executed

## Slide 69: A processor is just a lot of transistors connected very carefully
ALU plus other operations make up a Core
  And decode logic
Multiple cores, plus registers, plus caches make up a Processor
  And other stuff these days like graphics

## Slide 70: Outline
Structure Layout
Struct Padding and Alignment
Unions
Assembly to Transistors (and back)