## Slide 1: Lecture 13 Cache Memories
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2022
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Announcements
Homework 3 due today
Attack Lab due next week
  Get started ASAP!
  Be sure to check out the Campuswire post on “Attack Lab Even Return Requirement”
  PM Huaxuan Chen did an overview of the Attack Lab
    Slides posted to Campuswire, and recording on Canvas->Panopto

## Slide 3: Today’s Goals
Discuss organization of various cache designs
  Direct-mapped caches
  N-way set-associative caches
  Fully-associative caches
Understand how cache memories are used to reduce the average time to access memory

## Slide 4: Outline
Cache Organization
Associativity
Cache Performance

## Slide 5: Caching speeds up code
Cache: smaller, faster storage device that keeps copies of a subset of the data in a larger, slower device
  If the data we access is already in the cache, we win!
  Can get access time of faster memory, with overall capacity of larger
Locality helps predict which data code is likely to access
  So want to design caches to take advantage of it!
    Most code has good locality
    Well-written code has great locality!
  Spatial locality: if you need a byte, you’re likely to need its neighbors
    Caches should load whole blocks, not single bytes!
  Temporal locality: if you need a byte, you’re likely to need it again
    Caches should try to keep recently cached data in the cache!

## Slide 6: Cache memories
A specific instance of the general principle of caching
  Small, fast SRAM-based memories between CPU and main memory
  Can include multiple levels
    L1 = small, but really fast, L2 = larger, slower, L3, etc.
CPU looks for data in caches first
  e.g., L1, then L2, then L3, then finally in main memory as a last resort
Mechanisms we’ll see today are implemented in hardware
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memories

## Slide 7: How You Probably Thought a Memory Access Worked
Some memory address
Address of word:
Memory:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 8: How a Memory Access Actually Works
Some memory address
Address of word:
Memory:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
L1 Cache:
L2 Cache:
...
...
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 9: General Cache Organization (S, A, B)
A blocks per set (associativity)
K = 2s sets
cache set
B-1
2
1
0
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = K x A x B data bytes
valid bit
cache block
(aka cache line)
Set ≈ column from last time.
Specific data can go in only one set!
tag identifies which data is in this cache block
Notes: Typical B: 32, 64, sometimes up to 256

## Slide 10: Cache Access
Some memory address
Address of word:
Cache:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
t bits
s bits
b bits
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 11: Cache Read (1): Locate Set
A lines per set
K = 2s sets
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
Locate set
0xFF
0xFF
Each address maps to a particular set!
Data has to be stored at that particular set!
Even if that set is full and there “is space” elsewhere!
(That’s where conflict misses come from.)

## Slide 12: Cache Read (2): Tag Match + Valid
A lines per set
K = 2s sets
tag
v
valid bit
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
Locate set
Locate block in set
Tag matches + valid bit set  Cache Hit!
0xFF
0xFF
0x1E45
0x1E45
1
Within a set, could be anywhere! So, need to check all lines!
But if it’s not in that set, it’s not in the cache at all! (It’s the only place it could be.)

## Slide 13: Cache Read (3): Block Offset
A lines per set
K = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
data begins at this offset
Locate set
Locate line in set
Tag matches + V bit set  Cache Hit!
Locate data starting at offset
block
offset
0xFF
0xFF
0x1E45
0x1E45
1
0x2
2

## Slide 14: Example: 128 sets, 64 bytes per block
00…0
1
63
2
1
0
127
66
65
64
191
130
129
128
Memory:
t bits
s bits
b bits
6510 = 100 00012
00...0
0000001
000001
64 bytes per block  b = 6 bits
128 sets  s = 7 bits
remaining address bits  t bits
address of a byte in memory
A lines per set
set 0:
set 1:
set 2:
set 127:
Goal: Get byte M[65] from cache
QUIZ #1: which set
should we look in?
QUIZ #2: which tag
are we looking for?
QUIZ #3: which byte
within the block is the
one that we want?

## Slide 15: Cache access overview
A lines per set
2s sets
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
data begins at this offset
block
offset
Address of word:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
...
return var;
...
...
movq -12(%rsp),%rax
...
valid bit
tag identifies which data is in this cache block

## Slide 16: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
  Don’t want them to get (or at least not to stay) out of sync!
    Otherwise, who do you believe?
Multiple configuration options that a cache could have

## Slide 17: Write configurations
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (delay write until we evict this cache block)
    Need a dirty bit (indicate if line differs from memory)
    We had an example of that last time
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory, doesn’t bring into cache)
Typical
  Write-back + Write-allocate ← by far the most common
  Write-through + No-write-allocate

## Slide 18: Break + Question
64-bit, byte-addressed system
32 kB cache
  512 sets and 64-byte blocks
How many bits for Tag?
  A: 6 bits
  B: 9 bits
  C: 17 bits
  D: 49 bits
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
s bits

## Slide 19: Break + Question
64-bit, byte-addressed system
32 kB cache
  512 sets and 64-byte blocks
How many bits for Tag? (6 bits for block, 9 bits for set)
  A: 6 bits
  B: 9 bits
  C: 17 bits
  D: 49 bits (Tag is remaining bits. 64 - 6 - 9 = 49)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
s bits

## Slide 20: Outline
Cache Organization
Associativity
Cache Performance

## Slide 21: Cache memory associativity
When designing a cache, a number of parameters to choose
  Total size (C), cache block size (B), number of sets (K), …
The most interesting one: associativity (A)
  i.e., how many cache blocks per set
  Has a significant impact on effectiveness (and complexity!)

## Slide 22: Associativity choices
Associativity 1 → direct-mapped caches
  One cache block per set, blocks can only go in that one block
  Whenever we place data in a set, must evict whatever is there
Associativity >1 → set-associative caches
  Can keep multiple cache blocks that would map to the same set
Single set → fully-associative caches
  Any cache block can go anywhere, 1 big set, tag is all that matters
  Very rare for cache memories due to expensive hardware

## Slide 23: Direct-mapped cache (associativity = 1)
K = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set

## Slide 24: Direct-mapped cache (associativity = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
tag match? if yes  hit
valid? +
block offset
tag
Address of int:

## Slide 25: Direct-mapped cache (associativity = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
tag match? if yes  hit
valid? +
int is here (4 bytes)
block offset
Address of int:

## Slide 26: Direct-mapped cache (associativity = 1)
K = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set
If tag doesn’t match or valid bit is not set: cache miss!
 old line is evicted and replaced with currently requested one
X
X
tag
1
7
6
5
0
4
1
2
3
Address of int:

## Slide 27: Direct-mapped cache simulation
7 [0 11 12]
8 [1 00 02]
0 [0 00 02]
1 [0 00 12]
x
t=1
s=2
b=1
xx
x
block
v
tag
0 [0 00 02]
1 0 m[1] m[0]
1 0 m[1] m[0]
1 0 m[7] m[6]
1 1 m[9] m[8]
1 0 m[1] m[0]
1 0 m[7] m[6]
miss
hit
miss
miss
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
1 1 m[9] m[8]
0
0
0
0
???

## Slide 28: What are the types of each miss here?
7 [0 11 12]
8 [1 00 02]
0 [0 00 02]
1 [0 00 12]
x
t=1
s=2
b=1
xx
x
Conflict misses: There is “room” in the cache, but two blocks map to the same set; one evicts the other!
block
v
tag
0 [0 00 02]
miss
hit
miss
miss
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
Compulsory Miss
Compulsory Miss
Compulsory Miss
Conflict Miss
1 0 m[7] m[6]
Options:
Compulsory
Capacity
Conflict
1 0 m[1] m[0]

## Slide 29: Pause for questions on direct-mapped caches

## Slide 30: Associativity choices
Associativity 1 → direct-mapped caches
  One cache block per set, blocks can only go in that one block
  Whenever we place data in a set, must evict whatever is there
Associativity >1 → set-associative caches
  Can keep multiple cache blocks that would map to the same set
Single set → fully-associative caches
  Any cache block can go anywhere, 1 big set, tag is all that matters
  Very rare for cache memories due to expensive hardware

## Slide 31: 2-way set-associative cache (associativity = 2)
A = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set

## Slide 32: 2-way set-associative cache (associativity = 2)
A = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
compare both
valid? +
tag match? if yes  hit
block offset
tag
The data we want is either on the left, or on the right, or not in the cache at all.
It can’t be anywhere else! Addresses map to a single set!

## Slide 33: 2-way set-associative cache (associativity = 2)
A = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
compare both
valid? +
tag match? if yes = hit
block offset
short int is here (2 bytes)
If no match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
  More clever → lower miss rate, but harder to implement in hardware

## Slide 34: 2-way set-associative cache simulation
Address trace (reads, one byte per read):
0 [00 0 02]
1 [00 0 12]
7 [01 1 12]
8 [10 0 02]
0 [00 0 02]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[1-0]
hit
miss
1
01
M[7-6]
miss
1
10
M[9-8]
hit
Set 0
Set 1
The same address sequence in the direct mapped cache resulted in:
miss
hit
miss
miss
miss
M=16 addresses, byte-addressable,
B=2 bytes/block, K=2 sets, A=2 blocks/set
Higher associativity =
Less likely to have to evict!
Temporal locality: want data in cache to stay in cache!
v
Tag
Block
Same total size and block size as before.
Associativity (and thus # of sets) changed.

## Slide 35: Pause for questions on set-associative caches

## Slide 36: Fully-associative caches
What changes with fully-associative caches?
  Anything can go anywhere
  Only one set (s = 0 bits)
Otherwise, same steps as for a set-associative cache
  Compare tag against all blocks in the set

## Slide 37: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400
  0x0410
  0xC002
  0xC048
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051

## Slide 38: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000
  0x0410⇨0b0000 0100 0001 0000
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051

## Slide 39: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000 → Tag 0x010 HIT
  0x0410⇨0b0000 0100 0001 0000 → Tag 0x010 (same block!) HIT
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051

## Slide 40: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000 → Tag 0x010 HIT
  0x0410⇨0b0000 0100 0001 0000 → Tag 0x010 (same block!) HIT
  0xC002⇨0b1100 0000 0000 0010 → Tag 0x300 HIT
  0xC048⇨0b1100 0000 0100 1000 → Tag 0x301 (different block!) MISS
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051

## Slide 41: Associativity Pros and Cons
Direct-mapped
  Simplest to implement: look-up compares tag with 1 cache line → requires fewer transistors, which can be used elsewhere on the chip
  Conflicts can easily lead to thrashing
    Two cache lines map to the same set, program needs both, and they keep kicking each other out of the cache. Lots of misses. Bad times.
Set-associative
  More complex implementation: requires more (HW) tag comparators
  Lower miss rate than direct-mapped caches (fewer conflict misses)
    2-way is a significant improvement over direct-mapped
    4-way is a more modest improvement over 2-way, and so on
Fully-associative
  One comparator per cache line in the cache. Ouch.
    Often a deal-breaker for hardware
  Very low miss rate!

## Slide 42: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
Keep separate caches for instructions and data. Don’t want them to step on each other’s toes!
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Last resort before going to main memory (slow!) So want this large and highly-associative, to have very few misses.
Block size: 64 bytes for all caches.

## Slide 43: Outline
Cache Organization
Associativity
Cache Performance

## Slide 44: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    Can be quite small (e.g., < 1%) for L2, depending on dataset size, etc.
    However, many applications have >30% miss rate in L2 cache
Hit Time
  Time to deliver a line in the cache to the processor
    Includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycles for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
  Typically 50-200 cycles for main memory
    Not really a “penalty”, just how long it takes to read from memory

## Slide 45: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if comparing L1 and main memory
Would you believe a 99% hit rate is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 100 instructions: 100 cycles (1 per instruction) + 3*100 (misses)
  on average: 1 cycle/instr. + 0.03 * 100 cycles/instr. = 4 cycles/instr.
  99% hits: on average: 1 cycle/instr. + 0.01 * 100 cycles/instr. = 2 cycles/instr.
This is why “miss rate” is used instead of “hit rate”
  In our example, 1% miss rate vs. 3% miss rate
  Makes the radical performance difference more obvious
“Computation is what happens between cache misses.”

## Slide 46: Average Memory Access Time (AMAT)
AMAT = Hit time + Miss rate × Miss penalty
  Generalization of previous formula
Can extend for multiple layers of caching
  AMAT = Hit Time L1 + Miss Rate L1 × Miss Penalty L1
    Miss Penalty L1 = Hit Time L2 + Miss Rate L2 × Miss Penalty L2
    Miss Penalty L2 = Hit Time Main Memory
Multi-level caching helps minimize AMAT

## Slide 47: Outline
Cache Organization
Associativity
Cache Performance