## Slide 1: Lecture 02 Embedded Software
CE346 – Microcontroller System Design
Branden Ghena – Spring 2025
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Make sure you have your personal lab setup working
  Ask in office hours or on Piazza if you run into issues
Labs will start this Friday!!!
  You MUST come to your scheduled lab session
    If there’s some known obligation and you give me a heads up, I can let you move to the other section
  If you want to permanently change lab sessions (to the later lab at 3pm) let me know
  I’ll hand out Microbits as part of lab

## Slide 3: Weekly Schedule
Office Hours
  Monday 2-3
  Tuesday 2-3, 5-6 (joint)
  Wednesday 11-1, 2-3
  Thursday 5-6
Checkoffs and debugging
  But also ANY class question
  These are for you to use

## Slide 4: Today’s Goals
Discuss challenges of embedded software
Describe compilation and linking of embedded code
  (Actually applies to all code, but you probably never learned much about linking before)
Introduce Memory-Mapped I/O as a mechanism for communicating with peripherals
Explore the microcontroller boot process

## Slide 5: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process

## Slide 6: Review: C memory layout
Stack Section
  Local variables
  Function arguments
Heap Section
  Memory granted through malloc()
Static Section (a.k.a. Data Section)
  Global variables
  Static function variables
Text Section (a.k.a Code Section)
  Program code
Stack
Heap
Static
Text
Address 0x0000000000000000
Address 0xFFFFFFFFFFFFFFFF

## Slide 7: Assumptions of embedded programs
Expect limitations
  Very little memory
  Very little computational power
  Very little energy
Don’t expect a lot of support
  Likely no operating system
  Might not even have error reporting capabilities
Your code runs the entire system
  Single application on the system that runs forever
Moral: think differently about your programs

## Slide 8: Ramifications of limited memory
Stack and Data sections are limited
  Be careful about too much recursion
  Be careful about large local variables
Large data structures defined globally are preferred
  In embedded, we often encourage global variables for large things
  Fail at compile time rather than run-time
Heap section might exist but should only be used cautiously
  What do you do if the heap runs out?

## Slide 9: Avoiding dynamic memory
Malloc is scary in an embedded context
What if there’s no more memory available?
  Traditional computer
    Swap memory to disk
    Worst case: wait for a process to end (or kill one)
  Embedded computer
    There’s likely only a single application
    And it’s the one asking for more memory
    So it’s not giving anything back anytime soon
This is unlikely to happen at boot
  Instead it’ll happen hours or days into running as memory is slowly exhausted…

## Slide 10: Limitations on processing power
Typically not all that important
  Code still runs pretty fast
    10 MHz -> 100 ns per cycle (i.e. ~100 ns per instruction)
    ~10 million instructions per second
  Controlling hardware usually doesn’t have a lot of code complexity
    Quickly gets to the “waiting on hardware” part (apps are I/O bound)
Problems
  Machine learning
    Learning on the device is a big challenge
    Memory limitations make it hard to fit weights anyways
  Cryptography
    Public key encryption takes seconds to minutes

## Slide 11: Common programming languages for embedded
C
  For all the reasons that you assume
  Easy to map variables to memory usage and code to instructions
Assembly
  Not entirely uncommon, but rarer than you might guess
  C code optimized by a modern compiler is likely faster
  Notable uses:
    Cryptography to create deterministic algorithms
    Operating Systems to handle process swaps
C++
  Similar to C but with better library support
  Libraries can take up a lot of code space though ~100 KB
    Some specialized versions of libraries take up less space

## Slide 12: Rarer programming languages for embedded
Rust
  Modern language with safety and reliability guarantees
  Increasingly relevant in the embedded space
    But with a high learning curve
Python, Javascript, Scratch, etc.
  Mostly toy languages
  Fine for simple things but incapable of complex operations
    Especially low-level things like managing memory
  Microbit supports all of these, play around with them sometime:
    https://makecode.microbit.org/
    https://python.microbit.org/v/3
    https://scratch.mit.edu/microbit

## Slide 13: What’s missing from programming languages?
The embedded domain has several requirements that other domains do not
What is missing from programming languages that it wants?
  Sense of time
  Sense of energy

## Slide 14: Programming languages have no sense of time
Imagine a system that needs to send messages to a motor every 10 milliseconds
  Write a function that definitely completes within 10 milliseconds
Accounting for timing when programming is very challenging
  We can profile code and determine timing at runtime
  If we know many details of hardware, instructions can give timing
    Unless the code interacts with external devices

## Slide 15: Determining energy use is rather complicated
Software might
  Start executing a loop
  Turn on/off an LED
  Send messages over a wired bus to another device
Determining energy these operations take is really difficult
  Even with many details of the hardware
  Different choices of processor clocks can have a large impact
  Often profiled at runtime after writing the code
    Iterative write-test-modify cycle

## Slide 16: Break + Question
volatile float value = 1337.3235;
volatile float result = sqrt(value);
Which program takes longer to run?
printf(“Hello world!\n”);
Program 1:
Program 2:

## Slide 17: Break + Question
volatile float value = 1337.3235;
volatile float result = sqrt(value);
Which program takes longer to run?
printf(“Hello world!\n”);
33 microseconds
~2112 instructions
3392 microseconds
~217088 instructions
Majority of the time isn’t spent in instructions though
Printf takes about 100x longer!!
Program 1:
Program 2:

## Slide 18: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process

## Slide 19: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for code size instead of speed)

## Slide 20: Cross compilers compile for different architectures
The compiler we’ll be using is a cross compiler
  Run on one architecture but compile code for another
    Example: runs on x86-64 but compiles armv7e-m
GCC naming scheme: ARCH-VENDOR-(OS-)-ABI-gcc
  arm-none-eabi-gcc
    ARM architecture
    No vendor
    No OS
    Embedded Application Binary Interface
  Others: arm-none-linux-gnueabi-gcc, i686-pc-windows-msvc-gcc

## Slide 21: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables

## Slide 22: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do x86-64 compilers know which addresses to use?

## Slide 23: Informing linker of system memory
Linker actually places code and variables in memory
  It needs to know where to place things
How do x86-64 compilers know which addresses to use?
  Standard layout for all processes
  Virtual memory allows all applications to use the same memory addresses
Embedded solution
  Only run a single application
  Provide our own standard layout: an LD file
    Specifies memory layout for a certain system
    Places sections of code in different places in memory

## Slide 24: Anatomy of an LD file
nRF52833: 512 KB Flash, 128 KB SRAM
First, LD file defines memory regions
  MEMORY {
  FLASH (rx) : ORIGIN = 0x00000000, LENGTH = 0x80000
  RAM (rwx) : ORIGIN = 0x20000000, LENGTH = 0x20000
  }
A neat thing about microcontrollers: pointers have meaning
  Just printing the value of a pointer can tell you if it’s in Flash or RAM

## Slide 25: Anatomy of an LD file
It then places sections of code into those memory regions
  .text : {
  KEEP(*(.Vectors))
  *(.text*)
  *(.rodata*)
  . = ALIGN(4);
  } > FLASH __etext = .;
  .data : AT (__etext) {
  __data_start__ = .;
  *(.data*)
  __data_end__ = .;
  } > RAM
  .bss : {
  . = ALIGN(4);
  __bss_start__ = .;
  *(.bss*)
  . = ALIGN(4);
  __bss_end__ = .;
  } > RAM

## Slide 26: Sections of code
Where do these sections come from?
Most are generated by the compiler
  .text, .rodata, .data, .bss
  You need to be deep in the docs to figure out how the esoteric ones work
Some are generated by the programmer
  Allows you to place certain data items in a specific way
  __attribute__((section(".foo")))
  int test[10] = {0,0,0,0,0,0,0,0,0,0};

## Slide 27: Embedded compilation steps
Same first steps as any system
Compiler
  Turn C code into assembly
  Optimize code (often for size instead of speed)
Linker
  Combine multiple C files together
  Resolve dependencies
    Point function calls at correct place
    Connect creation and uses of global variables
Output: a binary (or hex) file

## Slide 28: Loading the hex file onto a board
This is a use case for JTAG
  You provide it a hex file which specifies addresses and values
  It writes those into Flash on the microcontroller
The LD file already specified addresses
  So passing around hex files is enough to load an application
  But a hex file for one microcontroller won’t work on another with a different memory layout

## Slide 29: Example
Demonstrated in the blink application in lab repo
  https://github.com/nu-ce346/nu-microbit-base/tree/main/software/apps/blink

## Slide 30: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process

## Slide 31: Embedded environments
There are a multitude of embedded software systems
  Every microcontroller vendor has their own
  Popular platforms like Arduino
We’re using the Nordic software development libraries plus some extensions made by my research group
  It’ll be a week until that matters for the most part
  We’ll start off by writing low-level drivers ourselves without libraries

## Slide 32: Software Development Kit (SDK)
Libraries provided by Nordic for using their microcontrollers
  Actually incredibly well documented! (relatively)
  Various peripherals and library tools
SDK documentation
  https://docs.nordicsemi.com/bundle/sdk_nrf5_v16.0.0/page/index.html
  Warning: search doesn’t really work
Possibly more useful: the list of data structures
  Search that page for whatever “thing” you’re working with
  https://docs.nordicsemi.com/bundle/sdk_nrf5_v16.0.0/page/annotated.html

## Slide 33: nRF52x-base
Wrapper built around the SDK by Lab11
  Branden Ghena, Brad Campbell (UVA), Neal Jackson, a few others
  Allows everything to be used with Makefiles and command line
  https://github.com/lab11/nrf52x-base
We include it as a submodule
  It has a copy of the SDK code and softdevice binaries
  It has a whole Makefile system to include to proper C and H files
  We include a Board file that specifies our specific board’s needs and capabilities
Go to repo to explain

## Slide 34: Break + xkcd
https://xkcd.com/303/

## Slide 35: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process

## Slide 36: How does a computer talk with peripherals?
A peripheral is a hardware unit within a microcontroller
  Sort of a “computer-within-the-computer”
  Performs some kind of action given input, generates output
We interact with a peripheral’s interface
  Called registers (actually are from EE perspective, but you can’t use them)
  Read/Write like they’re data
How do we read/write them?
  Options:
    Special assembly instructions
    Treat like normal memory

## Slide 37: Memory-mapped I/O (MMIO): treat devices like normal memory
Certain physical addresses do not actually go to memory
Instead they correspond to peripherals
  And any instruction that accesses memory can access them too!
Every microcontroller I’ve ever seen uses MMIO
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 38: Memory map on nRF52833
Flash 0x00000000
SRAM 0x20000000
APB peripherals 0x40000000
  Everything but GPIO
AHB peripherals 0x50000000
  Just GPIO
UICR – User Information Config
FICR – Factory Information Config

## Slide 39: Example nRF52 peripheral placement
0x1000 is plenty of space for each peripheral
  1024 registers, each 32 bits
  No reason to pack them tighter than that

## Slide 40: Example register layout
32-bit value
  Bits 0-4 are field A
  Bit 5 is field B
  Bit 31 is field C
  Others are unused
Each field has value ranges and descriptions of what it means

## Slide 41: Registers can vary wildly in complexity

## Slide 42: Bit Masking
How do you manipulate certain bits within a number?
Use bit manipulation operations
  ~, &, |, <<, >>
Steps
  Create a “bit mask” which is a pattern to choose certain bits
  Use & or | to combine it with your number
  Optional: Use >> to move the bits to the least significant position

## Slide 43: Bit mask values
Selecting bits, use the AND operation
  1 means to select that bit
  0 means to not select that bit
Writing bits
  Writing a one, use the OR operation
    1 means to write a one to that position
    0 is unchanged
  Writing a zero, use the AND operation
    0 means to write a zero to that position
    1 is unchanged
Select bottom four bits:
num & 0x0F
Set 6th bit to one:
num | (1 << 6)
num | (0b01000000)
Clear 6th bit to zero: num & (~(1 << 6))
num & (~(0b01000000))
num & (0b10111111)

## Slide 44: Example: selecting bits
Select bits 2 and 3 from a number
Input: 0b01100100
0b01100100
Mask: 0b00001100
0b01100100
& 0b00001100
0b00000100
Finally, shift right by two to get the values in the least significant position:
0b00000001
In C: result = (input & 0x0C) >> 2;

## Slide 45: Manipulating a register value
Check Port value
  value = (REG >> 5) & 1 or (REG & (1 << 5)) >> 5
Write port value
  REG |= (1 << 5) // set port to 0
  REG &= ~(1 << 5); // set port to 1

## Slide 46: TEMP on nRF52833 example
Internal temperature sensor
  0.25° C resolution
  Range equivalent to microcontroller IC (-40° to 105° C)
  Various configurations for the temperature conversion (ignoring)
https://docs.nordicsemi.com/bundle/ps_nrf52833/page/temp.html

## Slide 47: Interacting with the temperature peripheral

## Slide 48: Reading a temperature value
32-bit value
2’s complement (i.e., signed)
0.25 ℃ steps (so 0 = 0℃, 4 = 1℃, etc.)

## Slide 49: MMIO addresses for TEMP
What addresses do we need? (ignore interrupts for now)
  0x4000C000 – TASKS_START
  0x4000C100 – EVENTS_DATARDY
  0x4000C508 - TEMP

## Slide 50: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;

## Slide 51: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;
  0x4000C000 is cast to a uint32_t*
  Then dereferenced
  And we write 1 to it
  “There are 32-bits of memory at 0x4000C000. Write a 1 there.”

## Slide 52: Example code
To the terminal!
Let’s write it from scratch

## Slide 53: Example code (temp_mmio app)

## Slide 54: Using structs to manage MMIO access
Writing simple C code and access peripherals is great!
Problems:
  Need to remember all these long addresses
  Need to make sure compiler doesn’t stop us!
Solution:
  Wrap entire access in a struct!
  Compilers turn it into the same thing in the end anyways

## Slide 55: C structs
Collection of variables placed together in memory
  typedef struct {
  uint32_t variable_one;
  uint32_t variable_two;
  uint32_t array[2];
  } example_struct_t;
Placement rules - Variables are placed adjacent to each other in memory except:
  Fields are always aligned to a multiple of their size
  Padding added to the end to make the total size a multiple of the biggest member
  Microcontrollers can usually ignore these: all registers are the same size!

## Slide 56: Temperature peripheral MMIO struct
typedef struct {
uint32_t TASKS_START;
uint32_t TASKS_STOP;
uint32_t _unused_A[62];
uint32_t EVENTS_DATARDY;
uint32_t _unused_B[0x204/4 - 1];
uint32_t INTENSET;
uint32_t INTENCLR;
uint32_t _unused_C[(0x508 – 0x308)/4 – 1];
uint32_t TEMP;
} temp_regs_t;
volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);
With increasingly verbose ways to write the size of the “unused” space (any of these will do, but don’t forget the -1)

## Slide 57: Temperature peripheral MMIO struct
typedef struct {
uint32_t TASKS_START;
uint32_t TASKS_STOP;
uint32_t _unused_A[62];
uint32_t EVENTS_DATARDY;
uint32_t _unused_B[0x204/4 - 1];
uint32_t INTENSET;
uint32_t INTENCLR;
uint32_t _unused_C[(0x508 – 0x308)/4 – 1];
uint32_t TEMP;
} temp_regs_t;
volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);
// code to access
TEMP_REGS->TASKS_START = 1;
while (TEMP_REGS->EVENTS_DATARDY == 0);
float temperature = ((float)TEMP_REGS->TEMP)/4.0;

## Slide 58: Using MMIO structs
Note: structs still don’t get you individual bits, they only get you the 32-bit registers themselves
You’ll need to do bit manipulations to get the read/write fields you want
Bit fields are an option in C that can allow access to individual bits, but are generally not used
  Implementation-specific details for how they actually work
  What if you need to change multiple fields simultaneously?

## Slide 59: Break + Question
Are compiled binaries portable to other types of microcontrollers?

## Slide 60: Break + Question
Are compiled binaries portable to other types of microcontrollers?
  Definitely not
  1) Each microcontroller has its own layout of Flash and RAM, so we might need to put our code in different locations
  2) Each microcontroller has its own MMIO addresses and devices And every device works at least slightly differently
  Can sometimes get away with it for microcontrollers in the same family
    I.e., class code might work on an nRF52840 instead of our nRF52833

## Slide 61: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process

## Slide 62: How does a microcontroller start running code?
Power comes on
Microcontroller needs to start executing assembly code
You expect your main() function to run
  But a few things need to happen first

## Slide 63: Step 0: set a stack pointer
Assembly code might need to write data to the stack
  Might call functions that need to stack registers
ARM: Valid address for the stack pointer is at first address in Flash
  Needs to point to somewhere in RAM
  Hardware loads it into the Stack Pointer when it powers on

## Slide 64: Step 1: set the program counter (PC)
a.k.a. the Instruction Pointer (IP) in x86 land
32-bit ARM: valid instruction pointer is at address 4 in Flash
  Could point to RAM, usually to Flash though
  In interrupt terms: this is the “Reset Handler”!
  Automatically loaded into the PC after the SP is loaded
    Again, hardware does this

## Slide 65: Step 2: “reset handler” prepares memory
Code that handles system resets
  Either reset button or power-on reset
  Address was loaded into PC in Step 1
Reset handler code:
  Loads initial values of .data section from Flash into RAM
  Loads zeros as values of .bss section in RAM
  Calls SystemInit
    Starts correct clocks for the system
    Handles various hardware configurations/errata
  Calls _start
nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/gcc_startup_nrf52833.S nu-microbit-base/software/nrf52x-base/sdk/nrf5_sdk_16.0.0/modules/nrfx/mdk/system_nrf52.c

## Slide 66: Step 3: set up C runtime
_start is provided by newlib
  An implementation of libc – the C standard library
  Startup is a file usually named crt0
Does more setup, almost none of which is relevant for our system
  Probably is this code that actually zeros out .bss
  Sets argc and argv to 0
  Calls main() !!!
https://sourceware.org/git/gitweb.cgi?p=newlib-cygwin.git;a=blob_plain;f=libgloss/arm/crt0.S;hb=HEAD

## Slide 67: Online writeup with way more details and a diagram
Relevant guide!!
  https://embeddedartistry.com/blog/2019/04/17/exploring-startup-implementations-newlib-arm/
  Covers the nRF52!

## Slide 68: Outline
Embedded Software Overview
Embedded Toolchain
  Lab Software Environment
Memory-Mapped I/O
Boot Process