## Slide 1: Lecture 15 Wrapup + Microprocessors
CE346 – Microcontroller System Design
Branden Ghena – Spring 2025
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Project check-ins on Friday
  Friday 1-5 pm in the lab room
  PMs will be there to chat with groups and generally provide help
Tuesday and Thursday next week will be office hours instead of lecture
Next (probably last) project orders on Sunday
  Put things on list by end-of-day Saturday
  After that it’ll “make the best out of what you have”

## Slide 3: Today’s Goals
Discuss remaining parts of the Microbit and nRF52833
  Realize that we’ve covered almost everything on the system!!
Compare and contrast other microcontrollers and other similar hardware platforms

## Slide 4: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 5: Microbit
Used almost all of this!
Remaining:
  Batteries
  Wireless
  KL27Z I2C

## Slide 6: Internal Microbit connections

## Slide 7: KL27 I2C Interface
Device information
  Version of board and JTAG firmware
  Power state of board
    USB, Battery, both
    Voltage values for battery and VIN
  USB connection state
  Disable the power LED!!
Flash Storage
  128 kB of the KL27’s Flash is readable/writable over I2C
https://github.com/microbit-foundation/spec-i2c-protocol/blob/main/spec/index.md

## Slide 8: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 9: nRF52833 Peripherals
Tour of the nRF52833 peripherals
With some details on the ones we haven’t talked about
  Wireless
  Crypto
  Audio

## Slide 10: nRF52833 Peripherals
Cortex-M4F processor
32-bit ARM core
Floating point
Includes Interrupt control and SysTick (an extra timer)

## Slide 11: nRF52833 Peripherals
Memory buses

## Slide 12: nRF52833 Peripherals
JTAG and Debugging
Allows code updates
Allows GDB to step through code

## Slide 13: nRF52833 Peripherals
Volatile memory
SRAM, 128 kB

## Slide 14: nRF52833 Peripherals
Nonvolatile memory
Flash, 512 kB
Non-Volatile Memory Controller

## Slide 15: nRF52833 Peripherals
Power and Clock management

## Slide 16: nRF52833 Peripherals
GPIO pins

## Slide 17: nRF52833 Peripherals
Various timers
Watchdog Timer
Real-Time Counter
Timer peripheral

## Slide 18: nRF52833 Peripherals
Programmable Peripheral Interconnect
  Event->Task chaining
Random Number Generator
Temperature sensor

## Slide 19: nRF52833 Peripherals
Wireless radio
  Bluetooth Low Energy
  802.15.4 (Zigbee or Thread)
Cryptography
  ECB (AES mode)
  CCM (AES mode)
  AAR (Accelerated Address Resolver)
    For BLE random addresses

## Slide 20: nRF52833 Peripherals
Wired communication protocols
USB Device
SPI
  Controller/Peripheral
TWI (I2C)
  Controller/Peripheral
UART

## Slide 21: nRF52833 Peripherals
Inter-IC Sound (I2S)
  Wired communication bus explicitly for audio data
  Unrelated to I2C
Like a synchronous UART
  Clock, data in, data out
Additional signals
  MCK – synchronization
  LRCK – left/right channel select

## Slide 22: nRF52833 Peripherals
NFC
  Near-Field Communication
Close-range wireless communication protocol
“Tap-to-pay” systems

## Slide 23: nRF52833 Peripherals
GPIOTE
  GPIO interrupts

## Slide 24: nRF52833 Peripherals
Analog inputs
Comparator
Low-Power Comparator
Successive Approximation Analog-to-Digital Converter

## Slide 25: nRF52833 Peripherals
Quadrature Decoder peripheral
Detects rotation speeds and direction
  Usually for motors

## Slide 26: Quadrature Encoding
Usually two receivers and disks: A & B That gets you direction and speed

## Slide 27: nRF52833 Peripherals
Pulse Width Modulation
Pulse Density Modulation
  Similar idea to PWM
  Input-only peripheral
  Targets microphones

## Slide 28: nRF52833 is complete
That’s just about everything!
First 550 out of 600 pages of nRF52833 datasheet
  Remaining 50 are hardware details
    Pinout for different packages
    Recommended circuit layout
    Soldering details

## Slide 29: Break + Open Question
What doesn’t the nRF52833 have a peripheral for? (i.e., what could you imagine a peripheral for that it doesn’t have)

## Slide 30: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 31: Older microcontrollers (90s-00s)
Focus: cheap, small computer systems
PIC
  8, 16, and 24-bit MIPs architecture
  PICAXE available with Basic interpreter
AVR
  8-bit custom architecture (AVR architecture)
  Used in Arduinos
  AT Tiny 4: $0.30 per unit
    4 I/O pins, 32 Bytes RAM, 512 Bytes ROM

## Slide 32: More capable microcontrollers (00s-10s)
Focus: diversify into extreme low power and more capable systems
MSP430
  16-bit custom architecture (MSP430 architecture)
  Capable, but also extremely low power
    <1 μA sleep current
STM32, Atmel SAM series (Cortex-M0, M3, M4, M4F)
  32-bit ARM architecture (ARMv7)
    Leverage success of ARM on smartphones
  Every peripheral under the sun. Plus a variety of memory choices

## Slide 33: Cortex M Series
A number of options for increasing capabilities
In practice:
  Cortex-M0+ for low-end systems
  Cortex-M4 for high capability systems
New systems
  M23, M33, M55, M85
  Faster
  Some have DSP instructions
https://en.wikipedia.org/wiki/ARM_Cortex-M

## Slide 34: Modern system-on-chips (10s-20s?)
Focus: increase memory and capability
  Include radios in the same chip
nRF51 and nRF52 series
  32-bit ARM microcontrollers (Cortex M)
  Include 2.4 GHz radio: Bluetooth Low Energy and 802.15.4/Thread
Others have followed this same path
  TI CC26XX
  Apollo3
  STM32WL

## Slide 35: Future microcontrollers (20s and beyond)
Multi-core systems
  Not for performance, but for separation of concerns
    Run radio code on one core
    Application code goes on the other core
  Also allows BIG.little architecture
    Higher performance core when interpreting data
    Lower performance core for sampling sensors
  nRF54 series really emphasizes this
    Multiple BIG ARM processors and little RISC-V processors

## Slide 36: Break + Open Question
Consider the lifecycles of computer systems
  i.e., how long are people still actively using them for?
  How long does a processor generation need to be supported?
    Think Intel Core i7-7500U or Apple M1
  How long does a microcontroller chip need to be supported?
    Think nRF52833 or MSP430

## Slide 37: Break + Open Question
Consider the lifecycles of computer systems
  i.e., how long are people still actively using them for?
  How long does a processor generation need to be supported?
    Think Intel Core i7-7500U or Apple M1
    After some number of years, new products no longer use it
    Old products eventually wear out or are unsupported
  How long does a microcontroller chip need to be supported?
    Think nRF52833 or MSP430
    New products might still use them years later, because redesigning embedded systems is hard and new chips aren’t that much better

## Slide 38: Popular components rarely die
Majority of popular older options still exist
  Designers can trade off cost, capability, and efficiency alongside “modern features”
Upgrading for an existing product is unlikely
  Large cost, little benefit
Example: Arduino still primarily uses AVR
  Works just fine for its needs
  Also releases new boards with nRF52s (Arduino Nano 33 BLE)

## Slide 39: Fall 2024: cheapest microcontroller
ATTINY10-TSHR
  8-bit custom architecture
  32 bytes of RAM
  1 kB of Flash
  4 I/O pins
  $0.44 per microcontroller
    Still an “active” chip being manufactured

## Slide 40: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 41: Microcontroller knowledge is transferrable
Your knowledge of microcontrollers applies to almost all of them
  They have similar peripherals that work in similar ways
The exact names and configurations will definitely be different
  But the fundamentals stay the same
Let’s prove this with a quick view of two microcontrollers
  Atmel SAM4L
  Texas Instruments MSP430

## Slide 42: Atmel SAM4L Microcontroller
ARM Cortex M4F (same processor!)
Lots of very configurable peripherals
  USART, SPI, TWI, I2S, DAC, ADC, Timer, …
  Kind of a “do-everything” microcontroller

## Slide 43: SAM4L GPIO
GPIO register map (heavily abbreviated)

## Slide 44: Setting or clearing individual bits
Actually, each register appears four times in a row
  Read/write version
  Set version (like nRF *SET)
  Clear version (like nRF *CLR)
  Toggle version

## Slide 45: SAM4L Timers
Three 16-bit timers
  Each of which can have multiple inputs clock signals with prescaler values
  Timers can be chained together to make up to a 48-bit timer
One register for reading counter
Three registers for “compare interrupts”

## Slide 46: SAM4L PWM
PWM peripheral is essentially built into Timer peripheral
Timer peripheral also supports a “Waveform” mode where it generates an output GPIO signal, i.e. PWM
One comparison point is low-to-high transition, another is high-to-low transition

## Slide 47: Texas Instruments MSP430 (MSP430FR59xx)
Example of a very different microcontroller
16-bit custom architecture processor
2 kB RAM
64 kB FRAM
  Non-volatile, byte-writable

## Slide 48: MSP430 GPIO register map
Registers are a single byte in size
Oddly, some have an “undefined” reset state 😱

## Slide 49: Example MSP430 GPIO register: OUT
Example 8-bit register. Controls 8 pins in a GPIO “port”

## Slide 50: MSP430 Timer peripheral
A choice of input clocks goes through dividers to run a 16-bit timer
  Five total timers available on the system
  Some can trigger external output pins, some are only internal

## Slide 51: MSP430 PWM
The MSP430 Timer peripheral handles PWM as well!

## Slide 52: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 53: Microprocessor system design
What about modern microprocessors? (really SoC’s)
  Similar idea, but a LOT more stuff
Various peripherals, which might not be focused on sensor I/O
  Less ADCs and I2C more Ethernet and Graphics
External memory busses
  Microprocessors expect external memory to exist on the system
  Which means that they need pins for an external memory bus

## Slide 54: Beaglebone
Cheap, single board computer
  Like Raspberry Pi
Gross diagram that’s actually in their datasheet

## Slide 55: Resources on the Beaglebone and its microprocessor
https://beagleboard.org/bone-original
https://beagleboard.org/static/beaglebone/BEAGLEBONE_SCHEM_A3.pdf
https://transistor-man.com/files/emu/beaglebone_hardware/BONE_SRM.pdf
https://www.ti.com/product/AM3358

## Slide 56: AM3358 processor
ARM Cortex A8
  32-bit processor
  1 GHz clock
  300 pins!!
Internal memory
  176 kB ROM
  64 kB RAM
External memory
  DDR2/3, 400 MHz RAM
  NAND or NOR Flash

## Slide 57: AM3358 peripherals
Advanced peripherals
  Graphics
  Ethernet
  USB, CAN
Regular peripherals
  GPIO, Timers
  ADC
  UART, SPI, I2C

## Slide 58: How much bigger is a microprocessor?
nRF52833 datasheet:
  600 pages total
AM3358 datasheet:
  250 pages of electrical information
  5000 pages of peripheral information
  And it’s not that the basic peripherals are much larger
    UART: 60 pages
    I2C: 20 pages
    Four different timers at ~30 pages each

## Slide 59: Memory interface - DDR
Double Data Rate (DDR)
Address bits
  17 pins (3 bank, 14 address)
  Bank + Address selects a 2 kB chunk out of 2 GB
Data bits
  16 pins
Clocks, Chip select
Various sequencing signals
Pinout on the Beaglebone

## Slide 60: Break + Question
Wires (traces) for high-speed busses like memory must be match, to ensure that all are exactly the same length. Why?

## Slide 61: Break + Question
Wires (traces) for high-speed busses like memory must be match, to ensure that all are exactly the same length. Why?
Speed of electricity in the wires matters
If one wire is a foot longer than the others, its signal arrives 1 ns late
  Even fractions of nanoseconds could matter for high-speed communication

## Slide 62: Flash interface - MMC
Multi-media Card interface
  Used to communicate with SD Cards
  Also for eMMC Flash chips (which act like SD Cards, but soldered in place)
For SD cards SPI can usually be used
For eMMC 4-bit version of interface
  Clock
  Command
  Data 0, 1, 2, 3
Pinout on the Beaglebone

## Slide 63: Ethernet interface - RMII
Reduced Media-Independent Interface (RMII)
Pinout on the Beaglebone

## Slide 64: Other processor pinouts on the Beaglebone
Lots of acronyms that we recognize!
Analog inputs
UARTs
I2C
GPIOs
Timers

## Slide 65: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs

## Slide 66: FPGA systems
When else might you run into large busses like memory?
On an FPGA!
  Field-Programmable Gate Array (FPGA)
  Configurable hardware
    Engineers write a description of the hardware (Verilog or VHDL)
    FPGA implements that hardware
  Much faster than software, but still slower than a custom chip

## Slide 67: Combined FPGA + Microcontroller

## Slide 68: Busses: AHB vs APB
Advanced High-performance Bus (AHB)
  Multiple bus controllers
  Pipelined operation
  Burst transfers of data
  Used for high-speed memory operations
Advanced Peripheral Bus (APB)
  Simpler interface
  Lower power
  Used for most peripheral communication

## Slide 69: APB usage
Bus has three states
  IDLE
    Nothing is happening
    Default
  SETUP
    A transfer of data is about to happen
    Address and configuration signals are set
  ACCESS
    Data is actually transferred over the bus

## Slide 70: Example APB write operation
Setup phase begins
with this rising edge
Setup
Phase
Access
Phase

## Slide 71: Example APB read operation
Setup
Phase
Access
Phase
Setup phase begins
with this rising edge

## Slide 72: With an FPGA you can create your own peripherals
Busses can be exposed to the FPGA for it to use
Example use case
  Custom camera with selectable pixel lines and an ADC
  Don’t want to manually control it with software (too slow)
  Create a hardware peripheral on the FPGA that takes software commands like “grab a frame” and implements them

## Slide 73: Example register map
Verilog HDL that describes a register map
Reads in the address from the bus to determine which register is written to
Modifies internal registers based on the bits of the data

## Slide 74: Performing peripheral operations
On every clock edge, check status registers
If they are active, iterate through a state machine
  Possibly many states to make the actual operation occur

## Slide 75: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Microcontroller history
  Other microcontroller peripherals
  Microprocessors
  FPGAs