## Slide 1: Lecture 04 BLE Advertisement Deep Dive
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2022
Materials in collaboration with Pat Pannuto (UCSD)

## Slide 2: Announcements
Reminder – Lab1: Wireshark
  Due Thursday by 11:59 pm
  Late policy: 50% of points if submitted within a week of deadline
Project Proposals
  Due next week Friday (04/22) by 11:59 pm
  Added details about what to include on Canvas assignment
    Submit PDF to Gradescope
Hardware for labs
  I have some! I’ll pass out after class today/Thursday

## Slide 3: Today’s Goals
Describe BLE advertising and scanning roles
Deep dive into advertisements. Questions we might ask as researchers.
  How much energy do advertisements take?
  What is the probability of receiving a packet?
    What is the probability of receiving data?
  What are the real-world use cases of advertisements?

## Slide 4: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions

## Slide 5: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 6: Advertising
BLE discovery mechanism
  Make nearby devices aware of advertiser’s existence
  Communicate some information from or about advertiser
  Traditional purpose is to enable connections, but this is also useful for general communication
Advertisements
  Periodic broadcast messages with data
Scan Requests/Responses
  Scanner sends responses after getting a request
    Only occurs when scanner is listening
  Almost literally “bonus advertisement data”

## Slide 7: Advertising packet layering

## Slide 8: BLE advertising header
ADV_IND
  Advertisement
  Allows connections and scan requests
ADV_NONCONN_IND
  Advertisement
  No connections or scan requests
ADV_SCAN_IND
  Advertisement
  No connections but allows scan requests
SCAN_REQ
  Scan request
SCAN_RSP
  Scan response

## Slide 9: Advertisement payloads
AdvA – address of the advertiser
  TxAdd bit from header specifies if this is a “public” or “random” address
Remaining up to 31 bytes are available for use
Putting it all together, up to 47 bytes total:
Preamble 1 Byte | Access Address 4 Bytes | Header 2 Bytes | Advertiser Address 6 Bytes | Advertiser Data (Payload) 0-31 Bytes | CRC 3 Bytes
BLE Packet
Advertising PDU

## Slide 10: Scan Requests and Responses
Scan request
  Just the two addresses: the scanner’s and the advertiser’s
Scan response
  Identical to an advertisement
  But only occurs after a request

## Slide 11: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why?
User picks the rate as a tradeoff of energy and discovery latency

## Slide 12: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why? Avoid repeat collisions
User picks the rate as a tradeoff of energy and discovery latency

## Slide 13: Advertising event
Three transmissions, one on each advertising channel
  Always in the same order
Transmission, followed by listening window on that same channel
  Requests will be sent >=150 us (Inter-Frame Spacing, IFS) after Tx
  Followed by a retune to the next channel frequency
This short listen window is the magic “low energy” part

## Slide 14: Preserving energy in communication
Most energy is spent listening
  This is due primarily to how long listening durations are compared to transmissions
Example: maximum-sized BLE transmission:
  8 bits/byte * 47 bytes = 376 bits at 1 Mbps = 0.376 ms transmitting
  So listening for an entire second is >2500 times longer
  But listening for only 0.376 ms requires sub-ms synchronization, which itself costs energy to manage…
  Instead, when advertising, nRF radios listen for ~0.200 ms, only after a transmission

## Slide 15: Payload of an advertisement
What do you stick in the BLE payload anyways?
  Theoretically whatever you want, but that isn’t very compatible
  Point is to specify capabilities of the advertiser
Desire: specify payloads in such a way that all scanners can interpret what they mean about the device
  This is different from traditional internet packets
  Broadcasts are for _anyone_ to hear, not a specific server/application
Which fields are or aren’t present is device-specific
  A lot more possible fields than will really be used on any device

## Slide 16: TLV Format
Type – Length – Value (Wikipedia)
  Actually, BLE does the length part first
  Scanner can hop through length/type pairs to find what interests it

## Slide 17: Payload types
Listed in the Core Specification Supplement [Supplement v9]
  Each might have their own considerations about AD Data format
Flags (supported modes: BLE and Bluetooth) required by Apple?
Name
Service UUID
TX Power Level
Manufacturer-specific data
And about twenty others

## Slide 18: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions

## Slide 19: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle?

## Slide 20: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle? Save energy

## Slide 21: A warning about scanning expectations
Scanners will NOT receive 100% of packets sent
  Even ignoring range issues
Packets are lost due to (in roughly descending order):
  Duty cycle
  Sharing 2.4 GHz antenna with WiFi
  Retune period after each scanning interval
  Dropped packets in the receive software
  Packet collisions

## Slide 22: Break + Putting it all together
Advertisements are received when the channel of the scan window and the channel of the advertisement overlap in time (and space)

## Slide 23: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions

## Slide 24: Advertisements are already being used for communication.
BLE advertisements are uncoordinated, broadcast messages designed for discovery.
Devices are being deployed using advertisements.
  Beacons – iBeacon
  Tracking – Tile
  Local communication – Apple Continuity
  Sensor deployments – PowerBlade
Notes: PowerBlade is a great example of this.
  It’s a plug-load power meter
  Initially configured to use advertisements as a simple method for reading measurements with a smartphone
  We are interested in household deployments where dozens of PowerBlades will be deployed to measure all the loads in a home
  Can we still use BLE advertisements for data transfer in the presence of many other devices?

## Slide 25: Beacons
Advertising with advertisements!
Web of Things
  Real-world tags that broadcast virtual-world identifiers
iBeacon and Eddystone
  Formats for sending URLs and device identifiers
  Use existing BLE fields (Service Data and Manufacturer-Specific Data)

## Slide 26: Tracking
Find devices nearby
  Get a sense of distance to the device
Find my X
  Tile: find my keys
  Apple: find my device
Uses TX power level field
  Lists the transmitted power of the device
  Pathloss = TX power – RSSI (all in dBm)

## Slide 27: Problem with RSSI-based distance – not accurate
Pathloss is NOT only due to distance
RSSI is way worse at this than you hope it would be
Citation: literally everyone has made this figure at some point

## Slide 28: Local communication: Apple Continuity
Communication with only nearby devices
Apple Continuity
Martin, Jeremy, et al. "Handoff all your privacy–a review of apple’s bluetooth low energy continuity protocol." Proceedings on Privacy Enhancing Technologies 2019.4 (2019): 34-53.

## Slide 29: Local Communication: Exposure Notifications
Apple and Google collaboration to use phones for contact tracing
  Smartphone constantly broadcasts identifier.
  Periodically, each smartphone listens for broadcasts around it.
  Check list of identifiers to see if you’ve been around someone who is sick.
Requires government/healthcare system interactions to determine when an identifier should be flagged as sick
  24 states (not Illinois) adopted this
Implemented at OS level in background

## Slide 30: Sensor deployments
Report data so gateways and users can retrieve it simultaneously
  Easy introspection during a deployment
  Satisfy users’ curiosity
Ignore difficult questions about networking
  Just broadcast the data!
DeBruin, Samuel, et al. "Powerblade: A low-profile, true-power, plug-through energy meter." Proceedings of the 13th ACM Conference on Embedded Networked Sensor Systems. 2015.

## Slide 31: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions

## Slide 32: Paper: power measurements of BLE advertisements
Schrader, Raphael, et al. "Advertising power consumption of bluetooth low energy systems." 2016 3rd International Symposium on Wireless Systems within the Conferences on Intelligent Data Acquisition and Advanced Computing Systems (IDAACS-SWS). IEEE, 2016.

## Slide 33: Energy model for BLE advertisements
Creates a set of states and metrics for how much power each uses and for what duration
  power * duration = energy

## Slide 34: Measurements of Power Use
Power use and duration (energy)
  nRF51 (nRF51822)
  nRF52 (nRF52832)

## Slide 35: How much energy does it cost to send data over advertisements?
Configuration
  nRF51822 microcontroller
  Maximum payload size
  +4 dBm transmit power
  Connectable advertisement
  Sleep power 11 µW
One packet per second example:
  110 µW average
  ~270 days on a CR2032
One packet per minute example:
  13 µW average
  ~2250 days on a CR2032

## Slide 36: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions

## Slide 37: Questions about network capability
What are the odds that a transmitted advertisement will be received?
  Packet reception rate
If M redundant advertisements are sent instead, what are the odds that at least one are received?
  Data reception rate
How do these odds vary with number of devices, advertising interval, and packet size?

## Slide 38: BLE advertisements are periodic, broadcast transmissions.
Advertisement events occur periodically (Tadv_interval: 20 ms–10 s).
Random delay appended before each transmission (tadv_delay: 0–10 ms).
Data payload of up to 31 bytes.
time
Tadv_interval
+ tadv_delay
advertisement event
advertisement event
Bluetooth SIG. Bluetooth Core Specification 4.2. (2014).
Notes: How does communication work with BLE advertisements?
Each advertisement has a payload, which we can place sensor data in.
If data naturally has a periodic update rate, we can match the advertisement interval to that, so each advertisement has new sensor data.

## Slide 39: What causes transmissions not to be received?
Not within range of the gateway.
  Or various other losses within the gateway itself
Two devices try to send at the same time (packet collision).
broadcast domain
X
X

## Slide 40: What is the probability of a packet collision?
Packet 0
time
tadv_0
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).

## Slide 41: What is the probability of a packet collision?
Packet 0
Packet 1
time
tadv_0
tadv_1
Packet 1
Packet 1
Packet 1
Packet 1
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).
Notes: Collisions occur if any part of the two packets overlap
  Particularly true for BLE that only has an 8-bit preamble

## Slide 42: What is the probability of a packet collision?
Packet 0
Packet 1
time
tadv_0
tadv_1
=
Probability of Collision
=
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).
Notes: The vulnerable period is the sum of the two advertisement durations
While the transmission window is the advertisement interval plus the expected value of the random delay

## Slide 43: Break + Determine Probability of Multiple Failures
Given:
  Probability of Collision
Determine:
  Probability of Reception for data sent redundantly across M packets

## Slide 44: Break + Determine Probability of Multiple Failures
Given:
  Probability of Collision
Determine:
  Probability of Reception for data sent redundantly across M packets
  i.e., what are the odds that at least one of the packets doesn’t collide
  1 – (Probability of CollisionM)
    (Pc)M = Probability that all of them collide
    1-that = Probability that NOT all of them collide

## Slide 45: How do we determine reception rate?
With redundancy, we care about data reception instead of packet reception.
Naïve model:
Data Reception Assumption: repeat packet collisions are independent.
  True for any arbitrary selection of two BLE devices
  False for two devices that have recently collided
Notes: Earlier we demonstrated the probability of collision, which can be used to determine packet reception rates.
Now with redundancy, we don’t care about the reception of any one packet, but the reception rate of the data that is being sent over them.
Naively, we can take the probability of collision and repeat it for any number of redundant packets.
There is an assumption in that model that repeat collisions are independent, which I’ll show you is false.

## Slide 46: When are transmissions from two devices independent?
Assumption is true for any BLE device that has been advertising for some time
  Sum of random delays grows the uncertainty of transmission.
  Applied to periodic transmissions, any point in interval becomes equally likely.
    Range of 1x delay, 2x delay, 3x delay, until it wraps
time
Tadv_interval
delay
Tadv_interval
delay
Tadv_interval
delay

## Slide 47: When are transmissions from two devices NOT independent?
Independence assumption is false for two BLE devices that have recently collided.
  If Tadv_interval is identical, next transmissions with be close in time.
  Collision is determined by difference of random delays.
  Further repeat collisions have the same probability of occurrence.
time
Tadv_interval
delay
New time period collisions could occur within
Notes: If two devices have collided before, and have the same interval, at the next period they will certainly collide again.
BLE has a random delay appended to reduce this possibility.
But we’ve now greatly reduced the transmission window that the a collision could occur in. We can calculate this to determine a distinct probability of repeat collision.
Note that further repeat collisions are bounded by the same difference of random delays, and therefore have the probability of a second repeat collision is the same as the probability of a first repeat collision.

## Slide 48: Calculating probability of a repeat collision
Difference of two uniform random delays forms a triangular distribution
difference in transmission time
probability
tadv_0
tadv_1
Probability of Repeat Collision

## Slide 49: Important lesson: spend time on things that are important
How important was accounting for repeat collisions?
Maximum error is about a 1% change in Data Reception Rate.
This is due to size of delay 10 ms compared to size of transmission ~300 µs.
200 ms interval advertisements

## Slide 50: Equations for modeling data transmissions
Packet Reception Rate
  Probability that at the transmitted packet does not have a collision with any of N transmitting devices
Data Reception Rate
  Probability that at least one of M redundant packets does not have a collision with any of N transmitting devices

## Slide 51: Is the model valid?
Empirical testing setup:
  50 devices
  1 meter from scanner
  5-10 cm apart
Transmit monotonically increasing sequence numbers.
Sweep number of devices and advertising intervals.

## Slide 52: The model is accurate across advertisement rates and deployment sizes.
Accuracy is fairly consistent across intervals.
The model consistently overestimates the measured PRR values.
The effect could be due to RF interference.

## Slide 53: The model accurately accounts for redundancy as well.
The same dataset can be used to measure the effect of redundancy by grouping sets of sequence numbers.
The model again slightly overestimates, but error reduces quickly as DRR approaches 100%.

## Slide 54: What questions can we answer with a collision model?
Original questions
  What are the odds that a transmitted advertisement will be received?
  If M redundant advertisements are sent instead, what are the odds that at least one are received?
  How do these odds vary with number of devices, advertising interval, and packet size?
Additional questions
  Can redundancy make advertisements reliable?
  Is it better to transmit often for high redundancy or rarely for less congestion?

## Slide 55: Redundancy results in high DRR even with many devices.
In this example, a sensor has new data once per second and sends it in 1-3 packets.
Even without redundancy, data reception rates never fall below 87% even with 200 devices in a deployment, assuming no interference.

## Slide 56: Redundancy is (normally) better than less congestion.
Design question:
Send more packets to gain from redundancy? OR
Send less packets to reduce congestion?
The answer changes, but only with many devices.
Notes: This plot changes with advertisement rate, and can get as low as 100 devices

## Slide 57: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions
  Bonus: Scan Responses

## Slide 58: Scan requests/responses seem intriguing
Why not send most data in scan responses instead of advertisements?
  Theoretically could reduce energy costs
Scan we use scan requests as a form of acknowledgement?
  Could relieve need for redundant transmissions
Problem: scan requests/responses don’t work all that well

## Slide 59: Scan Requests and Responses are broken
Goal: provide a little extra advertisement data on demand
Problem: exponential backoff for lost messages
  If there is a request without a response, scanners assume collision with another scanner and exponentially back off from requesting
  But collisions are far more likely between a device and a scanner, which should not have back off
  Result is that scan requests will occur far less frequently than expected
  Instead, just send additional advertisements with different data
  Kravets, Robin, Albert F. Harris III, and Roy Want. "Beacon trains: blazing a trail through dense BLE environments." Proceedings of the Eleventh ACM Workshop on Challenged Networks. 2016.

## Slide 60: Outline
BLE roles
  Advertising
  Scanning
Communicating with advertisements
  Advertisement Use Cases
  Energy Use
  Packet Collisions
  Bonus: Scan Responses