## Slide 1: Lecture 04 BLE Advertisement Deep Dive
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021

## Slide 2: Announcements
I updated the Project Proposal link on canvas with additional information about your proposal
  https://canvas.northwestern.edu/courses/133790/assignments/841765
Reminder: due end-of-day on the 1st
  Come talk to me in office hours about your project before then if you’ve got questions or concerns
  Also feel free to post project ideas on campuswire

## Slide 3: Today’s Goals
Describe BLE scanning role
Deep dive into advertisements. Questions we might ask as researchers.
  How much energy do advertisements take?
  What is the probability of receiving a packet?
    What is the probability of receiving data?
  What are the real-world use cases of advertisements?

## Slide 4: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases

## Slide 5: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle?

## Slide 6: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle? Save energy

## Slide 7: Putting it all together
Advertisements are received when the channel of the scan window and the channel of the advertisement overlap in time (and space)

## Slide 8: A warning about scanning expectations
Scanners will NOT receive 100% of packets sent
  Even ignoring range issues
Packets are lost due to (in roughly descending order):
  Duty cycle
  Sharing 2.4 GHz antenna with WiFi
  Retune period after each scanning interval
  Dropped packets in the receive software
  Packet collisions

## Slide 9: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases

## Slide 10: Paper: power measurements of BLE advertisements
Schrader, Raphael, et al. "Advertising power consumption of bluetooth low energy systems." 2016 3rd International Symposium on Wireless Systems within the Conferences on Intelligent Data Acquisition and Advanced Computing Systems (IDAACS-SWS). IEEE, 2016.

## Slide 11: Energy model for BLE advertisements
Is this valuable?
  Is this surprising?
Does this seem accurate?
  When does it apply?

## Slide 12: Measurements of Power Use
Power use and duration (energy)
  nRF51 (nRF51822)
  nRF52 (nRF52832)
Does this seem accurate?
  What conditions are the tests performed under?

## Slide 13: Overall thoughts on the paper?
Any additional thoughts?
Grad students: is this a good paper?
  And how are you defining good?

## Slide 14: Overall thoughts on the paper?
Any additional thoughts?
Grad students: is this a good paper?
  And how are you defining good?
Note: I think this would make an excellent class project.
  ~70-80% of this would be sufficient for a good grade.

## Slide 15: How much energy does it cost to send data over advertisements?
Configuration
  nRF51822 microcontroller
  Maximum payload size
  +4 dBm transmit power
  Connectable advertisement
  Sleep power 11 µW
One packet per second example:
  110 µW average
  ~270 days on a CR2032
One packet per minute example:
  13 µW average
  ~2250 days on a CR2032

## Slide 16: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases

## Slide 17: Questions about network capability
What are the odds that a transmitted advertisement will be received?
  Packet reception rate
If M redundant advertisements are sent instead, what are the odds that at least one are received?
  Data reception rate
How do these odds vary with number of devices, advertising interval, and packet size?

## Slide 18: BLE advertisements are periodic, broadcast transmissions.
Advertisement events occur periodically (Tadv_interval: 20 ms–10 s).
Random delay appended before each transmission (tadv_delay: 0–10 ms).
Data payload of up to 31 bytes.
time
Tadv_interval
+ tadv_delay
advertisement event
advertisement event
Bluetooth SIG. Bluetooth Core Specification 4.2. (2014).
Notes: How does communication work with BLE advertisements?
Each advertisement has a payload, which we can place sensor data in.
If data naturally has a periodic update rate, we can match the advertisement interval to that, so each advertisement has new sensor data.

## Slide 19: What causes transmissions not to be received?
Not within range of the gateway.
  Or various other losses within the gateway itself
Two devices try to send at the same time (packet collision).
broadcast domain
X
X

## Slide 20: What is the probability of a packet collision?
Packet 0
time
tadv_0
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).

## Slide 21: What is the probability of a packet collision?
Packet 0
Packet 1
time
tadv_0
tadv_1
Packet 1
Packet 1
Packet 1
Packet 1
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).
Notes: Collisions occur if any part of the two packets overlap
  Particularly true for BLE that only has an 8-bit preamble

## Slide 22: What is the probability of a packet collision?
Packet 0
Packet 1
time
tadv_0
tadv_1
=
Probability of Collision
=
Jeon, Wha Sook, et al. "Performance analysis of neighbor discovery process in bluetooth low-energy networks." (IEEE Transactions on Vehicular Technology, 2016). Perez-Diaz de Cerio, David, et al. "Analytical and experimental performance evaluation of BLE neighbor discovery process including non-idealities of real chipsets." (Sensors, 2017).
Notes: The vulnerable period is the sum of the two advertisement durations
While the transmission window is the advertisement interval plus the expected value of the random delay

## Slide 23: How do we determine reception rate?
With redundancy, we care about data reception instead of packet reception.
Naïve model:
Data Reception Assumption: repeat packet collisions are independent.
  True for any arbitrary selection of two BLE devices
  False for two devices that have recently collided
Notes: Earlier we demonstrated the probability of collision, which can be used to determine packet reception rates.
Now with redundancy, we don’t care about the reception of any one packet, but the reception rate of the data that is being sent over them.
Naively, we can take the probability of collision and repeat it for any number of redundant packets.
There is an assumption in that model that repeat collisions are independent, which I’ll show you is false.

## Slide 24: When are transmissions from two devices independent?
Assumption is true for any BLE device that has been advertising for some time
  Sum of random delays grows the uncertainty of transmission.
  Applied to periodic transmissions, any point in interval becomes equally likely.
    Range of 1x delay, 2x delay, 3x delay, until it wraps
time
Tadv_interval
delay
Tadv_interval
delay
Tadv_interval
delay

## Slide 25: When are transmissions from two devices NOT independent?
Independence assumption is false for two BLE devices that have recently collided.
  If Tadv_interval is identical, next transmissions with be close in time.
  Collision is determined by difference of random delays.
  Further repeat collisions have the same probability of occurrence.
time
Tadv_interval
delay
New time period collisions could occur within
Notes: If two devices have collided before, and have the same interval, at the next period they will certainly collide again.
BLE has a random delay appended to reduce this possibility.
But we’ve now greatly reduced the transmission window that the a collision could occur in. We can calculate this to determine a distinct probability of repeat collision.
Note that further repeat collisions are bounded by the same difference of random delays, and therefore have the probability of a second repeat collision is the same as the probability of a first repeat collision.

## Slide 26: Calculating probability of a repeat collision
Difference of two uniform random delays forms a triangular distribution
difference in transmission time
probability
tadv_0
tadv_1
Probability of Repeat Collision

## Slide 27: Important lesson: spend time on things that are important
How important was accounting for repeat collisions?
Maximum error is about a 1% change in Data Reception Rate.
This is due to size of delay 10 ms compared to size of transmission ~300 µs.
200 ms interval advertisements

## Slide 28: Equations for modeling data transmissions
Packet Reception Rate
  Probability that at the transmitted packet does not have a collision with any of N transmitting devices
Data Reception Rate
  Probability that at least one of M redundant packets does not have a collision with any of N transmitting devices

## Slide 29: Is the model valid?
Empirical testing setup:
  50 devices
  1 meter from scanner
  5-10 cm apart
Transmit monotonically increasing sequence numbers.
Sweep number of devices and advertising intervals.

## Slide 30: The model is accurate across advertisement rates and deployment sizes.
Accuracy is fairly consistent across intervals.
The model consistently overestimates the measured PRR values.
The effect could be due to RF interference.

## Slide 31: The model accurately accounts for redundancy as well.
The same dataset can be used to measure the effect of redundancy by grouping sets of sequence numbers.
The model again slightly overestimates, but error reduces quickly as DRR approaches 100%.

## Slide 32: What questions can we answer with a collision model?
Original questions
  What are the odds that a transmitted advertisement will be received?
  If M redundant advertisements are sent instead, what are the odds that at least one are received?
  How do these odds vary with number of devices, advertising interval, and packet size?
Additional questions
  Can redundancy make advertisements reliable?
  Is it better to transmit often for high redundancy or rarely for less congestion?

## Slide 33: Redundancy results in high DRR even with many devices.
In this example, a sensor has new data once per second and sends it in 1-3 packets.
Even without redundancy, data reception rates never fall below 87% even with 200 devices in a deployment, assuming no interference.

## Slide 34: Redundancy is (normally) better than less congestion.
Design question:
Send more packets to gain from redundancy? OR
Send less packets to reduce congestion?
The answer changes, but only with many devices.
Notes: This plot changes with advertisement rate, and can get as low as 100 devices

## Slide 35: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases

## Slide 36: Advertisements are already being used for communication.
BLE advertisements are uncoordinated, broadcast messages designed for discovery.
Devices are being deployed using advertisements.
  Beacons – iBeacon
  Tracking – Tile
  Local communication – Apple Continuity
  Sensor deployments – PowerBlade
Notes: PowerBlade is a great example of this.
  It’s a plug-load power meter
  Initially configured to use advertisements as a simple method for reading measurements with a smartphone
  We are interested in household deployments where dozens of PowerBlades will be deployed to measure all the loads in a home
  Can we still use BLE advertisements for data transfer in the presence of many other devices?

## Slide 37: Beacons
Advertising with advertisements!
Web of Things
  Real-world tags that broadcast virtual-world identifiers
iBeacon and Eddystone
  Formats for sending URLs and device identifiers
  Use existing BLE fields (Service Data and Manufacturer-Specific Data)

## Slide 38: Tracking
Find devices nearby
  Get a sense of distance to the device
Find my X
  Tile: find my keys
  Apple: find my device
Uses TX power level field
  Lists the transmitted power of the device
  Pathloss = TX power – RSSI (all in dBm)

## Slide 39: Problem with RSSI-based distance – not accurate
Pathloss is NOT only due to distance
RSSI is way worse at this than you hope it would be
Citation: literally everyone has made this figure at some point

## Slide 40: Local communication
Communication with only nearby devices
Apple Continuity
Martin, Jeremy, et al. "Handoff all your privacy–a review of apple’s bluetooth low energy continuity protocol." Proceedings on Privacy Enhancing Technologies 2019.4 (2019): 34-53.

## Slide 41: Sensor deployments
Report data so gateways and users can retrieve it simultaneously
  Easy introspection during a deployment
  Satisfy users’ curiosity
Ignore difficult questions about networking
  Just broadcast the data!
DeBruin, Samuel, et al. "Powerblade: A low-profile, true-power, plug-through energy meter." Proceedings of the 13th ACM Conference on Embedded Networked Sensor Systems. 2015.

## Slide 42: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases
Bonus: Scan Responses

## Slide 43: Scan requests/responses seem intriguing
Why not send most data in scan responses instead of advertisements?
  Theoretically could reduce energy costs
Scan we use scan requests as a form of acknowledgement?
  Could relieve need for redundant transmissions
Problem: scan requests/responses don’t work all that well

## Slide 44: Scan Requests and Responses are broken
Goal: provide a little extra advertisement data on demand
Problem: exponential backoff for lost messages
  If there is a request without a response, scanners assume collision with another scanner and exponentially back off from requesting
  But collisions are far more likely between a device and a scanner, which should not have back off
  Result is that scan requests will occur far less frequently than expected
  Instead, just send additional advertisements with different data
  Kravets, Robin, Albert F. Harris III, and Roy Want. "Beacon trains: blazing a trail through dense BLE environments." Proceedings of the Eleventh ACM Workshop on Challenged Networks. 2016.

## Slide 45: Outline
BLE roles
  Advertising
  Scanning
Energy Use
Packet Collisions
Advertisement Use Cases
Bonus: Scan Responses