## Slide 1: Lecture 06 802.15.4
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021

## Slide 2: Today’s Goals
Introduction to 802.15.4
Overview of physical layer details
Exploration of link layer
  Network topologies
  Communication structure
  Access control
  Packet structure

## Slide 3: References
802.15.4 Specification [2006]
  “Part 15.4: Wireless Medium Access Control (MAC) and Physical Layer (PHY) Specifications for Low-Rate Wireless Personal Area Networks (WPANs)”
Other helpful references:
  Paper introducing the 802.15.4 draft
  NXP 802.15.4 Stack User Guide
  2005 presentation on 802.15.4

## Slide 4: Outline
Overview
Physical Layer
Link Layer
Packet Structure

## Slide 5: Comparison of networks
Data
Throughput
Range

## Slide 6: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range

## Slide 7: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range
There are some missing qualities here. Why be closer to the origin?

## Slide 8: Comparison of networks
Bluetooth
WiFi
Cellular
BLE
802.15.4
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 9: IEEE 802
Network standards for variable-sized packets
  Ethernet
  WiFi
  WPANs
E.g. not networks that send periodic constant-sized packets

## Slide 10: IEEE 802.15
Wireless Personal-Area Networks (WPAN)
  All the things within the workspace of a person
  Conceptually smaller domain that the Local Area Network
  Realistically about the same thing as a LAN
Formerly included a Bluetooth spec
  Bluetooth SIG took over governance

## Slide 11: 802.15.4 Overview
Goals
  Explicit support for low-cost, low-power, low-throughput devices
  Focus on low complexity for specification
    Only PHY and MAC are part of specification
  Target home automation
    Secondarily industrial control/monitoring, vehicular sensing, and agricultural uses
Other contemporary technologies
  WiFi 802.11b and Bluetooth Classic
    Too complex in specification and overachieving in capability

## Slide 12: IEEE 802.15.4
Low-Rate Wireless PAN
  250 kbps, ~100 m range
  Radio hardware available with low-power and low-cost
Specification: 2003
  Also 2006, 2011, 2015, and 2020 revisions
    Mostly various added capabilities such as extra PHY layers
    Also define optional security, scheduling, and larger frame sizes
We’ll mostly work off of the 2006 version
  Thread is based on 2006 version
  Zigbee is based on the original 2003 version
  Roughly 200 pages of meaningful specification (100 of appendices)
    Compare to 3000 pages of Bluetooth/BLE

## Slide 13: Outline
Overview
Physical Layer
Link Layer
Packet Structure

## Slide 14: 802.15.4 Physical Layers
Multiple options of physical layers are supported
  We’ll focus on 2.4 GHz (2400 MHz)

## Slide 15: Physical Layer
O-QPSK modulation
  Offset Quadrature Phase-Shift Keying
  Twice the data rate of BPSK for same BER
  Cost: most complicated design of receivers
    Which is pretty minimal with all the transistors we’ve got
    Plus the ability to reuse previous designs
  4 bits per symbol
Symbols versus bits
  A symbol is the unit of data transfer for a modulated signal
    Does not necessarily correspond 1:1 with bits
  The rate of symbols per second is a baudrate
802.15.4 bit rate at 2.4 GHz: 250 kbps
  62.5 kBaud

## Slide 16: 802.15.4 RF channels
27 channels across three bands
5 MHz channel separation at 2.4 GHz
  Compare to 2 MHz for BLE

## Slide 17: Regional bands
Different RF bands have different regional availability
Also have different rules
  915 MHz: 400 ms dwell time
  868 MHz: 1% duty cycle

## Slide 18: Signal strength
Transmit power
  Typical: 0 dBm (remember: 1 mW)
Receiver sensitivity
  nRF52840 802.15.4: -100 dBm
    Compare to BLE sensitivity of -95 dBm
  Minimum acceptable: -85 dBm
  Circa-2006 radios (CC2420): -95 dBm
Which has longer range, 802.15.4 or BLE? Why?

## Slide 19: Signal strength
Transmit power
  Typical: 0 dBm (remember: 1 mW)
Receiver sensitivity
  nRF52840 802.15.4: -100 dBm
    Compare to BLE sensitivity of -95 dBm
  Minimum acceptable: -85 dBm
  Circa-2006 radios (CC2420): -95 dBm
Which has longer range, 802.15.4 or BLE? Why?
  802.15.4 with +5 dBm more margin; lower bit rate plays into this

## Slide 20: Outline
Overview
Physical Layer
Link Layer
Packet Structure

## Slide 21: 802.15.4 network topologies
Only specifies PHY and MAC, but has use cases in mind

## Slide 22: Star and Tree topologies
PAN Coordinator
  Receives and relays all messages
  Most capable and power-intensive
Coordinators (a.k.a. Routers)
  Control “clusters”
  Receives and relays to its children
  Communicates up to parent coordinator
End Devices
  Only communicate with single parent coordinator
  Least capable and power intensive

## Slide 23: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
What are disadvantages of mesh?

## Slide 24: Mesh networks
Most devices are capable of communicating with multiple neighbors
What are advantages of mesh?
  Devices can communicate over longer distances
  Device failures less likely to collapse the entire network
What are disadvantages of mesh?
  Some nodes have to spend more energy communicating
  Network protocol becomes more complicated to manage routing

## Slide 25: Reminder: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First, wait a random amount (collision avoidance part)
Then, listen for a duration and determine if anyone is transmitting (carrier sense part)
  If idle, you can transmit
  If busy, repeat step 1 (often increasing maximum wait time)
Can be combined with notion of slotting
  Synchronize to slots (smaller than transmit times)
  Wait for a number of slots
  Listen for idle slots

## Slide 26: Modes of operation
Beacon-enabled PAN
  Slotted CSMA/CA
  Structured communication patterns
  Optionally with some TDMA scheduled slots
Non-beacon-enabled PAN
  Unslotted CSMA/CA
  No particular structure for communication
    Could be defined by other specifications, like Thread or Zigbee

## Slide 27: Beacon-enabled superframe structure
Beacons occur periodically [15 ms – 245 seconds]
  Devices must listen to each beacon
Contention Access Period
  Slotted CSMA/CA synchronized by beacon start time
Inactive Period
  No communication occurring. Assumes sleepy devices
Contention Access Period
Beacon
Inactive Period
Beacon
…

## Slide 28: Guaranteed Time Slots (GTS)
PAN Coordinator may create a Contention Free Period with Guaranteed Time Slots
  TDMA schedule assigned to specific devices
  Slots eat up part of the Contention Access Period
  No CSMA/CA within a slot
Contention Access Period
Beacon
Inactive Period
Beacon
Guaranteed Time Slots
…

## Slide 29: Handling tree-based topologies
All coordinators listen to beacon from PAN coordinator
  And can participate in that contention period
Send their own beacons to child devices during inactive period
  Children participate in that contention period

## Slide 30: Non-beacon-enabled PAN
Same idea, just no beacons
  Which removes synchronization benefit (and slotted CSMA/CA)
  Also removes beacon listening cost
    Devices only need to check for activity before transmitting
  Still need an algorithm to determine when it should receive data
    All the time is a huge energy drain
    Algorithms can get complicated here
    Does BLE mechanism of listen-after-send apply?
Contention Access Period
…

## Slide 31: Non-beacon-enabled PAN
Same idea, just no beacons
  Which removes synchronization benefit (and slotted CSMA/CA)
  Also removes beacon listening cost
    Devices only need to check for activity before transmitting
  Still need an algorithm to determine when it should receive data
    All the time is a huge energy drain
    Algorithms can get complicated here
    Does BLE mechanism of listen-after-send apply?
      Only if sending to a high-power device, not among equals
Contention Access Period
…

## Slide 32: Receiving messages
Listen during entire contention period
  Can receive direct messages from any other device
  Can immediately respond to messages as well
Request messages from Coordinator
  Make all communication go through Coordinator
  Send a request-for-data packet to coordinator to get information
  Coordinator can include list of devices with pending data in beacon
More complicated listening algorithms are possible

## Slide 33: Clear Channel Assessment (CCA)
The “listen” part of CSMA/CA
Variety of implementations are acceptable
Energy above threshold
  Energy for 8 symbol durations above threshold (RSSI)
Carrier sense
  Valid 802.15.4 carrier signal
Energy AND/OR Carrier

## Slide 34: Slotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 35: Unslotted CSMA/CA operation
Have data to send
Wait for next backoff slot (synchronized from beacon)
Wait for 0-7 backoff slots (slot is 20 symbol durations: 320 us)
Listen for two empty slots
  Idle: Transmit
  Occupied: wait 0-15 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat (upper limit configurable)
    Next time: 0-31 backoff slots and repeat
    Next time: 0-31 backoff slots and repeat
    Timeout

## Slide 36: Outline
Overview
Physical Layer
Link Layer
Packet Structure

## Slide 37: Base packet format
Synchronization
  Preamble: four bytes of zeros
  Start-of-Packet: 0xA7
PHY Header
  One field: length 0-127
  Why still 8 bits?

## Slide 38: Base packet format
Synchronization
  Preamble: four bytes of zeros
  Start-of-Packet: 0xA7
PHY Header
  One field: length 0-127
  Why still 8 bits? Because computers depend on bytes

## Slide 39: MAC frame format
Sequence number
  8-bit monotonically increasing
Addressing fields
  PAN and addresses
  Varies based on frame type
Frame payload
  Depends on frame type
Frame check sequence
  16-bit CRC
Frame control
  Header

## Slide 40: Frame control
Frame type
  Type of payload included
Security enabled
  Packet is encrypted
  (extra 0-14 byte header)
Frame pending
  Fragmented packet
Acknowledgement required
PAN ID compression
  No PAN ID if intra-network
Addressing modes
  Which fields to expect
Why no length field?

## Slide 41: Frame control
Frame type
  Type of payload included
Security enabled
  Packet is encrypted
  (extra 0-14 byte header)
Frame pending
  Fragmented packet
Acknowledgement required
PAN ID compression
  No PAN ID if intra-network
Addressing modes
  Which fields to expect
Why no length field?
Already in prior header

## Slide 42: Frame types - Beacon
Beacon
  Information about the communication structure of this network
  Sent in response to requests from scanning devices
  Sent periodically at start of Superframes (if in use)
    Sent without CSMA/CA
MAC Header
  Source address only, broadcast to everyone
Packet contents
  Superframe details, including Guaranteed Time Slots (if any)
  Pending addresses lists devices for which Coordinator has data

## Slide 43: Frame types - Data
Data
  Data from higher-layer protocols
MAC Header
  Source and/or Destination addresses as necessary
Packet Contents
  Whatever bytes are desired (122 bytes – address sizes)
  May be fragmented across packets

## Slide 44: Frame types – MAC Command
MAC Command
  Various commands for supporting link layer
    Join/leave network
    Change coordinator within network
    Request data from coordinator
    Request Guaranteed Time Slot
MAC Header
  Source and/or Destination addresses as necessary

## Slide 45: Frame types - Acknowledgement
Acknowledgement
  Acknowledges a Data or MAC Command packet
  Not beacons or other acknowledgements
    What happens if acknowledgement isn’t received?
MAC Header
  Repeats Sequence Number of acknowledged packet
  No Source or Destination addresses
Sent TIFS after the packet it is acknowledging (immediately)

## Slide 46: Frame types - Acknowledgement
Acknowledgement
  Acknowledges a Data or MAC Command packet
  Not beacons or other acknowledgements
    What happens if acknowledgement isn’t received?
      Packet will be transmitted again
MAC Header
  Repeats Sequence Number of acknowledged packet
  No Source or Destination addresses
Sent TIFS after the packet it is acknowledging (immediately)

## Slide 47: Analysis: maximum goodput
Assume best possible case for data transmission
  122 Bytes per packet
    At 250 kbps -> 3.904 ms
  Plus Inter-frame spacing of 40 symbols
    At 62.5 kBaud -> 0.640 ms
  122 Bytes / 4.544 ms -> 214 kbps
    Compare to BLE advertisements: 9.92 kbps
    Compare to BLE connections: 520 kbps

## Slide 48: Outline
Overview
Physical Layer
Link Layer
Packet Structure