## Slide 1: Lecture 08 Analog Input
CE346 – Microprocessor System Design
Branden Ghena – Fall 2023
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Project proposals are due tonight!
  Plan is to get you project proposal feedback over the next several days
  18 out of 60 students submitted already (7 groups)
Remember to answer the post-lab questions on Canvas!
  You can do them late if you forget, but don’t forget

## Slide 3: Today’s Goals
Explore methods for sensing analog signals
  Comparators
  Analog-to-Digital Converters
Discuss nRF implementation of these peripherals

## Slide 4: Outline
Comparators (and nRF implementations)
General ADC Design
nRF ADC Implementation

## Slide 5: Analog signals
Exist in infinite states
  From a maximum to a minimum
Often used for interactions with the real world
  Sensors usually generate analog signals
Microbit example: microphone

## Slide 6: Interacting with analog signals
Microcontrollers are inherently digital
Need a method for translating analog signal into a digital one
Options:
  Determine if signal is higher or lower than some amount (Boolean)
  Determine voltage value of signal (N-bit number)

## Slide 7: Interacting with analog signals
Microcontrollers are inherently digital
Need a method for translating analog signal into a digital one
Options:
  Determine if signal is higher or lower than some amount (Boolean)
  Determine voltage value of signal (N-bit number)
  Determination is done by a Comparator

## Slide 8: General comparator design
Compares an analog input signal to a reference voltage
VOUT digital signal
  High: VIN > VREF
  Low: VIN < VREF
Advantages:
  Simple
  Low power

## Slide 9: Comparator design questions
What reference voltages are available?
  A few internal voltages
  Usually also allows external references from input pins
When is an output generated?
  Usually when status changes
    Low-to-high, High-to-low, Both (like GPIO interrupts)

## Slide 10: Hysteresis
A window added around signal state changes to prevent small amounts of noise from changing the output

## Slide 11: nRF low-power comparator (LPCOMP)

## Slide 12: nRF low-power comparator (LPCOMP)
Input: one of eight analog input pins

## Slide 13: nRF low-power comparator (LPCOMP)
Reference: one of two analog inputs or selection of VDD * N/16
  VDD: Input voltage of the system

## Slide 14: nRF low-power comparator (LPCOMP)
Hysteresis: +/- 50 mV range around VIN- when enabled

## Slide 15: nRF low-power comparator (LPCOMP)
Events: transition signals + ready (~150 μs startup time)

## Slide 16: nRF low-power comparator (LPCOMP)
Can also request what the current comparison state is (high/low)

## Slide 17: nRF low-power comparator (LPCOMP)
Can be used for low-power wakeup of microcontroller

## Slide 18: nRF COMP peripheral
Analog Comparator (not low power)
  More advanced version of a comparator (otherwise similar)
What advantages would a more capable comparator have?
  Configurable hysteresis
    LPCOMP: +/- 50 mV COMP: any of the N/64 voltage levels
  Faster detection
    LPCOMP: 5 μs COMP: 0.1-0.6 μs (depending on power mode)
  More possible reference voltages
    LPCOMP: VDD or input COMP: VDD, 1.2v, 1.8v, 2.4v, or input
    LPCOMP: 16 levels COMP: 64 levels

## Slide 19: nRF COMP peripheral

## Slide 20: Break + Question: Internal reference voltages
Why have internal voltage references other than VDD?

## Slide 21: Break + Question: Internal reference voltages
Why have internal voltage references other than VDD?
  What if want you want to measure is VDD?
    Battery voltage
    Did someone just unplug me?
    etc.
  What if VDD isn’t stable?
    Battery voltage
    Energy-harvesting system
    Hard to know what any particular value means…

## Slide 22: Outline
Comparators (and nRF implementations)
General ADC Design
nRF ADC Implementation

## Slide 23: Interacting with analog signals
Microcontrollers are inherently digital
Need a method for translating analog signal into a digital one
Options:
  Determine if signal is higher or lower than some amount (Boolean)
  Determine voltage value of signal (N-bit number)
  Translation is done by an Analog-to-Digital Converter (ADC)

## Slide 24: Quantization
Analog voltages are represented by discrete voltage levels
Comparators are 1-bit ADCs
  Split into two regions
  Good ADCs split into 4000-16000 regions
More levels gives a more accurate representation of the signal

## Slide 25: Translating voltage and ADC counts
VREF selects maximum range
Ground is usually minimum range
Resolution depends on hardware
  Either hardcoded or a selection
0 V
1 V
2 V
3 V
3.3 V
0 V
Analog
256
0
Digital (8-bit)
77
155
232
4096
0
Digital (12-bit)
1241
2482
3723

## Slide 26: Wait, shouldn’t that range have a -1 somewhere?
TLDR: no
  https://electronics.stackexchange.com/questions/286949/what-value-to-use-to-convert-adc-value-to-voltage
Each bit pattern represents a range of analog values
  Using 2Resolution minimizes the error for each bit within that range
Alternative important point:
  The error in an ADC will be +/- at least one bit anyways, so this doesn’t matter

## Slide 27: Quantization error
Resolution choice determines magnitude of error
  Each extra bit halves the magnitude of error

## Slide 28: Analog to digital translation process
Two steps:
Acquisition
  Read in signal for some amount of time
  Signal connected to a capacitor
  Fills capacitor up to voltage level
  Speed depends on input resistance
    1-100 μs is common
Conversion
  Determine which digital value the read signal corresponds to

## Slide 29: Direct-conversion ADC
Chain comparators together
  Each with a separate reference voltage
Digital value determined immediately
  Also known as “Flash” ADCs
Downside: needs 2n-1 comparators
  Reserved for expensive applications

## Slide 30: Successive-Approximation ADC
Method: Binary Search
  Compare signal to generated reference
  Increase or decrease reference as needed
  Repeat
DAC creates reference (Digital-to-Analog Converter)
  Final value of DAC is the ADC value

## Slide 31: Successive Approximation Example
4-bit ADC with an input signal VIN

## Slide 32: Successive Approximation Example
Compare ½ VREF (0b????) to VIN
  If VIN is greater, bit is 1. Else zero

## Slide 33: Successive Approximation Example
Compare ½ VREF (0b0???) to VIN
  If VIN is greater, bit is 1. Else zero
  VIN is less. So set that bit to zero

## Slide 34: Successive Approximation Example
2. Compare 1/4 VREF (0b0???) to VIN
  If VIN is greater, bit is 1. Else zero

## Slide 35: Successive Approximation Example
2. Compare 1/4 VREF (0b01??) to VIN
  If VIN is greater, bit is 1. Else zero
  VIN is greater. So set that bit to one

## Slide 36: Successive Approximation Example
3. Compare 3/8 VREF (0b01??) to VIN
  If VIN is greater, bit is 1. Else zero

## Slide 37: Successive Approximation Example
3. Compare 3/8 VREF (0b010?) to VIN
  If VIN is greater, bit is 1. Else zero
  VIN is less. So set that bit to zero

## Slide 38: Successive Approximation Example
4. Compare 5/16 VREF (0b010?) to VIN
  If VIN is greater, bit is 1. Else zero

## Slide 39: Successive Approximation Example
4. Compare 5/16 VREF (0b0101) to VIN
  If VIN is greater, bit is 1. Else zero
  VIN is greater. So bit is one

## Slide 40: Successive Approximation Example
5. Output is 5/16 VREF (0b0101)
  Slight underestimate of the real value, but as close as we can get
  More bits would get us even closer

## Slide 41: Successive Approximation Example
Performs a binary search to determine correct reference signal value
https://en.wikipedia.org/wiki/Successive-approximation_ADC

## Slide 42: Tradeoffs in ADC design
Direct-Conversion: more expensive (more silicon)
SAADC: more time consuming (more binary search time)
Most microcontrollers land on successive-approximation designs
  The slowdown isn’t an issue for slowly changing signals
  Quickly changing signals probably need special hardware anyways

## Slide 43: Break + Critical Thinking
How much ADC resolution is needed?

## Slide 44: Break + Critical Thinking
How much ADC resolution is needed?
  Resolution requirement depends on signal being sensed
  Temperature sensor probably doesn’t need 16-bit ADC
    Difference between 30.001℃ and 30.002℃ is usually irrelevant
  Microphone might though!
    Differences are audible until they are small enough
    16-bit or 24-bit tend to be common choices for audio data

## Slide 45: Outline
Comparators (and nRF implementations)
General ADC Design
nRF ADC Implementation

## Slide 46: nRF SAADC (Successive Approximation ADC)

## Slide 47: How most people use the SAADC

## Slide 48: How most people use the SAADC
8 different channel configurations
  Only one at a time
  Samples each, one after the other
Essentially virtualization in hardware!

## Slide 49: SAADC Resolution and Sampling
Resolution is selectable (for the whole peripheral)
  8, 10, 12, or 14 bits
  Result stored as 16-bit value regardless
Sampling time is selectable (for each channel)
  3-40 μs
  Longer sampling time is important for very low-current signals

## Slide 50: How most people use the SAADC
Input from analog pin (or VDD)

## Slide 51: Analog inputs on the Microbit
P0.30 is actually AIN6

## Slide 52: How most people use the SAADC
Maximum voltage range
  VDD or Reference

## Slide 53: How most people use the SAADC
DMA
  Writes results directly to memory

## Slide 54: Triggering sample collection
Can be triggered with TASK_START on demand
  Including through EVENT->TASK chaining
Includes a timer within itself to automatically trigger sampling
  Rate = 16 MHz / (2Scale) where scale is 11 bits
  Maximum rate is 7.8 kHz

## Slide 55: EasyDMA on the SAADC
There is no register to read ADC results from
Instead, you must use DMA to collect samples
At configuration time, provide:
  Pointer to RAM
    Must be RAM, not Flash
  Maximum count of 16-bit samples to be written starting at address
    Up to 32768
When complete, a register tells you the amount of samples written to RAM

## Slide 56: Event limit monitoring
Includes two comparators for each channel
  High and Low limits
Generates events whenever transitioning to above High or below Low
  Events can be ignored if unnecessary

## Slide 57: Temperature sensitivity
ADCs are often temperature sensitive
  nRF SAADC: 0.02% per degree C
Recommends recalibrating every change of 10 degrees C or more
  Automatic task for calibration
  Real concern for deployed devices
    Outdoors
    Wearable

## Slide 58: Design question
How many analog samples can the Microbit hold?

## Slide 59: Design question
How many analog samples can the Microbit hold?
  Available: 128 kB RAM, 512 kB Flash (64000 samples in RAM)
  Questions
    Are they packed or padded to 16-bit?
    How much memory are you using for other things?
    Are you moving them into Flash periodically? (or external storage)

## Slide 60: Outline
Comparators (and nRF implementations)
General ADC Design
nRF ADC Implementation