## Slide 1: Lecture 18 Wrapup
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
This is the last lecture!! 😭
  No class on Monday
Friday: Quiz 4
Next week: Project Demos
  See signup and details on Campuswire

## Slide 3: Today’s Goals
Discuss remaining parts of the Microbit and nRF52833
  Realize that we’ve covered almost everything on the system!!
Explore sensing systems research

## Slide 4: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 5: Microbit
Used almost all of this!
Remaining:
  Batteries
  Wireless
  KL27Z I2C
  Touch sensitive pads

## Slide 6: Internal Microbit connections

## Slide 7: KL27 I2C Interface
Device information
  Version of board and JTAG firmware
  Power state of board
    USB, Battery, both
    Voltage values for battery and VIN
  USB connection state
  Disable the power LED!!
Flash Storage
  128 kB of the KL27’s Flash is readable/writable over I2C

## Slide 8: Capacitive Touch Sensor
Pull-up resistors connected to metal pads
  Also connected to GPIO pin
Acts as a capacitor connected to ground

## Slide 9: Capacitive touch sensing method
Drive GPIO pin low
  Connects the pad to ground
Set GPIO pin as input and enable low-to-high interrupt
  Pad is pulled high. This takes time based on capacitance
  Use a timer to determine time until interrupt (order ~10 μs)
Repeat periodically
Sudden large increase in rise time ⇨ someone is touching!
  Finger acts as a large capacitor

## Slide 10: Capacitive touch works on any metal surface
Idea: Microbit door handle sensor
Connect a wire and a pull-up resistor to a metal door handle to sense when someone is touching it!
  Timing will be very different from capacitive pad, but should be repeatable and distinguishable from human touch

## Slide 11: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 12: nRF52833 Peripherals
Tour of the nRF52833 peripherals
With some details on the ones we haven’t talked about
  Wireless
  Crypto
  Audio

## Slide 13: nRF52833 Peripherals
Cortex-M4F processor
32-bit ARM core
Floating point
Includes Interrupt control and SysTick (an extra timer)

## Slide 14: nRF52833 Peripherals
Memory buses

## Slide 15: nRF52833 Peripherals
JTAG and Debugging
Allows code updates
Allows GDB to step through code

## Slide 16: nRF52833 Peripherals
Volatile memory
SRAM, 128 kB

## Slide 17: nRF52833 Peripherals
Nonvolatile memory
Flash, 512 kB
Non-Volatile Memory Controller

## Slide 18: nRF52833 Peripherals
Power and Clock management

## Slide 19: nRF52833 Peripherals
GPIO pins

## Slide 20: nRF52833 Peripherals
Various timers
Watchdog Timer
Real-Time Counter
Timer peripheral

## Slide 21: nRF52833 Peripherals
Programmable Peripheral Interconnect
Random Number Generator
Temperature sensor

## Slide 22: nRF52833 Peripherals
Wireless radio
  Bluetooth Low Energy
  802.15.4 (Zigbee or Thread)
Cryptography
  ECB (AES mode)
  CCM (AES mode)
  AAR (Accelerated Address Resolver)
    For BLE random addresses

## Slide 23: nRF52833 Peripherals
Wired communication protocols
USB Device
SPI
  Controller/Peripheral
TWI (I2C)
  Controller/Peripheral
UART

## Slide 24: nRF52833 Peripherals
Inter-IC Sound (I2S)
  Wired communication bus explicitly for audio data
  Unrelated to I2C
Like a synchronous UART
  Clock, data in, data out
Additional signals
  MCK – synchronization
  LRCK – left/right channel select

## Slide 25: nRF52833 Peripherals
NFC
  Near-Field Communication
Close-range wireless communication protocol
“Tap-to-pay” systems

## Slide 26: nRF52833 Peripherals
GPIOTE
  GPIO interrupts

## Slide 27: nRF52833 Peripherals
Analog inputs
Comparator
Low-Power Comparator
Successive Approximation Analog-to-Digital Converter

## Slide 28: nRF52833 Peripherals
Quadrature Decoder peripheral
Detects rotation speeds and direction
  Usually for motors

## Slide 29: Quadrature Encoding

## Slide 30: nRF52833 Peripherals
Pulse Width Modulation
Pulse Density Modulation
  Similar idea to PWM
  Input-only peripheral
  Targets microphones

## Slide 31: nRF52833 is complete
That’s just about everything!
First 550 out of 600 pages of nRF52833 datasheet
  Remaining 50 are hardware details
    Pinout for different packages
    Recommended circuit layout
    Soldering details

## Slide 32: This knowledge is transferrable!
Example: SAM4L datasheet
  Atmel Cortex M4F
  Various peripherals
    USART, SPI, TWI, I2S, DAC, ADC, Timer, …

## Slide 33: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 34: Conferences for sensing systems research
SenSys
  Conference on Embedded Networked Sensor Systems
IPSN
  Conference on Information Processing in Sensor Networks
MobiCom
  Conference on Mobile Computing and Networking
UbiComp
  Conference on Pervasive and Ubiquitous Computing
Various other systems or HCI venues
  Occasionally Electrical or Civil Engineering venues too

## Slide 35: Sensing systems research
Combination of engineering and exploration
Generally divides into two different focuses
  Often projects will mix some of each domain
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 36: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 37: Permamote (Jackson, Adkins, Dutta)
Goal: create a 10-year wireless sensor
Solutions
  Modern sensors and microcontroller
  Energy harvesting combined with rechargeable battery
  Non-rechargeable battery as backup power
https://lab11.eecs.berkeley.edu/content/pubs/jackson19capacity.pdf

## Slide 38: Bfree (Kortbeek, Bakar, Cruz, Yildririm, Pawelczak, Hester)
Goal: hobbyist intermittent systems
Solutions
  Automatic checkpointing in python runtime
  Hardware module for easy prototyping
  User studies to demonstrate improvements
https://dl.acm.org/doi/abs/10.1145/3432191

## Slide 39: Tock (Levy, Campbell, Ghena, Giffin, Pannuto, Dutta, Levis)
Goal: safe and reliable embedded OS
  Demonstrate this is possible on small embedded platforms
Solutions
  Dedicated OS kernel with separate applications
  Protect applications with hardware features
    Memory Protection Unit
  Protect kernel with language features
    Rust programming language
https://lab11.eecs.berkeley.edu/content/pubs/levy17multiprogramming.pdf

## Slide 40: Tock software organization
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
System Calls
6LoWPAN
SI7021
SD Card
Console
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf
Syscall Interface

## Slide 41: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 42: Opo (Huang, Kuo, Pannuto, Dutta)
Goal: sense distance of human interactions
  Real-time, high accuracy, deployable
Solutions
  Ultrasonic allows for low-power detection of nearby devices
  Also provides directionality
  Measure difference in arrival time of RF and Ultrasonic to determine distance
https://lab11.eecs.berkeley.edu/content/pubs/huang14opo.pdf

## Slide 43: Powerwatch (Klugman, Adkins, et al.)
Goal: measure electric grid reliability in developing regions
“Access alone is insufficient. Reliability matters too.”
Solutions:
  Wall-powered sensor with battery-backup to detect outages and report over cellular
  Infrastructure to collect measurements and cross-correlate
  Create a team to manage the deployment
https://lab11.eecs.berkeley.edu/content/pubs/klugman19scale.pdf

## Slide 44: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Sensing Systems Research

## Slide 45
Bonus: Signpost
  (Adkins, Ghena, Jackson, Pannuto, Rohrer, Campbell, Dutta)
https://lab11.eecs.berkeley.edu/content/pubs/adkins18signpost.pdf

## Slide 46: What things might we want to sense at the scale of a city?

## Slide 47: Air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2018.
[1]
[1]
[2]
[2]

## Slide 48: Audio detection, classification, and localization
[1] Girod et al. The Design and Implementation of a Self-Calibrating Distributed Acoustic Sensing Platform. 2006. [2] Lédeczi et al. Multiple Simultaneous Acoustic Source Localization in Urban Terrain. 2005. [3] Sounds of New York City. 2016.
[1]
[1]
[2]
[3]

## Slide 49: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 51
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 52
Air Quality Monitoring
Urban Noise Classification
Traffic Queue Sensing
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Sounds of New Your City. 2016. [3] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[2]
[3]
Lots of interesting applications and interested parties. But let’s look at the process of actually creating and deploying an application.

## Slide 53: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 54: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 55: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 56: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Sustainable Power
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 57: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Sustainable Power
Weatherproof Casing
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 58: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1]
Sustainable Power
Weatherproof Casing
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 59: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1] Sounds of New York City. 2016
[1]
Sustainable Power
Weatherproof Casing
[1]

## Slide 60: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Storage
Storage Driver
Deploy
[1] Purple Air. 2018
[1]
Sustainable Power
Weatherproof Casing
[1]
Networking Driver

## Slide 61: Signpost Enables City-Scale Sensing
Sensing Hypothesis/Hardware
Deploy
[1] Purple Air. 2018.
[1]
[1]
Integrate with Signpost
Joshua Adkins, Branden Ghena, Neal Jackson, Pat Pannuto, Samuel Rohrer, Bradford Campbell, and Prabal Dutta ”The Signpost Platform for City-Scale Sensing." IPSN’18

## Slide 62
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 63: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1] Purple Air. 2018
[1]
Sustainable Power
Weatherproof Casing
[1]

## Slide 64
Deployment | Services Needed |  |  |  |  |  | 
 | Power | Networking | Processing | Storage | Time | Synch | Location
Caraoke [3] |  |  |  |  |  |  | 
Bouillet et al. [4] |  |  |  |  |  |  | 
Aircloud [5] |  |  |  |  |  |  | 
Girod et al. [6] |  |  |  |  |  |  | 
Ledeczi et al. [7] |  |  |  |  |  |  | 
SenseFlow [8] |  |  |  |  |  |  | 
Argos [9] |  |  |  |  |  |  | 
SONYC [1] |  |  |  |  |  |  | 
Kyun Queue [10] |  |  |  |  |  |  | 
Micronet [11] |  |  |  |  |  |  | 
Higher power/linux class processing
Can be provided with a GPS

## Slide 65: Software abstraction through a single interface
Sensing Hypothesis/Hardware
Networking
Storage
Sustainable Power
Sensor
Platform
GPS
High Performance Processing
Platform Interface
Platform Controller
- Ubiquitous
- Easy to adapt/implement
- Physically pluggable

## Slide 66: Abstracting away functionality
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Sustainable Power
Weatherproof Casing
Sensor
Platform

## Slide 67: A hardware abstraction is not sufficient
Sensing Hypothesis/Hardware
Networking
Storage
Sustainable Power
Sensor
Platform
GPS
High Performance Processing

## Slide 68: A hardware abstraction is not sufficient
Sensing Hypothesis/Hardware
Networking
Storage
Sustainable Power
Sensor
Platform
GPS
High Performance Processing
Networking Interface
Storage Interface
Processing Interface
GPS Interface
Multiple Interfaces = Multiple Drivers

## Slide 69: Software abstraction through a single interface
Sensing Hypothesis/Hardware
Networking
Storage
Sustainable Power
Sensor
Platform
GPS
High Performance Processing
Platform Interface
Platform Controller

## Slide 70
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 71: Some applications require granularity
Data can change greatly in low distances
Outlier
Notes: If we want to

## Slide 72: Deployment overhead drives cost
Expensive to work with the city
Time consuming
Not conducive to experimentation!
Do not rely on wired infrastructure
No wired power
  Solar provides more power density than batteries
No wired networking
Should not modify existing infrastructure

## Slide 73: Multi-tenancy is beneficial to testbeds
One deployment can enable many stakeholders simultaneously
Need to ensure that they do not conflict

## Slide 74
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 75: The Signpost Platform

## Slide 76: Core modules provide shared resources
GPS
Processing
Storage
Making the platform modular supports upgradeability
Networking
BLE
LoRa
3G
Control Module
Radio Module

## Slide 77: Measurement and isolation support multi-tenancy
Power Metering
Isolation
& Monitoring

## Slide 78: Standard interface for accessing shared resources
Any software framework can be used for modules

## Slide 79: Array of Things is one platform approach
Include sensors as platform resources
Applications are software that act on sensor data
High-power hardware and expensive to deploy

## Slide 80: Signpost explores the other end of the spectrum
What can we do with less?
Low-power, low-capability, extremely deployable
Limited provided resources, but lots of extensibility
Focus on modularity
Too difficult to start from scratch for every upgrade/change
  Components are more expensive
  Deployments is more difficult
The platform should be viewed as shared infrastructure!
  Amortize cost with multiple sensors and applications

## Slide 81
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 82: How much power does a Signpost harvest?
Higher daily variations than directional variations
Notes: Bigger text ,fix font
Write takeaways on the slide

## Slide 83: How much power can each module draw?
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 84: How much power can each module draw?
Seattle 95th Percentile = 3 mW
San Diego 95th Percentile = 162 mW
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 85: How much power can each module draw?
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 86: Resources are charged to modules which use them
Notes: Fix font

## Slide 87: Applications running on Signpost
Environmental monitoring (posting to Weather Underground)
Vehicle counting (and bell tower)
TV whitespace sensing
Notes: Fix font, callout on diurnal power patter/concert