## Slide 1: Lecture 13 Introduction to LPWANs
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021

## Slide 2: Today’s Goals
Introduction to the Wide-area communication space
Apply knowledge from the course to understand LPWAN design
Overview of unlicensed-band LPWANs
  LoRaWAN

## Slide 3: Resources
Sigfox
  Sigfox Technical Overview
  IETF Descriptions
    https://www.ietf.org/proceedings/97/slides/slides-97-lpwan-25-sigfox-system-description-00.pdf
    https://tools.ietf.org/html/draft-zuniga-lpwan-sigfox-system-description-04
LoRaWAN
  LoRaWAN Specification version 1.1
  LoRaWAN Regional Parameters version 1.0.2

## Slide 4: Outline
Wide-Area Network Background
Design an LPWAN
Unlicensed LPWANs
  LoRaWAN

## Slide 5: Wide area networks
Communication at the region/city scale rather than the building/residence scale
  Throughout cities
  Agricultural deployments
  Industrial facilities
City-scale sensing is one very popular domain
  What might we want to sense throughout a city?

## Slide 6: Air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2018.
[1]
[1]
[2]
[2]

## Slide 7: Audio detection, classification, and localization
[1] Girod et al. The Design and Implementation of a Self-Calibrating Distributed Acoustic Sensing Platform. 2006. [2] Lédeczi et al. Multiple Simultaneous Acoustic Source Localization in Urban Terrain. 2005. [3] Sounds of New York City. 2016.
[1]
[1]
[2]
[3]

## Slide 8: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 10: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 11: How do we collect data from a sensor?
Manually collect measurements
  Too much work
Connect it to WiFi (or Ethernet)
  Too many separate networks
Pay for cellular access
  Too expensive for many devices

## Slide 12: How do we collect data from MANY sensors?
Manually collect measurements
  Too much work
Connect it to WiFi (or Ethernet)
  Too many separate networks
Pay for cellular access
  Too expensive for many devices

## Slide 13: We need another network option
Requirements:
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small

## Slide 14: Long-range, low-data needs haven’t historically been met
Data
Throughput
Range
WiFi

## Slide 15: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range

## Slide 16: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 17: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
2G
3G
4G
BLE
Zigbee
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 18: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 19: Outline
Wide-Area Network Background
Design an LPWAN
Unlicensed LPWANs
  LoRaWAN

## Slide 20: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?

## Slide 21: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?
  Modulation
  Tx Power
  Carrier Frequency Band
  Data Throughput
  Channel Bandwidth

## Slide 22: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?
  Modulation
    Unclear. Can’t be too crazy for cheap devices.
  Tx Power
    High (much higher than 0 dBm)
  Carrier Frequency Band
    Low (something lower than 2.4 GHz, 915 MHz or lower?)
  Data Throughput
    Low (much lower than 1 Mbps)
  Channel Bandwidth
    Unclear. Likely smaller for lower frequency carrier.

## Slide 23: Design a low-power wide-area network
Any particular MAC choices for lower power?

## Slide 24: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Diversity of devices in network
    High power gateway, low power devices in star topology
  Devices should be off whenever possible
    Listen-after send for downlink
  Remove requirements for synchronization
    No TDMA access control if it can be avoided
    Aloha, CSMA

## Slide 25: Long-range CSMA is problematic
Long-range makes everything more challenging
  Kilometers of range mean kilometers between devices
Detection of channel use is less reliable
  Active research in clear channel assessment for LPWANs
Hidden terminal problem has a wider range
  Might make RTS/CTS more important
Result: CSMA doesn’t dominate LPWANs like it does WLANs

## Slide 26: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 27: Outline
Wide-Area Network Background
Design an LPWAN
Unlicensed LPWANs
  LoRaWAN

## Slide 28: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Low rate (1-20 kbps) and long range (~5 km)
  Shorter range than Sigfox but much higher bit rate
Most popular LPWAN protocol
  Target of academic research
  Industry involvement in hardware and deployments

## Slide 29: LoRa PHY uses a different modulation
Chirp Spread Spectrum (CSS)
  Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 30: Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel

## Slide 31: CSS has a Spreading Factor which determines bit rate
Spreading Factor is essentially the rate-of-change of frequency
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision

## Slide 32: LoRaWAN channels
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not well used in practice)
Eight, 500 kHz downlink channels

## Slide 33: LoRaWAN gateways
No synchronization with end devices
Instead listen to entire bandwidth simultaneously
  Only 12 MHz total
  Recognize preambles and allocate a hardware to decode packet
    Normal gateways: 8 decoders
    Good gateways: 64 decoders

## Slide 34: LoRaWAN data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate options depend on channel in use
  Unbalanced uplink and downlink
64-channel uplink
  1-5 kbps data rate
Allowable rates based on dwell time restriction (400 ms)

## Slide 35: LoRaWAN link budget
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is about a kilometer in urban environments

## Slide 36: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: listen-after-send (class A device)
  Two windows for RX on different channels

## Slide 37: Optional downlink mechanisms
Periodic listening (class B device)
  Synchronized with periodic beacons
    TX still unsynchronized Aloha
  Mostly unused
Continuous listening (class C device)
  Always-on receivers

## Slide 38: LoRaWAN packet format
Frame header includes device address
MAC Payload maximum size depends on data rate
  Again based on dwell time in the US
Data Rate Index | MAC Payload Size
0 | 19 bytes
1 | 61 bytes
2 | 133 bytes
3 | 250 bytes
4 | 250 bytes

## Slide 39: LoRaWAN network details

## Slide 40: LoRaWAN hardware
Numerous hardware modules and development kits
  Almost all use Semtech radio chips (Semtech owns LoRa PHY)
Recent addition: STM32WLE5 LoRa SoC
  Cortex-M4 + LoRa radio (analogous to nRF52840)

## Slide 41: LoRaWAN network providers
Somewhat-managed network providers
  The Things Network (predominantly in Europe)
  Helium
    Any can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 42: LoRaWAN interested parties
MachineQ is a subsidiary of Comcast providing LoRaWAN networks
Long-term goal
  Indoor-to-outdoor LoRaWAN gateways combined with WiFi
  Tune down power for 100-200 meter range

## Slide 43: Outline
Wide-Area Network Background
Design an LPWAN
Unlicensed LPWANs
  LoRaWAN