## Slide 1: Lecture 12 Cache Memories
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2025
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Deadline reminders
  Homework 3 on Thurday
  Attack Lab next week Tuesday
Next week
  Homework 4 & SETI Lab come out
  No lecture next week Thursday
    Enjoy the break

## Slide 3: Today’s Goals
Understand how locality makes a cache useful
Discuss organization of various cache designs
  Direct-mapped caches
  N-way set-associative caches
  Fully-associative caches

## Slide 4: Caching in a memory hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
Blocks cannot be stored in an arbitrary location!
They can only live at one of a fixed set of locations.
In this example: they must be in the same “column” for both levels.

## Slide 5: General caching concepts
Request
14
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
14
4*
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14

## Slide 6: General caching concepts
12
Request
12
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14
Cache miss
  b is not at level k, so the level k cache must fetch it from level k+1, e.g., block 12
  If the level-k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Here, we pick 4; same column as 12
    4 is “dirty”, need to write back to k+1
    More on this next lecture
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
12
4*
Request
12
4*
4*
12
12
“ * ” means the block is dirty (i.e., it has been modified)

## Slide 7: Outline
Locality of Reference
Cache Organization
Associativity

## Slide 8: Caching speeds up code
Cache: smaller, faster storage device that keeps copies of a subset of the data in a larger, slower device
  If the data we access is already in the cache, we win!
  Can get access time of faster memory, with overall capacity of larger
But how do we decide which data to keep in the cache?
  Can we predict which data is likely to be necessary in the future?

## Slide 9: Locality
Goal: predict which data the CPU will want to access
  So we can bring it to (and keep it in!) fast memory
  Problem: memory is huge! (billions of bytes) how do you decide which to save?
Principle of Locality
  Programs tend to access data in predictable ways
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time

## Slide 10: Types of locality practice
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time
Quiz: what kind of locality?
  Data
    Reference array elements in succession:
    Reference sum each iteration:
  Instructions
    Execute instructions in sequence:
    Cycle through loop repeatedly:
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Spatial locality
Temporal locality
Temporal locality

## Slide 11: Locality example
Can get a sense for whether a function has good locality just by looking at its memory access patterns
Does this function have good locality?
Yes!
  Array is accessed in same row-major order in which it is stored in memory
  a through a+3 , a+4 through a+7, a+8 through a+11, etc.
int sumarrayrows(int a[M][N]){
int sum = 0;
for (int i = 0; i < M; i++) {
for (int j = 0; j < N; j++) {
sum += a[i][j];
}
}
return sum;
}
Temporal or spatial locality?
Spatial: accesses to array
Temporal: accesses to sum
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
Notes: sum: both
a: mostly spatial
loop body instructions: both

## Slide 12: Locality example
Does this function have good locality?
No!
  Scans array column-wise instead of row-wise
  a through a+3, then a+4*N through a+4*N+3, etc.
  Holy jumping around memory Batman!
More on that in a later lectures
int sumarraycols(int a[M][N]){
int sum = 0;
for (int j = 0; j < N; j++) {
for (int i = 0; i < M; i++) {
sum += a[i][j];
}
}
return sum;
}
1
5
2
0
6
1
5
2
1
3
1
5
2
1
7
1
5
2
2
1
Notes: sum: both
instructions: both
a: nope!

## Slide 13: Locality to the Rescue!
How can we exploit locality to bridge the CPU-memory gap?
  Use it to determine which data to put in a cache!
Spatial locality
  When level k needs a byte from level k+1, don’t just bring one byte
  Bring neighboring bytes as well!
  Good chances we’ll need them too in the near future
Temporal locality
  Anything accessed goes in the cache, and we’ll try to keep it there for a while
  Good chances we’ll need it again in the near future
Result: most accesses should be cache hits!
  Memory system: size of largest memory, with speed close to that of fastest memory

## Slide 14: Cache misses will still happen
Only 1%-0.1% of memory is in the cache
  So we’ll sometimes need to access the other 99%
When evaluating system performance, the most important part is understanding why a cache miss occurred

## Slide 15: What causes a cache miss?
Cold (compulsory) miss
  Cold misses occur when a block is accessed for the first time
  No one ever accessed it, so there wasn’t any reason to bring it into cache
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
  There’s no way the working set can all fit in the cache, so there will be misses
Conflict miss
  In most caches, blocks cannot be stored in any available slot
  If two blocks need to go in the same slot, need to evict the old one to store the new!
  If after that, we need to access the old block, conflict miss!
    We had a conflict, evicted a block, and now we miss trying to access that block
  Note: can happen even when there is “room” elsewhere in the cache!
  We’ll show examples of this next lecture

## Slide 16: Break + Question
When you first start up a program, it runs really slowly for a few seconds. What kind of cache misses are occurring?
When you have too many browser tabs open and active, all of the tabs run more slowly. What kind of cache misses are occurring?
Miss types: Cold, Capacity, Conflict

## Slide 17: Break + Question
When you first start up a program, it runs really slowly for a few seconds. What kind of cache misses are occurring?
  Cold (aka Compulsory) misses. The data has never been loaded before!
When you have too many browser tabs open and active, all of the tabs run more slowly. What kind of cache misses are occurring?
  Capacity misses. You have too much data to fit it all in the cache
    Could be Conflict misses as well, but probably not
Miss types: Cold, Capacity, Conflict

## Slide 18: Outline
Locality of Reference
Cache Organization
Associativity

## Slide 19: Cache memories
A specific instance of the general principle of caching
  Small, fast SRAM-based memories between CPU and main memory
  Can include multiple levels
    L1 = small, but really fast, L2 = larger, slower, L3, etc.
CPU looks for data in caches first
  e.g., L1, then L2, then L3, then finally in main memory as a last resort
Mechanisms we’ll see today are implemented in hardware

## Slide 20: How You Probably Thought a Memory Access Worked
Some memory address
Address of word:
Memory:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 21: How a Memory Access Actually Works
Some memory address
Address of word:
Memory:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
L1 Cache:
L2 Cache:
...
...
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 22: General Cache Organization (S, A, B)
A blocks per set (associativity)
K = 2s sets
cache set
B-1
2
1
0
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = K x A x B data bytes
valid bit
cache block
(aka cache line)
Set ≈ column from last lecture.
Specific data can go in only one set!
tag identifies which data is in this cache block
Notes: Typical B: 32, 64, sometimes up to 256

## Slide 23: Cache Access
Some memory address
Address of word:
Cache:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
t bits
s bits
b bits
...
return var;
...
...
movq -12(%rsp),%rax
...

## Slide 24: Cache Read (1): Locate Set
A blocks per set
K = 2s sets
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
Locate set
0xFF
0xFF
Each address maps to a particular set!
Data has to be stored at that particular set!
Even if that set is full and there would be space elsewhere!
(That’s where conflict misses come from.)

## Slide 25: Cache Read (2): Tag Match + Valid
A blocks per set
K = 2s sets
tag
v
valid bit
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
Locate set
Locate block in set
Tag matches + valid bit set  Cache Hit!
0xFF
0xFF
0x1E45
0x1E45
1
Within a set, could be anywhere! So, need to check all blocks!
But if it’s not in that set, it’s not in the cache at all! (It’s the only place it could be.)

## Slide 26: Cache Read (3): Block Offset
A blocks per set
K = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
data begins at this offset
Locate set
Locate block in set
Tag matches + V bit set  Cache Hit!
Locate data starting at offset
block
offset
0xFF
0xFF
0x1E45
0x1E45
1
0x2
2

## Slide 27: Example: 128 sets, 64 bytes per block
00…0
1
63
2
1
0
127
66
65
64
191
130
129
128
Memory:
t bits
s bits
b bits
6510 = 100 00012
00...0
0000001
000001
64 bytes per block  b = 6 bits
128 sets  s = 7 bits
remaining address bits  t bits
address of a byte in memory
A blocks per set
set 0:
set 1:
set 2:
set 127:
Goal: Get byte M[65] from cache
QUIZ #1: which set
should we look in?
QUIZ #2: which tag
are we looking for?
QUIZ #3: which byte
within the block is the
one that we want?

## Slide 28: Cache access overview
A blocks per set
2s sets
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
data begins at this offset
block
offset
Address of word:
%rax
%rdx
%rcx
%rbx
%rsi
%rdi
%rsp
0x104
...
return var;
...
...
movq -12(%rsp),%rax
...
valid bit
tag identifies which data is in this cache block

## Slide 29: Break + Question
64-bit, byte-addressed system
32 kB cache
  512 sets and 64-byte blocks
How many bits for Tag?
  A: 6 bits
  B: 9 bits
  C: 17 bits
  D: 49 bits
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
s bits

## Slide 30: Break + Question
64-bit, byte-addressed system
32 kB cache
  512 sets and 64-byte blocks
How many bits for Tag? (6 bits for block, 9 bits for set)
  A: 6 bits
  B: 9 bits
  C: 17 bits
  D: 49 bits (Tag is remaining bits. 64 - 6 - 9 = 49)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
s bits

## Slide 31: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
  Don’t want them to get (or at least not to stay) out of sync!
    Otherwise, who do you believe?
Multiple configuration options that a cache could have

## Slide 32: Write configurations
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (delay write until we evict this cache block)
    Need a dirty bit (indicate if block differs from memory)
    We had an example of that last lecture
What to do on a write-miss?
  Write-allocate (load into cache, update block in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory, doesn’t bring into cache)
Typical combinations
  Write-back + Write-allocate ← by far the most common
  Write-through + No-write-allocate

## Slide 33: Outline
Locality of Reference
Cache Organization
Associativity

## Slide 34: Cache memory associativity
When designing a cache, a number of parameters to choose
  Total size (C), cache block size (B), number of sets (K), …
The most interesting one: associativity (A)
  i.e., how many cache blocks per set
  Has a significant impact on effectiveness (and complexity!)

## Slide 35: Associativity choices
Associativity 1 → direct-mapped caches
  One cache block per set, data blocks can only go in that one cache block
  Whenever we place data in a set, must evict whatever is there
Associativity >1 → set-associative caches
  Can keep multiple blocks that would map to the same set
Single set → fully-associative caches
  Any block can go anywhere, 1 big set, tag is all that matters
  Very rare for cache memories due to expensive hardware

## Slide 36: Direct-mapped cache (associativity = 1)
K = 2s sets
Direct mapped: One block per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set

## Slide 37: Direct-mapped cache (associativity = 1)
Direct mapped: One block per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
tag match? if yes  hit
valid? +
block offset
tag
Address of int:

## Slide 38: Direct-mapped cache (associativity = 1)
Direct mapped: One block per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
tag match? if yes  hit
valid? +
int is here (4 bytes)
block offset
Address of int:

## Slide 39: Direct-mapped cache (associativity = 1)
K = 2s sets
Direct mapped: One block per set
Assume: cache block size 8 bytes
t bits
0…01
100
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set
If tag doesn’t match or valid bit is not set: cache miss!
 old block is evicted and replaced with currently requested one
X
X
tag
1
7
6
5
0
4
1
2
3
Address of int:

## Slide 40: Direct-mapped cache simulation
x
t=1
s=2
b=1
xx
x
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
m[0] is the value of memory at address 0
The actual values are irrelevant for this problem

## Slide 41: Direct-mapped cache simulation
x
t=1
s=2
b=1
xx
x
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
m[0] is the value of memory at address 0
The actual values are irrelevant for this problem
Every Block in the cache holds two bytes, so we can split memory into blocks
Every two bytes is a block. And blocks are aligned (so bytes 1 and 2 are separate blocks)
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory

## Slide 42: Direct-mapped cache simulation
block
v
tag
x
t=1
s=2
b=1
xx
x
0 [0 00 02]
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
0
1 0 m[1] m[0]

## Slide 43: Direct-mapped cache simulation
block
v
tag
x
t=1
s=2
b=1
xx
x
0 [0 00 02]
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
1 0 m[1] m[0]
1 [0 00 12]
???

## Slide 44: Direct-mapped cache simulation
block
v
tag
x
t=1
s=2
b=1
xx
x
0 [0 00 02]
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
1 0 m[1] m[0]
1 [0 00 12]
hit

## Slide 45: Direct-mapped cache simulation
block
v
tag
x
t=1
s=2
b=1
xx
x
0 [0 00 02]
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
1 0 m[1] m[0]
1 [0 00 12]
hit
7 [0 11 12]
miss
1 0 m[7] m[6]
0

## Slide 46: Direct-mapped cache simulation
block
v
tag
x
t=1
s=2
b=1
xx
x
0 [0 00 02]
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory
1 0 m[1] m[0]
1 [0 00 12]
hit
7 [0 11 12]
miss
1 0 m[7] m[6]

## Slide 47: Direct-mapped cache simulation
7 [0 11 12]
8 [1 00 02]
1 [0 00 12]
1 [0 00 12]
x
t=1
s=2
b=1
xx
x
block
v
tag
0 [0 00 02]
1 0 m[1] m[0]
1 0 m[1] m[0]
1 0 m[7] m[6]
1 1 m[9] m[8]
1 0 m[1] m[0]
1 0 m[7] m[6]
miss
hit
miss
miss
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
1 1 m[9] m[8]
0
0
0
0
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory

## Slide 48: What are the types of each miss here?
7 [0 11 12]
8 [1 00 02]
1 [0 00 12]
1 [0 00 12]
x
t=1
s=2
b=1
xx
x
Conflict misses: There is “room” in the cache, but two blocks map to the same set; one evicts the other!
block
v
tag
0 [0 00 02]
miss
hit
miss
miss
miss
M=16 addresses,
byte-addressable B=2 bytes/block
K=4 sets A=1 blocks/set
Address trace (reads, one byte per read):
set 002
set 012
set 102
set 112
0
0
Compulsory Miss
Compulsory Miss
Compulsory Miss
Conflict Miss
1 0 m[7] m[6]
Options:
Compulsory
Capacity
Conflict
1 0 m[1] m[0]
offset | 0 | 1 | 2 | 3
0x0 | m[0] | m[1] | m[2] | m[3]
0x4 | m[4] | m[4] | m[6] | m[7]
0x8 | m[8] | m[9] | m[10] | m[11]
0xC | m[12] | m[13] | m[14] | m[16]
Memory

## Slide 49: Pause for questions on direct-mapped caches

## Slide 50: Associativity choices
Associativity 1 → direct-mapped caches
  One cache block per set, blocks can only go in that one block
  Whenever we place data in a set, must evict whatever is there
Associativity >1 → set-associative caches
  Can keep multiple cache blocks that would map to the same set
Single set → fully-associative caches
  Any cache block can go anywhere, 1 big set, tag is all that matters
  Very rare for cache memories due to expensive hardware

## Slide 51: 2-way set-associative cache (associativity = 2)
A = 2: Two blocks per set
Assume: block size 8 bytes
t bits
0…01
100
Address of short:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
find set

## Slide 52: 2-way set-associative cache (associativity = 2)
A = 2: Two blocks per set
Assume: block size 8 bytes
t bits
0…01
100
Address of short:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
compare both
valid? +
tag match? if yes  hit
block offset
tag
The data we want is either on the left, or on the right, or not in the cache at all.
It can’t be anywhere else! Addresses map to a single set!

## Slide 53: 2-way set-associative cache (associativity = 2)
A = 2: Two blocks per set
Assume: block size 8 bytes
t bits
0…01
100
Address of short:
7
6
5
0
tag
v
4
1
2
3
7
6
5
0
tag
v
4
1
2
3
compare both
valid? +
tag match? if yes = hit
block offset
short is here (2 bytes)
If no match:
One block in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …
  More clever → lower miss rate, but harder to implement in hardware

## Slide 54: 2-way set-associative cache simulation
Address trace (reads, one byte per read):
0 [00 0 02]
1 [00 0 12]
7 [01 1 12]
8 [10 0 02]
0 [00 0 02]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1
The same address sequence in the direct mapped cache resulted in:
miss
hit
miss
miss
miss
M=16 addresses, byte-addressable,
B=2 bytes/block, K=2 sets, A=2 blocks/set
Higher associativity =
Less likely to have to evict!
Temporal locality: want data in cache to stay in cache!
v
Tag
Block
Same total size and block size as before.
Associativity (and thus # of sets) changed.

## Slide 55: Pause for questions on set-associative caches

## Slide 56: Fully-associative caches
What changes with fully-associative caches?
  Anything can go anywhere
  Only one set (s = 0 bits)
Otherwise, same steps as for a set-associative cache
  Compare tag against all blocks in the set

## Slide 57: Fully-Associative Cache Practice
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
??
t=??
s=0
b=??
??

## Slide 58: Fully-Associative Cache Practice
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 59: Fully-Associative Cache Practice
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400
  0x0410
  0xC002
  0xC048
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 60: Fully-Associative Cache Practice
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000
  0x0410⇨0b0000 0100 0001 0000
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 61: Fully-Associative Cache Practice
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000
  0x0410⇨0b0000 0100 0001 0000
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 62: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000
  0x0410⇨0b0000 0100 0001 0000
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx
You figure out the rest!

## Slide 63: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000 → Tag 0x010 HIT
  0x0410⇨0b0000 0100 0001 0000 → Tag 0x010 (same block!) HIT
  0xC002⇨0b1100 0000 0000 0010
  0xC048⇨0b1100 0000 0100 1000
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 64: Break + Question
Fully-associative cache on a 16-bit system
  One set (fully associative!)
  Eight, 64-byte blocks
Are the following addresses in the cache?
  0x0400⇨0b0000 0100 0000 0000 → Tag 0x010 HIT
  0x0410⇨0b0000 0100 0001 0000 → Tag 0x010 (same block!) HIT
  0xC002⇨0b1100 0000 0000 0010 → Tag 0x300 HIT
  0xC048⇨0b1100 0000 0100 1000 → Tag 0x301 (different block!) MISS
Tag: 0x010
Tag: 0x011
Tag: 0x000
Tag: 0x1FF
Tag: 0x052
Tag: 0x300
Tag: 0x050
Tag: 0x051
xxxxxxxxxx
t=10
s=0
b=6
xxxxxx

## Slide 65: Associativity Pros and Cons
Direct-mapped
  Simplest to implement: look-up compares tag with 1 cache block → requires fewer transistors, which can be used elsewhere on the chip
  Conflicts can easily lead to thrashing
    Two cache blocks map to the same set, program needs both, and they keep kicking each other out of the cache. Lots of misses. Bad times.
Set-associative
  More complex implementation: requires more (HW) tag comparators
  Lower miss rate than direct-mapped caches (fewer conflict misses)
    2-way is a significant improvement over direct-mapped
    4-way is a more modest improvement over 2-way, and so on
Fully-associative
  One comparator per cache block in the cache means a LOT of hardware. Ouch.
    Often a deal-breaker for hardware
  Very low miss rate!

## Slide 66: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way,
  Access: 4 cycles
Keep separate caches for instructions and data. Don’t want them to step on each other’s toes!
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Last resort before going to main memory (slow!) So want this large and highly-associative, to have very few misses.
Block size: 64 bytes for all caches.

## Slide 67: Outline
Locality of Reference
Cache Organization
Associativity