## Slide 1: Lecture 03 BLE Introduction
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2022
Materials in collaboration with Pat Pannuto (UCSD)

## Slide 2: Administrivia
Think about project ideas
  Make posts on campuswire with ideas to iterate on
    Also good for recruiting partners
  I’m happy to schedule office hours to discuss!
First lab is available
  Goal: familiarize yourself with Wireshark
    Install it, do some basic scanning, explore a little
  Writeup: “prove to me that you did this lab”
    Due next week Thursday by end-of-day
    Submit on Gradescope
  Next week: Wireshark + BLE

## Slide 3: Today’s Goals
Introduction to Bluetooth Low Energy
  What are the goals of the protocol?
  What do the lower layers look like?
  What roles do devices take?

## Slide 4: Bluetooth Low Energy Resources
Good walkthrough of BLE:
  https://www.silabs.com/documents/public/user-guides/ug103-14-fundamentals-ble.pdf
[5.2 specification] [4.2 specification] (link to PDF download)
  Also: [Supplement v9]
I used a mix of 5.2 and 4.2 for this
  Will talk about BLE 5 differences as part of next lecture

## Slide 5: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning

## Slide 6: Basics of Bluetooth Low Energy (BLE)
Direct device-to-device communication
  Usually: Computer to Thing
  Smartphone to device, Laptop to device, etc.
Focus on making the “Thing” really low energy
  Push energy-intensive requirements onto “Computer”
Devices (Computer or Thing) are servers with accessible fields
  Not the traditional send-explicit-packets interface you might be expecting
  Lower layers are still exchanging packets to make it work

## Slide 7: A note on outdated notation
Master/Slave paradigm
  Master is the “Computer” and is in charge of interaction
  Slave is the “Device” and has little control over interaction parameters
  Really common notation in EE side of the world.
    Not intended to be harmful, but also literally inconsiderate.
Field is changing for the better. It’s going to take some time.
  Central/Peripheral
  Device/Peripheral
  Controller/Peripheral
  Master/Minion
  Primary/Secondary

## Slide 8: BLE development
Protocol development
  Research product
  Specification
  Hardware support
  Usefulness and iteration
Bluetooth Low Energy
  Research in early 2000s: Bluetooth Low End Extension and Wibree
  Specification in 2009: Bluetooth version 4.0
  Hardware support in 2011/12: iPhone 4s, nRF51 series
  4.1 and 4.2 (2014), 5.0 (2016, first in phones 2017, really 2019 though)

## Slide 9: Bluetooth has a long history — the IoT is near-exclusively BLE (Bluetooth 4.0+) as opposed to Bluetooth Classic (<4.0)

## Slide 10: Bluetooth Specification
Problem: a bit overwhelming…
  5.2 spec: 3256 pages
  We only care about Vol 6: Low Energy Controller
    Part A: Physical Layer Specification
    Part B: Link Layer Specification
    CSS: Part A: Data Types Specification
    So ~250 pages
Tip: be willing to just ignore things when skimming specs
  5.2 spec covers BLE and Bluetooth Classic and a bunch of upper layer stuff that we never have to care about

## Slide 11: BLE Layers
Host – Configuration and Server
  GAP – Generic Access Profile
    Configure advertising
  GATT – Generic ATTribute profile
    Configure connections
HCI - Host Controller Interface (sigh)
Controller - Communication
  Link Layer – send packets
  RF and PHY – send bits
GAP
Host
Controller

## Slide 12: BLE mechanisms
Advertising
  Discovery
  Advertisements – broadcast messages indicating device details
  Ephemeral, uni-directional communication from Advertiser to Scanner(s)
  ALOHA access control
Connections
  Interaction
  Bi-directional communication between Peripheral and Central
  Maintained for some duration
  TDMA access control

## Slide 13: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 14: Multiple roles at the same time
Topology picture is a simplification of roles
A single device can have multiple roles simultaneously
  Scanning and Advertising simultaneously
  Peripheral and Scanner and Advertiser simultaneously
  Peripheral and Scanner and Central and Advertiser simultaneously
    Getting a bit out of hand though
Also possible:
  One Peripheral can be connected to multiple Centrals
    This is relatively new in BLE still, you’ll find old docs saying you can’t

## Slide 15: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
  Laptop
  Smartphone

## Slide 16: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
    Advertiser and Peripheral
  Laptop
    Scanner and Central
  Smartphone
    Advertiser, Peripheral, Scanner, and Central

## Slide 17: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning

## Slide 18: BLE frequency
2.4 GHz carrier, Forty 2-MHz channels, 1 Mbps data rate
  37, 38, 39 for advertising
  0-36 for connection (FHSS)
Why doesn’t BLE avoid WiFi altogether?

## Slide 19: BLE frequency
2.4 GHz carrier, Forty 2-MHz channels, 1 Mbps data rate
  37, 38, 39 for advertising
  0-36 for connection (FHSS)
Why doesn’t BLE avoid WiFi altogether?
Can’t on 2.4 GHz
Wants 2.4 GHz for technology improvements

## Slide 20: BLE modulation
Gaussian Frequency-Shift Keying (GFSK)
  Improvement on base Frequency-shift Keying
  Smoother transitions between bits -> reduces nearby interference

## Slide 21: Gaussian FSK lessens spectral leakage at the expense of some loss in intersymbol discriminability
Notes: Images from http://j3.rf-explorer.com/40-rfe/article/53-tutorial-how-to-use-rf-explorer-to-monitor-a-rfbee?start=4

## Slide 22: An example from `good case` BLE hardware
Notes: Fig 8 in https://download.ni.com/evaluation/rf/intro_to_bluetooth_test.pdf

## Slide 23: BLE signal strength
Remember nRF52840 capabilities
  Transmit: up to 8 dBm
  Receive sensitivity: -95 dBm

## Slide 24: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning

## Slide 25: Packet structure
Same packet structure for both advertisements and connections
  Fields are filled in little endian (the opposite of network byte order 😡)
Access address unique for each connection (randomly chosen)
  In Advertising always set to 0x8E89BED6

## Slide 26: Device addresses
Public and private address forms
Public
  48 bits: 24-bits of company ID, 24-bits of company assigned number
  Literally the same MAC address scheme as Ethernet and WiFi
Private
  Top two MSbs specify type
    46 bits of random
    46 bits of hash of an identity key
Why have the two types?

## Slide 27: Device addresses
Public and private address forms
Public
  48 bits: 24-bits of company ID, 24-bits of company assigned number
  Literally the same MAC address scheme as Ethernet and WiFi
Private
  Top two MSbs specify type
    46 bits of random
    46 bits of hash of an identity key
Why have the two types? Privacy

## Slide 28: Data whitening
Avoid long series of repetitive bits (all zeros or all ones)
  Would cause RF noise to be more focused in one direction
  Radio hardware desires output to have zero DC-bias (or close to that)
  Great example of the PHY and MAC being interwoven in wireless
I always forget this exists, since hardware usually handles it automatically

## Slide 29: Bit processing pipeline

## Slide 30: Break + Question
With enough scanners, could you track BLE devices as they move?

## Slide 31: Break + Question
With enough scanners, could you track BLE devices as they move?
  Depends on how long they use a device address for
  You can do a scan of BLE transmissions to find device addresses
  Scans at multiple locations can detect when a device moves throughout an area
  But if the device re-randomizes between two scanners, you can’t follow it anymore
    Re-randomizing at a scanner could be detectable…

## Slide 32: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning

## Slide 33: Advertising
BLE discovery mechanism
  Make nearby devices aware of advertiser’s existence
  Communicate some information from or about advertiser
  Traditional purpose is to enable connections, but this is also useful for general communication
Advertisements
  Periodic broadcast messages with data
Scan Requests/Responses
  Scanner sends responses after getting a request
    Only occurs when scanner is listening
  Almost literally “bonus advertisement data”

## Slide 34: Advertising packet layering

## Slide 35: BLE advertising header
ADV_IND
  Advertisement
  Allows connections and scan requests
ADV_NONCONN_IND
  Advertisement
  No connections or scan requests
ADV_SCAN_IND
  Advertisement
  No connections but allows scan requests
SCAN_REQ
  Scan request
SCAN_RSP
  Scan response

## Slide 36: Advertisement payloads
AdvA – address of the advertiser
  TxAdd bit from header specifies if this is a “public” or “random” address
Remaining up to 31 bytes are available for use
Putting it all together, up to 47 bytes total:
Preamble 1 Byte | Access Address 4 Bytes | Header 2 Bytes | Advertiser Address 6 Bytes | Advertiser Data (Payload) 0-31 Bytes | CRC 3 Bytes
BLE Packet
Advertising PDU

## Slide 37: Scan Requests and Responses
Scan request
  Just the two addresses: the scanner’s and the advertiser’s
Scan response
  Identical to an advertisement
  But only occurs after a request

## Slide 38: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why?
User picks the rate as a tradeoff of energy and discovery latency

## Slide 39: Advertising timing
Advertising Events occur periodically [20ms – 10.24 s] (or longer)
  Plus a random delay after each instance [0-10ms]
  Why? Avoid repeat collisions
User picks the rate as a tradeoff of energy and discovery latency

## Slide 40: Advertising event
Three transmissions, one on each advertising channel
  Always in the same order
Transmission, followed by listening window on that same channel
  Requests will be sent >=150 us (Inter-Frame Spacing, IFS) after Tx
  Followed by a retune to the next channel frequency
This short listen window is the magic “low energy” part

## Slide 41: Preserving energy in communication
Most energy is spent listening
  This is due primarily to how long listening durations are compared to transmissions
Example: maximum-sized BLE transmission:
  8 bits/byte * 47 bytes = 376 bits at 1 Mbps = 0.376 ms transmitting
  So listening for an entire second is >2500 times longer
  But listening for only 0.376 ms requires sub-ms synchronization, which itself costs energy to manage…
  Instead, when advertising, nRF radios listen for ~0.200 ms, only after a transmission

## Slide 42: Payload of an advertisement
What do you stick in the BLE payload anyways?
  Theoretically whatever you want, but that isn’t very compatible
  Point is to specify capabilities of the advertiser
Desire: specify payloads in such a way that all scanners can interpret what they mean about the device
  This is different from traditional internet packets
  Broadcasts are for _anyone_ to hear, not a specific server/application
Ideas?

## Slide 43: TLV Format
Type – Length – Value
  Actually, BLE does the length part first
  Scanner can hop through length/type pairs to find what interests it

## Slide 44: Payload types
Listed in the Core Specification Supplement [Supplement v9]
  Each might have their own considerations about AD Data format
Flags (supported modes: BLE and Bluetooth) required by Apple?
Name
Service UUID
TX Power Level
Manufacturer-specific data
And about twenty others

## Slide 45: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning

## Slide 46: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle?

## Slide 47: Scanning Pattern
Iterate through channels, listening for advertisements
  Tscan_interval controls rate at which channels are changes
  Tscan_window controls duty cycle of listening
Why listen at a low duty cycle? Save energy

## Slide 48: Putting it all together
Advertisements are received when the channel of the scan window and the channel of the advertisement overlap in time (and space)

## Slide 49: A warning about scanning expectations
Scanners will NOT receive 100% of packets sent
  Even ignoring range issues
Packets are lost due to (in roughly descending order):
  Duty cycle
  Sharing 2.4 GHz antenna with WiFi
  Retune period after each scanning interval
  Dropped packets in the receive software
  Packet collisions

## Slide 50: Outline
BLE Background
BLE Layers
  Physical Layer
  Link Layer
BLE roles
  Advertising
  Scanning