## Slide 1: Lab 1 Embedded Programming
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021

## Slide 2: Today’s Goals
Provide background information for students not familiar with embedded systems software
Describe details about the Nordic software system
  And the nrf52x-base software system

## Slide 3: Outline
Microcontrollers
Programming Embedded Systems
Embedded Software

## Slide 4: What is a microcontroller anyways?
Entire computer in a single chip
  Processor
  Working memory: SRAM (like RAM)
  Nonvolatile memory: Flash (like SSD)
  Peripherals
    I/O pins
    Analog Inputs and Outputs
    Timers
    Wireless radios
    Cryptography accelerators
  Power management
    Buses
      UART
      I2C
      SPI
      USB

## Slide 5: How is a microcontroller different?
A very constrained computer
  Simple processor
    16 or 32 bits (usually 32-bit these days)
    Processor speed in MHz
    Single core, pipelined processor
    No cache, or maybe a very small instruction cache
  Memory in KB
    Code executes right from read-only Flash (which is part of the address space)
  Often no OS support
    “bare-metal” programming

## Slide 6: Nordic semiconductor microcontrollers
32-bit ARM microcontrollers with integrated wireless radios
  2012 – nRF51 series with Cortex-M0
  2015 – nRF52 series with Cortex-M4
    nRF52840
      64 MHz processor
      512 KB Flash
      128 KB RAM
      BLE and 802.15.4/Thread support
  Very capable and low energy compared to other microcontrollers
  Also very good software support
    Which is incredibly rare

## Slide 7: Overview of nRF52840 capabilities
Go to Figure 1: Block diagram
https://infocenter.nordicsemi.com/pdf/nRF52840_PS_v1.1.pdf
Online documentation:
  https://infocenter.nordicsemi.com/topic/ps_nrf52840/keyfeatures_html5.html

## Slide 8: nRF52840DK
nRF52840 microcontroller
  4 buttons, 4 leds
  Antenna for wireless
  Various headers for connection to pins
JTAG programmer
  Connect through top USB port
  Enables loading of code and runtime debugging

## Slide 9: Outline
Microcontrollers
Programming Embedded Systems
Embedded Software

## Slide 10: Embedded systems are programmed in C
Occasionally assembly or C++
  Rarely other things (Rust, Lua, Python)
But even the few things C gives you aren’t necessarily available
  Heap space is likely nonexistent
    You have to choose some space in RAM to save as a heap
    And then include the algorithm for allocating that memory
  Printf is often nonexistent too
    There’s no STDIN/STDOUT/STDERR because there is no shell
    We hooked up printf for you on the nRF52840DK though!

## Slide 11: How do I build code for microcontrollers?
You need a couple of things
  Memory layout “.ld” file explains where memory is for linker
  A compiler toolchain for the correct architecture
Cross compilers
  Run on one architecture but compile code for another
    Example: runs on x86-64 but compiles armv7e-m
  GCC is named: ARCH-VENDOR-(OS-)-ABI-gcc
    arm-none-eabi-gcc
      ARM architecture
      No vendor
      No OS
      Embedded Application Binary Interface
    Others: arm-none-linux-gnueabi, i686-unknown-linux-gnu

## Slide 12: How do I load code onto microcontrollers?
JTAG (Joint Test Action Group)
  Hardware built into the microcontroller for testing purposes
  Can arbitrarily read/write memory
  Can single step process too, at runtime!
    GDB can connect to it! (sort of)
  RTT (Real Time Transfer) makes printf work over JTAG
Serial bootloaders
  Software runs on the microcontroller at boot that waits a short time for someone to contact it and upload code
  Convenient, but sometimes flaky

## Slide 13: Outline
Microcontrollers
Programming Embedded Systems
Embedded Software

## Slide 14: Embedded software
There are a multitude of embedded software systems
  Every microcontroller vendor has their own
  Popular platforms like Arduino
Embedded OSes
  Contiki, Riot, Zephyr, Mynewt, FreeRTOS, Tock
nRF52840DK has support across all of these
  I usually program it using the Nordic SDK though

## Slide 15: Software Development Kit (SDK)
Libraries provided by Nordic for using their microcontrollers
  Actually incredibly well documented! (relatively)
  Various peripherals and library tools
SDK documentation
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/index.html
  Warning: search doesn’t really work
Most useful link is probably to the list of data structures
  https://infocenter.nordicsemi.com/topic/sdk_nrf5_v16.0.0/annotated.html

## Slide 16: Softdevice
Sort of like an OS that only manages the radio
  Always running underneath your code
  You don’t have control over it, but can request things
    Actually through system calls
  Block of code that you cannot edit
Handles time-sensitive behaviors and can be certified
  This is the reason GDB doesn’t really work
We’ll load it automatically, and some of the library calls you make will interact with it, but you likely won’t have to think about it

## Slide 17: nRF52x-base
Wrapper built around the SDK by Lab11
  Branden Ghena, Brad Campbell (UVA), Neal Jackson, a few others
  Allows everything to be used with Makefiles and command line
  https://github.com/lab11/nrf52x-base
We include it as a submodule
  It has a copy of the SDK code and softdevice binaries
  It has a whole Makefile system to include to proper C and H files
  We include a Board file that specifies our specific board’s needs and capabilities
https://github.com/brghena/nu-wirelessiot-base

## Slide 18: Outline
Microcontrollers
Programming Embedded Systems
Embedded Software