## Slide 1: Lecture 03: Concurrency Sources and Challenges
CS343 – Operating Systems
Branden Ghena – Fall 2020
Some slides borrowed from: Stephen Tarzia (Northwestern), and UC Berkeley CS61C and CS162

## Slide 2: Today’s Goals
Describe where and why concurrency and parallelism are involved in computing.
Be disappointed by performance limits on concurrency.
Understand purpose and challenges of interrupts and signals.
Introduce concept of data races as a concurrency problem.

## Slide 3: Parallelism versus Concurrency
Two processes A and B
B
A
B
A
B
A
B
A
OR
time
time
time
time
Serial execution
Parallel execution
Concurrent execution

## Slide 4: Parallelism versus Concurrency
Parallelism
  Two things happen strictly simultaneously
Concurrency
  More general term
  Two things happen in the same time window
    Could be simultaneous, could be interleaved
  Concurrent execution occurs whenever two processes are both active
B
A
OR
time
time
OR
time

## Slide 5: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 6: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 7: Moore’s Law
“Every two years, the number of transistors on a chip of a fixed size doubles”

## Slide 8: Processors kept getting faster too

## Slide 9: Denard Scaling
Moore’s Law corollary: As transistors get smaller, the power density stays the same.
  If Moore’s Law holds true, we also get a doubling of “performance per watt” every two years!
  Manufacturers could raise the clock frequency between generations without more power consumption

## Slide 10
It’s the mid 1990s and you work at Microsoft.
You need to double the speed of Excel in two years time or you’re fired.
What do you do?

## Slide 11
It’s the mid 1990s and you work at Microsoft.
You need to double the speed of Excel in two years time or you’re fired.
What do you do?
Take a vacation

## Slide 12: Then they stopped getting faster
~2006: Leakage current becomes significant
Now smaller transistors don’t mean lower power

## Slide 13: So… now what?
In summary:
We can’t make transistors faster due to current leakage,
and because of that, we can’t reliably make performance better by waiting for clock speeds to increase,
but we have literally billions of transistors available to use.
How do we continue to get better performing computation?

## Slide 14: Exploit parallelism!
In reality the cause-and-effect of parallelism isn’t so simple. Key points:
  we can’t just increase frequency
  we do have a lot of transistors available
  parallelism is one approach to improve performance again

## Slide 15: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 16: Model of a processor
CPU
Instructions,
Registers,
Memory
Updated
Registers and
Memory
Instruction Fetch
Instruction Decode
Execute
Memory
Writeback
CPU

## Slide 17: But instructions don’t always have to be executed in order
movq (%rdi), %rax movq (%rsi), %rdx movq %rdx, (%rdi) movq %rax, (%rsi) addq %rcx, %rbx
We can apply the multiprogramming approach of executing this addq while the movq is waiting on memory.
Doesn’t have to go after the movq instructions because it uses different registers

## Slide 18: Out-of-order machines
Fetch many instructions at once!
Read register file, handle data dependencies with register renaming
Reorder instructions to make best use of CPU
Commit, or “write back” data to memory and regfile in the order the programmer expects
Generally: looks for independent instructions it can execute early

## Slide 19: Out-of-order processors obey normal execution results
Initial thoughts on out-of-order execution
  😱
  The processor could be executing my program in order it feels like?!!
  How do I possibly reason about anything?
Answer: the processor promises to have the same results as if things were done in the normal order.
CPU
Instructions,
Registers,
Memory
Updated
Registers and
Memory

## Slide 20: Multiple processes might rely on memory ordering
The processor can’t account for multiple processes though
If memory results are shared by two threads, the processor might mess something up for you.
What will Thread 1 print?
while (f == 0);
printf(“%d\n”, x);
x = 42;
f = 1;
f = 0;
x = 0;
// split into threads
Thread 1
Thread 2

## Slide 21: Multiple processes might rely on memory ordering
The processor can’t account for multiple processes though
If memory results are shared by two threads, the processor might mess something up for you.
What will Thread 1 print? Could be 42. Could be 0.
while (f == 0);
printf(“%d\n”, x);
x = 42;
f = 1;
f = 0;
x = 0;
// split into threads
Thread 1
Thread 2
This can be addressed with memory barriers

## Slide 22: How else do processors employ concurrency?
Goal: Make computer faster by performing multiple tasks
Solutions:
Use multiple cores to run multiple tasks in parallel
Run multiple tasks on a single core concurrently

## Slide 23: How else do processors employ concurrency?
Goal: Make computer faster by performing multiple tasks
Solutions:
Use multiple cores to run multiple tasks in parallel
Run multiple tasks on a single core concurrently

## Slide 24: Multiprocessor Systems (in pictures)
Processor 0
Control
Datapath
PC
Registers
(ALU)
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor 0 Memory Accesses
Processor 1
Control
Datapath
PC
Registers
(ALU)
Processor 1 Memory Accesses

## Slide 25: Multiprocessor Systems (in words)
A computer system with at least 2 processors or cores
  Each core has its own PC and registers
  Each core executes independent instruction streams
  Processors share the same system memory
    But use different parts of it
  Communication possible through loads and stores to a common location
Deliver high throughput for independent jobs via task-level parallelism

## Slide 26: Multiprocessor Example
Run Chrome and Minecraft simultaneously
Each are separate programs
Each has a different memory space
Each can run on a separate core
Don’t even need to communicate...
Note: OS can fake this by interleaving processes, but hardware can make it actually simultaneous

## Slide 27: How else do processors employ concurrency?
Goal: Make computer faster by performing multiple tasks
Solutions:
Use multiple cores to run multiple tasks in parallel
Run multiple tasks on a single core concurrently

## Slide 28: Multithreading processors
Basic idea: Processor resources are expensive and should not be left idle
Long memory latency to memory on cache miss?
  Hardware switches threads to bring in other useful work while waiting for cache miss
  Cost of thread context switch must be much less than cache miss latency
Switching threads is less expensive than processes because they share memory

## Slide 29: Hardware support for multithreading
Memory
Input
Output
Bytes
I/O-Memory Interfaces
Processor
Control
Datapath
PC 0
Registers 0
(ALU)
PC 1
Registers 1
Two copies of PC and Registers inside processor hardware
Looks like two processors to software (hardware thread 0, hardware thread 1)
Control logic decides which thread to execute an instruction from next
29

## Slide 30: Multithreading versus Multicore
Multithreading => Better utilization
  ≈5% more hardware for ≈1.3x better performance?
  Gets to share ALUs, caches, memory controller
Multicore => Duplicate processors
  ≈50% more hardware for ≈2x better performance?
  Share some caches (L2 cache, L3 cache), memory controller
Modern machines do both
  multiple cores with multiple threads per core

## Slide 31: My desktop computer
4 total cores
Each capable of 2 threads
≈ 8 processors

## Slide 32: Raspberry Pi 4
Quad core processor
One thread per core
3-way superscalar pipeline
L1 Cache
  32 KiB 2-way set associative data cache
  48 KiB 3-way set associative instruction cache
  Per core
L2 Cache
  512 KiB to 4 MiB (shared)
RAM 1-4 GB
$35
Literally all computers are doing parallelism these days

## Slide 33: Back up to the OS perspective
Modern operating systems must manage concurrency
  Both parallel operation and interleaving operations
Concurrency is worth it
  Performance gains are the reason

## Slide 34: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 35: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 36: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 37: Speedup Example
Imagine a program that takes 100 seconds to run
95 seconds in the blue part
5 seconds in the green part
95 s | 5 s

## Slide 38: Speedup from improvements
95 s | 5 s
Speedup with Improvement | = | Execution time without improvement
 |  | Execution time with improvement
5 s -> 2.5 s: Speedup = 100/97.5 = 1.026
5 s -> 1 s: Speedup = 100/96 = 1.042
5 s -> 0.001s: Speedup = 100/95.001 = 1.053
The impact of a performance improvement is relative to the importance of the part being improved!

## Slide 39
Speedup =
F = Fraction of execution time speed up S = Scale of improvement
(1 - F) + F
S
Non-speed-up part
Speed-up part
1
1
0.75 + 0.25
2
1
0.75 + 0.125
=
=
1.14
Example: 2x improvement to 25% of the program
Equivalent to prior equation
Amdahl’s Law

## Slide 40: Parallel speedup example
Speedup with improvement | 
Speedup with improvement | 
Consider an improvement which runs 20 times faster but is only usable 15% of the time
Speedup with improvement | 
Speedup with improvement | 
= 1.166
Speedup with improvement | 
Speedup with improvement | 
= 1.311
What if it’s usable 25% of the time?
Nowhere near 20x speedup!

## Slide 41: Amdahl’s (heartbreaking) Law (in pictures)
The amount of speedup that can be achieved through parallelism is limited by the non-parallel portion of your program!
Parallel
portion
Serial
portion
Time
Number of Processors
1
2
3
4
5
Speedup
Number of Processors

## Slide 42: Amdahl’s (heartbreaking) Law (in words)
Amdahl’s Law tells us that to achieve linear speedup with more processors:
  none of the original computation can be serial (non-parallelizable)
To get a speedup of 90 from 100 processors, the percentage of the original program that could be scalar would have to be 0.1% or less
Speedup = 1/(.001 + .999/100) = 90.99

## Slide 43: Check your understanding
Suppose a program spends 50% of its time in a square root routine.
How much must you speed up square root to make the program run 2x faster?
Speedup with improvement | 
Speedup with improvement | 
10
(A)
20
(B)
100
(C)
None of the above
(D)
50% | 50%

## Slide 44: Check your understanding
Suppose a program spends 50% of its time in a square root routine.
How much must you speed up square root to make the program run 2x faster?
Speedup with improvement | 
Speedup with improvement | 
10
(A)
20
(B)
100
(C)
None of the above
(D)
50% | 50%
Speedup = 1 / [ (1 - F) + (F/S) ]
2 = 1 / [ (1 - 0.5) + (0.5/S)]
S = 0.5 / ((1/2) – 0.5) = ∞
The square root would need to decrease to nothing before you got 2x speedup

## Slide 45: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 46: Where else does concurrency come from?
Processors introduce it for performance reasons by running multiple processes and threads
Interactions with the outside world introduce it because events occur whenever they feel like it
  Network request arriving
  User presses a key
  Motion sensor triggers
Also, we need some way to deal with errors the occur when executing instructions
  No pathway for returning an error from an instruction

## Slide 47: Interrupts
A way for the CPU to be, well, interrupted.
CPU hardware switches to privileged mode
  Now any instruction can be executed, including privileged ones.
Execution jumps to a predefined location
  Handler specified in the CPU’s interrupt vector table
  Lets the kernel deal with whatever the event was
Used to support asynchronous I/O
  Lets a hardware device tell the CPU that some data is ready
  Remember that a disk operation is millions of times slower than an add.
CPU has an electrical pin for hardware interrupts.
There is also an instruction for software interrupts (like traps!)

## Slide 48: Interrupt Vector Table
Table actually lives in memory somewhere, with function pointers for each vector number
Example from Tock for SAM4L chip (in Rust)

## Slide 49: Interrupt Vector Table
Table actually lives in memory somewhere, with function pointers for each vector number
Example from Tock for SAM4L chip (in Rust)

## Slide 50: Differences from traps
When we performed a system call:
  We knew it was about to happen.
  Set up our registers in advance.
  Performed what looked sort of like a function call.
Interrupts can happen whenever.
  This can get extremely complicated on modern systems with out-of-order execution, multiple cores and threads, and caches

## Slide 51: Interrupt handlers
Interrupt context
  Can’t just enter the kernel like we did with system calls
  Interrupt could have occurred while we were in the kernel
Handler code
  Execute some quick processing to deal with the interrupt
  Return so the hardware can bring us back to our normal operation
  Cannot pause to wait for something else to finish first because the entire core jumped to handling this interrupt
Handled by the operating system
  Processes are interrupted, but otherwise not normally involved

## Slide 52: Signals are asynchronous messages to processes
Sometimes the OS wants to send something like an interrupt to a process
  Your child process completed
  You tried to use an illegal instruction
  You accessed invalid memory
  You are terminating now
In POSIX systems, this idea is called “Signals”
1) SIGHUP 2) SIGINT 3) SIGQUIT 4) SIGILL 5) SIGTRAP
6) SIGABRT 7) SIGBUS 8) SIGFPE 9) SIGKILL 10) SIGUSR1
11) SIGSEGV 12) SIGUSR2 13) SIGPIPE 14) SIGALRM 15) SIGTERM
16) SIGSTKFLT 17) SIGCHLD 18) SIGCONT 19) SIGSTOP 20) SIGTSTP
21) SIGTTIN 22) SIGTTOU 23) SIGURG 24) SIGXCPU 25) SIGXFSZ
26) SIGVTALRM 27) SIGPROF 28) SIGWINCH 29) SIGIO 30) SIGPWR
31) SIGSYS ...

## Slide 53: Signals are asynchronous messages to processes
Sometimes the OS wants to send something like an interrupt to a process
  Your child process completed
  You tried to use an illegal instruction
  You accessed invalid memory
  You are terminating now
In POSIX systems, this idea is called “Signals”
1) SIGHUP 2) SIGINT 3) SIGQUIT 4) SIGILL 5) SIGTRAP
6) SIGABRT 7) SIGBUS 8) SIGFPE 9) SIGKILL 10) SIGUSR1
11) SIGSEGV 12) SIGUSR2 13) SIGPIPE 14) SIGALRM 15) SIGTERM
16) SIGSTKFLT 17) SIGCHLD 18) SIGCONT 19) SIGSTOP 20) SIGTSTP
21) SIGTTIN 22) SIGTTOU 23) SIGURG 24) SIGXCPU 25) SIGXFSZ
26) SIGVTALRM 27) SIGPROF 28) SIGWINCH 29) SIGIO 30) SIGPWR
31) SIGSYS ...
Process Errors

## Slide 54: Signals are asynchronous messages to processes
Sometimes the OS wants to send something like an interrupt to a process
  Your child process completed
  You tried to use an illegal instruction
  You accessed invalid memory
  You are terminating now
In POSIX systems, this idea is called “Signals”
1) SIGHUP 2) SIGINT 3) SIGQUIT 4) SIGILL 5) SIGTRAP
6) SIGABRT 7) SIGBUS 8) SIGFPE 9) SIGKILL 10) SIGUSR1
11) SIGSEGV 12) SIGUSR2 13) SIGPIPE 14) SIGALRM 15) SIGTERM
16) SIGSTKFLT 17) SIGCHLD 18) SIGCONT 19) SIGSTOP 20) SIGTSTP
21) SIGTTIN 22) SIGTTOU 23) SIGURG 24) SIGXCPU 25) SIGXFSZ
26) SIGVTALRM 27) SIGPROF 28) SIGWINCH 29) SIGIO 30) SIGPWR
31) SIGSYS ...
Process Termination

## Slide 55: Sending signals
OS sends signals when it needs to
Processes can ask the OS send signals with a system call
  int kill(pid_t pid, int sig);
Users send signals through OS from command line or keyboard
  Shell command: kill -9 pid (SIGKILL)
  CTRL-C (SIGINT)

## Slide 56: Handling signals
Programs can register a function to handle individual signals
  signal(int sig, sighandler_t handler);
What are you supposed to do about it?
  Do some quick processing to handle it
    Be careful, not all functions are safe to call here (re-entrant functions only)
  Reset the process and try again
  Quit the process (default handler)

## Slide 57: Signals Examples

## Slide 58: Examples: sending a signal
> kill -11 pid

## Slide 59: Example: catching a signal
void sighandler (int signum) {
printf("HA HA You can't kill me!\n");
}
int main (void) {
signal(SIGINT, sighandler);
printf("Starting\n");
while(1) {
printf("Going to sleep for a second...\n");
sleep(1);
}
return(0);
}
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <signal.h>

## Slide 60: Example: catching a segfault
int* pointer = 0x00000000;
void sighandler (int signum) {
printf("Oops, that pointer wasn't valid. Let's try a different one\n");
pointer++;
printf("About to read from pointer 0x%08lX\n", (long)pointer);
}
int main (void) {
signal(SIGSEGV, sighandler);
printf("About to read from pointer 0x%08lX\n", (long)pointer);
int test = *pointer;
return(0);
}
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <signal.h>

## Slide 61: Systems software needs to deal with concurrency
Reliable processes need to handle signals
OS kernels need to handle interrupts
This time it’s not just about performance
  It’s also about handling errors
  And interacting with the outside world
Challenges are similar
  Processor concurrency: shared state between multiple processes/threads
  Interrupts/Signals: shared state between a process and interrupt context

## Slide 62: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races

## Slide 63: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 64: Concurrency problem: data races
Consider two threads with a shared global variable: int count = 0
count could end up with a final value of 1 or 2. How?
Thread 1:
void main(){
count += 1;
}
Thread 2:
void main(){
count += 1;
}

## Slide 65: Concurrency problem: data races
Consider two threads with a shared global variable: int count = 0
count could end up with a final value of 1 or 2. How?
These instructions could be interleaved in any way.
Thread 1:
void main(){
mov 0x8049a1c, %eax
add $0x1, %eax
mov %eax, 0x8049a1c
}
Thread 2:
void main(){
mov 0x8049a1c, %eax
add $0x1, %eax
mov %eax, 0x8049a1c
}
Assuming “count” is in memory location 0x8049a1c

## Slide 66: Data race example
Thread 1 | Thread 2
mov 0x8049a1c, %eax | 
add $0x1, %eax | 
mov %eax, 0x8049a1c | 
 | mov 0x8049a1c, %eax
 | add $0x1, %eax
 | mov %eax, 0x8049a1c
Time
Thread 1 | Thread 2
mov 0x8049a1c, %eax | 
 | mov 0x8049a1c, %eax
 | add $0x1, %eax
 | mov %eax, 0x8049a1c
add $0x1, %eax | 
mov %eax, 0x8049a1c | 
Final value of count: 2
Final value of count: 1
Assuming “count” is in memory location 0x8049a1c

## Slide 67: Data race explanation
Thread scheduling is non-deterministic
  There is no guarantee that any thread will go first or last or not be interrupted at any point
If different threads write to the same variable
  The final value of the variable is also non-deterministic
  This is a data race

## Slide 68: Check your understanding: data races with multiple threads
Consider three threads with a shared global variable: int count = 0
What are the possible values of count?
Thread 1:
void main(){
count += 1;
}
Thread 2:
void main(){
count -= 1;
}
Thread 3:
void main(){
count += 2;
}

## Slide 69: Check your understanding: data races with multiple threads
Consider three threads with a shared global variable: int count = 0
What are the possible values of count? -1, 0, 1, 2, 3
How are you supposed to reason about this?! Need mechanisms for sharing memory.
Thread 1:
void main(){
count += 1;
}
Thread 2:
void main(){
count -= 1;
}
Thread 3:
void main(){
count += 2;
}

## Slide 70: Outline
Performance through concurrency
Concurrency introduced by the processor
Amdahl’s Law – limits on performance
Interrupts and Signals
A problem with concurrency: data races