## Slide 1: Lecture 03 Data Link Layer + BLE Introduction
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2025
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Hw: Background
  Goal: brush up on some embedded systems and networks background
  Due tonight
  Submit on Gradescope
Lab: Wireshark
  Goal: familiarize yourself with Wireshark
    Install it, do some basic scanning, explore a little
  We’ll do checkoffs during lab time tomorrow
    Friday 11:00-12:30 pm in Frances Searle 2370
    See you all there!

## Slide 3: Partnership survey
Labs (after this first one) will be in groups of exactly three
I’m trying to
  Figure out what the groups are
  Match up students who need groups
Please fill out the survey posted on Piazza
I’ll go through this weekend and match up groups

## Slide 4: Today’s Goals
Overview of concerns for the Data link layer
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols
Describe Medium Access Control mechanisms
Introduction to Bluetooth Low Energy
  What are the goals of the protocol?
  What do the lower layers look like?

## Slide 5: Review: OSI model of communication layers
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
Open Systems Interconnection (OSI)

## Slide 6: Review: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.7.30
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.7.30 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 7: Review: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 8: Review: Signal strength
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 9: Big Idea: many RF factors are interconnected
Energy, Distance, Throughput, and Reliability are all interconnected in communication
Protocols make choices of some and get the results on the others
To get more distance, choose one or more:
  Increase energy
  Communicate slower
  Accept a higher error rate

## Slide 10: Review: frequency and bandwidth
A pure sinusoid is energy at exactly one frequency
A messy sinusoid with data layered on top of it has nearby energy
  There’s a center of the signal energy
  Plus some amount of width, which depends on how complicated the data layered on top is

## Slide 11: Review: RF communication frequencies
IoT focus

## Slide 12: Wireless spectrum is limited...and valuable
FCC auctioned off 3.5 GHz spectrum in August 2020
  70 MHz
  $4.6 billion
FCC auctioned off 2.5 GHz spectrum in 2022
  $427 million
https://www.fiercewireless.com/wireless/t-mobile-pays-304m-fill-holes-its-25-ghz-spectrum

## Slide 13: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 14: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 15: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 16: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 17: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Often differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 18: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but this modulation is still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 19: Break + Video
Excellent explanation of modulation techniques: https://youtu.be/0faCad2kKeg?si=kK6l0g63XGVPdut9&t=240
  Listen for 3.5 minutes until 7:30 in the video
  “How Cell Service Actually Works” by Wendover Productions

## Slide 20: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 21: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 22: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Possible wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 23: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 24: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 25: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Task: Break into groups of 5 students each
  In a minute I’m going to ask each group a question
  Everyone in the group needs to answer correctly
  Fastest group to have everyone answer wins
  If two people talk at the same time, that group loses

## Slide 26: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)
Everyone speak in different languages -> code division multiple access (sort of, but not really)
Others?

## Slide 27: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 28: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 29: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 30: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad
My transmission
My transmission
Other transmission
Other transmission

## Slide 31: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
My transmission
Other transmission
Other transmission
My transmission
time

## Slide 32: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 33: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 34: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 35: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 36: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Very challenging for wireless systems
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm
  Area of active research!

## Slide 37: Hidden terminal problem
Device A
Device B
Device C

## Slide 38: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low
    Not always worth it

## Slide 39: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
CDMA
ALOHA
CSMA

## Slide 40: Contention-free access control protocols
Goal: split up communication such that devices will not conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 41: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
  Usually in conjunction with another scheme (but not always)
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 42: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 43: CDMA – Code Division Multiple Access
Split transmissions in ‘codes’
  Not new; original applications in radar and early satellite communications
Analogy: Multiple speakers in the same room all in different languages
  [The human brain is crazy good at ignoring what it doesn’t understand ]
Requires signal power coordination
  [everyone needs to speak ~the same volume]
  Can be hard in uncontrolled / dynamic environments
Also can be more performant with highly synchronized clocks
  i.e. if the code clock is known to both devices

## Slide 44: Break + Question
What is an advantage of Aloha over TDMA?

## Slide 45: Break + Question
What is an advantage of Aloha over TDMA?
  Simplicity! It’s really easy to implement Aloha
  No required centralization
    TDMA time schedule needs to be decided by something
    That thing is “in charge”
    Aloha can be entirely distributed

## Slide 46: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 47: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 48: Bluetooth Low Energy Resources
Good walkthrough of BLE:
  https://www.silabs.com/documents/public/user-guides/ug103-14-fundamentals-ble.pdf
[5.2 specification] [4.2 specification] (link to PDF download)
  Also: [Supplement v9]
I used a mix of 5.2 and 4.2 for this
  Will talk about BLE 5 differences as part of next lecture

## Slide 49: Basics of Bluetooth Low Energy (BLE)
Direct device-to-device communication
  Usually: Computer to Thing
  Smartphone to device, Laptop to device, etc.
Focus on making the “Thing” really low energy
  Push energy-intensive requirements onto “Computer”
Devices (Computer or Thing) are servers with accessible fields
  Not the traditional send-explicit-packets interface you might be expecting
  Lower layers are still exchanging packets to make it work

## Slide 50: A note on outdated notation
Master/Slave paradigm
  Master is the “Computer” and is in charge of interaction
  Slave is the “Device” and has little control over interaction parameters
  Really common notation in EE side of the world.
    Not intended to be harmful, but also literally inconsiderate.
Field is changing for the better. It’s going to take some time.
  Central/Peripheral
  Device/Peripheral
  Controller/Peripheral
  Master/Minion
  Primary/Secondary

## Slide 51: BLE development
Protocol development
  Research product
  Specification
  Hardware support
  Usefulness and iteration
Bluetooth Low Energy
  Research in early 2000s: Bluetooth Low End Extension and Wibree
  Specification in 2009: Bluetooth version 4.0
  Hardware support in 2011/12: iPhone 4s, nRF51 series
  4.1 and 4.2 (2014), 5.0 (2016, first in phones 2017, really 2019 though)

## Slide 52: Bluetooth has a long history — the IoT is near-exclusively BLE (Bluetooth 4.0+) as opposed to Bluetooth Classic (<4.0)

## Slide 53: Bluetooth Specification
Problem: a bit overwhelming…
  5.2 spec: 3256 pages
  We only care about Vol 6: Low Energy Controller
    Part A: Physical Layer Specification
    Part B: Link Layer Specification
    CSS: Part A: Data Types Specification
    So ~250 pages
Tip: be willing to just ignore things when skimming specs
  5.2 spec covers BLE and Bluetooth Classic and a bunch of upper layer stuff that we never have to care about

## Slide 54: BLE Layers
Host – Configuration and Server
  GAP – Generic Access Profile
    Configure advertising
  GATT – Generic ATTribute profile
    Configure connections
HCI - Host Controller Interface (sigh)
Controller - Communication
  Link Layer – send packets
  RF and PHY – send bits
GAP
Host
Controller

## Slide 55: BLE mechanisms
Advertising
  Discovery
  Advertisements – broadcast messages indicating device details
  Ephemeral, uni-directional communication from Advertiser to Scanner(s)
  ALOHA access control
Connections
  Interaction
  Bi-directional communication between Peripheral and Central
  Maintained for some duration
  TDMA access control

## Slide 56: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 57: Multiple roles at the same time
Topology picture is a simplification of roles
A single device can have multiple roles simultaneously
  Scanning and Advertising simultaneously
  Peripheral and Scanner and Advertiser simultaneously
  Peripheral and Scanner and Central and Advertiser simultaneously
    Getting a bit out of hand though
One Peripheral can even be connected to multiple Centrals
  Not in the original design though: you’ll find old docs saying you can’t
  And it’s not a normal use-case for BLE

## Slide 58: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
  Laptop
  Smartphone

## Slide 59: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
    Advertiser and Peripheral
  Laptop
    Scanner and Central
  Smartphone
    Advertiser, Peripheral, Scanner, and Central

## Slide 60: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background